## Slide 1: Sync Bit Duration Text Motion
Date: 2018-03-01
Authors:

## Slide 2: Background
At the January IEEE meeting the Task Group agreed that the Sync Bit Duration would be 2 µs
This is recorded in the Spec Framework Document [1]
[1] Po-Kai Huang, “Specification Framework for TGba,” IEEE 802.11-18/575r9, Jan 2018

## Slide 3: Motion
Move to make the following changes to Draft 0.1
  Move Steve Shellhammer
  Second Jia Jia
  Passed Unanimously
32.3.8.3.3 WUR-Sync field for Low Data Rate
For LDR, the WUR-Sync field is constructed as a multicarrier on-off keying (MC-OOK) signal. The OOK signal is constructed by concatenating two copies of the sequence TBD 32-bit sequence W, where each bit in the sequence is has duration TBD 2 μs. The bit sequence , and W is defined in Equation (32-2).
32.3.8.3.4 WUR-Sync field for High Data Rate
For HDR, the WUR-Sync field is constructed as a multicarrier on-off keying (MC-OOK) signal. The OOK signal is constructed as the bit-wise complement of the sequence TBD 32-bit sequence W, where each bit in the sequence is has duration TBD 2 μs, and W is defined in Equation (32-2).