## Slide 1: Simulation on the Effect of OFDM Symbol Design
Date: 2018-03-01
Authors:

## Slide 2: Introduction
At the January IEEE meeting it was shown [1] that the design of the OFDM symbol affects the high data rate WUR performance
Here we simulate several OFDM designs for the high data rate
  Single Carrier
    In January [2] single carrier (called Ideal OOK) was simulated, so we included it for reference
  Low PAPR for 4 µs (over full Manchester code). Used in our previous simulations
  Then design in [1] shown to be good for Channel Model D
Simulated for both AWGN and Channel Model D

## Slide 3: Low PAPR OFDM Symbol
Used in many of our earlier simulations
64-point FFT
Coefficients = [0,…, 0, 1, 1, 1, -1, -1, -1, 1, 1, -1, 1, 1, -1, 1, 0, … 0]
16-sample Cyclic Prefix
Generates 4 µs OFDM symbol
Used for full 4 µs Manchester code

## Slide 4: Proposal from [1]
32-point FFT
Coefficients = [0, 0, 0, … 0, 1, 1, -1, 0, -1, 1, 1, 0 0 0 … 0]
8-sample Cyclic Prefix
Generates 2 µs OFDM symbol
Used on each ‘On’ bit within Manchester code

## Slide 5: AWGN Simulations
Single Carrier is best. Low PAPR does well in AWGN

## Slide 6: Channel Model D Simulations
Single carrier does poorly in Channel Model D, due to less frequency diversity
Proposal from [1] a little better than Low PAPR, in Channel Model D

## Slide 7: SNR at 10% PER
Design | SNR @10% PER (AWGN) | SNR @10% PER (Model D)
Single Carrier | -3.74 dB | 5.30 dB
Low PAPR | -3.17 dB | 3.68 dB
Proposal from [1] | -2.41 dB | 3.40 dB

## Slide 8: Conclusions
Low PAPR is 0.76 dB better than Proposal from [1] in AWGN
  [1] indicated a 0.5 dB delta, so our results are reasonably similar to those results
Proposal in [1] is 0.28 dB better than Low PAPR design in Channel Model D
Maybe the WUR OFDM symbol generation can be left to vendor specific implementation
  Under different channel conditions the best subcarrier sequence may change
  Transmit diversity could also have an impact on the best subcarrier sequence
  Other factors like PA saturation may also have an effect

## Slide 9: References
Vinod Kristem, Shahrnaz Azizi, Thomas Kenney, “2 us OOK pulse for high rate, IEEE 802.11-18/97r0,” January 2018
Dennis Sundman, Leif Wilhelmsson, Miguel Lopez, “OOK Symbol Design,” IEEE 802.11-18/143r1, January 2018