## Slide 1: Considerations on VL WUR frames
Authors:
Alfred Asterjadhi,
George Cherian

## Slide 2: Introduction
A wake-up frame with variable length may contain the information for multiple STAs in the Frame Body [1]
  The detailed information of multiple STAs (e.g., bitmap, ID list) is TBD
  Unicast wake-up frame does not carry the information of multiple STAs
If Frame Body is present in WUR Wake Up frame and the Address field is set to 0, the Frame Body contains multiple WIDs [1]
We discuss the following items for multicast VL Wake Up frames:
  WID ordering and reception/discarding of multicast VL Wake Up frame
  WID size and contents of fields that contain the WID
We also propose to conclude on the TBDs of the Frame Body
  Inherit discussions from and adding some additional considerations [4]

## Slide 3: Ordering of WID identifiers
The order of WIDs in multicast VL Wake Up frame is undefined
  I.e., they could be in any order unless otherwise specified
  All WUR STAs need to parse all Frame Body to determine if the frame is intended to them
    While the Wake Up frame would be generally intended to a limited number of those STAs
Providing a deterministic ordering of WIDs in the Wake Up frames is beneficial
  Since it can be used by WUR STAs to early discard frames not intended to them
Discarding a Wake Up frame helps the WUR STAs to:
  Early drop Wake Up frames generated by OBSS WUR APs
    Increasing the chances of re-synching to concurrent WUR frames generated by own AP
  Avoid unnecessary processing of frames generated by WUR AP and intended to other STAs
    Reduce power consumption due to early termination of RX of these multicast VL Wake Up frames
MAC Header | Frame Body | FCS
Paged WID 1 | Paged WID 2 | Paged WID N

## Slide 4: Proposal: Ordering of WID
A WUR AP that generates a Wake Up frame that contains a Frame Body field with a list of WIDs shall order the WIDs in the Frame Body of the frame in order
  The AP shall not include the WID of a WUR STA that does not support reception of a Wake Up frame that contains a list of WIDs in the Frame Body field
A WUR STA that supports reception of Wake Up frames that contain Frame Body with a list of WIDs and receives such a frame may discard the frame if either of the following is true:
  Immediately after locating a WID in the WID list that is greater than the WID assigned to it and no WID equal to the WID assigned to it was located prior to it
  Immediately after locating the last WID in the WID list and the WID is less than the WID assigned to it

## Slide 5: Paged WID size
One or more WIDs [1B each or 2B each] [2]
  Option 1: One octet is sufficient to identify each of 256 STAs, and if more then:
    Schedule clones in orthogonal periods to avoid waking unintended STAs
    Pros: Reduced field size leads to minimal overhead
    Cons: Some loss of flexibility
  Option 2: Two octet is sufficient to identify each of 2048 STAs:
    Pros: Same signaling as PCR, flexible, allows extra control information to be exchanged
    Cons: Increased field size leads to increased overhead
Multiple Paged WIDs are present in multicast VL Wake Up frames
  Maximum length of the Frame Body field is either 8 octets or 16 octets [3]
    With Option 1: Up to 8 WUR STAs or up to 16 WUR STAs can be paged with one Wake Up frame
    With Option 2: Up to 4 WUR STAs or up to 8 WUR STAs can be paged with one Wake Up frame
MAC Header | Frame Body | FCS
Paged WID 1 | Paged WID 2 | Paged WID N
WID
8
Paged WID field
WID | Miscellaneous
12 | 4
Paged WID field

## Slide 6: Length of Frame Body [4]
We focus in determining the size of Length field and its unit for VL WUR frames
  Currently, the length is in units of TBD octets, and is up to 8 or 16 (TBD) octets
Size of Frame Body field will determine the maximum length of the WUR frame
  If Frame Body is 8 bytes then max WUR frame is 14 Bytes* (~1.9ms airtime@62.5kbps)
  If Frame Body is 16 Bytes then max WUR frame is 22 Bytes* (~3ms airtime@62.5kbps)
    Airtime is ~4 times less if 250 kbps is used for the transmissions
Proposal was [4]: Maximum length of Frame Body is 16 octets
    And the unit of the length field to be 2 octets in order to reduce the size of the Length field
Updated discussion:
  Some members expressed concern that airtime for WUR frame may be too long with 16 Octets
  Do not expect to be an issue because we already have a limitation on the airtime motioned [5]:
    “IEEE 802.11ba shall define an upper limit on the time duration of a WUR PPDU, to a TBD value that is less than the L-SIG LENGTH field limitation.”
    Which, depending on TBD value may lead to frames exceeding certain sizes be sent only at higher rate
 | Type | Length/Misc. | Reserved
Bits | 3-4 | 3-4 | rest

## Slide 7: Straw Poll 1
Do you support the following:
  A WUR AP that generates a Wake Up frame that contains a Frame Body field with a list of WIDs shall order the WIDs in the Frame Body of the frame in order
    The AP shall not include the WID of a WUR STA that does not support reception of a Wake Up frame that contains a list of WIDs in the Frame Body field
  A WUR STA that supports reception of Wake Up frames that contain Frame Body with a list of WIDs and receives such a frame may discard the frame if either of the following is true:
    Immediately after locating a WID in the WID list that is greater than the WID assigned to it and no WID equal to the WID assigned to it was located prior to it
    Immediately after locating the last WID in the WID list and the WID is less than the WID assigned to it

## Slide 8: Motion 1
Move to agree with the concept outlined below:
  A WUR AP that generates a Wake Up frame that contains a Frame Body field with a list of WIDs shall order the WIDs in the Frame Body of the frame in order
    The AP shall not include the WID of a WUR STA that does not support reception of a Wake Up frame that contains a list of WIDs in the Frame Body field
  A WUR STA that supports reception of Wake Up frames that contain Frame Body with a list of WIDs and receives such a frame may discard the frame if either of the following is true:
    Immediately after locating a WID in the WID list that is greater than the WID assigned to it and no WID equal to the WID assigned to it was located prior to it
    Immediately after locating the last WID in the WID list and the WID is less than the WID assigned to it
MOVED: Alfred Asterjadhi SECOND: Po-Kai Huang
Result: Passes with unanimous consent.

## Slide 9: Straw Poll 2
Do you support to amend the following text in the TGba SFD:
  “The length of the Frame Body field is in units of TBD 2 octets, and is up to 8 or 16 (TBD) octets.”

## Slide 10: References
[1] 11-18/0103r3 Further considerations on WUR frame format (J. Kim, et. al.)
[2] 11-17/1004r4 Considerations on WUR frame format (A. Asterjadhi, et. al.)
[3] 11-17/575r9 specification framework (P.K. Huang, et. al.)
[4] 11/18/0094r1 Fixing TBDs in WUR frame (A. Asterjadhi, et. al.)
[5] 11-17/1626r2 11ba PHY Frame Format—Length Discussions (H. Zhang, et. al.)