## Slide 1: TBD clarification for TGba D0.1 (WUR Beacon)
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We are working on specification draft from previous meeting
  However, there are still a lot of TBDs for us to work out
  So we will address TBDs related with WUR mode signaling

## Slide 3: Beacon period in Draft v0.1
WUR Beacon Period subfield in WUR Parameters field
  How to signal for WUR beacon period is TBD
  This subfield will be moved to WUR operation field in next version

## Slide 4: WUR Beacon Period
Signaling Method 1
  AP can notify WUR beacon period using PCR beacon period
    WUR AP may set WUR Beacon period as a multiple of PCR beacon period
  Define WUR Beacon Period subfield as follow
    This subfield has the value of WUR beacon period divided by PCR beacon period
      If value is 1, WUR beacon period is equal to PCR beacon period
      If value is 10, WUR beacon period is 10 times longer than PCR beacon period
      If value is 0, WUR beacon isn’t transmitted

## Slide 5: WUR Beacon Period
Signaling Method 1
  If WUR Beacon Period subfield has one octet
    maximum WUR beacon period can be about 4.64 hours (67 sec * 255)
    WUR beacon period can be up to 26 seconds when an AP use default PCR beacon period (100 TU, 102.4 msec)
    It seems one octet is enough
  (PCR) Beacon Interval field (IEEE 802.11-2016)
    2 octets, unit is TU
    Max value is 216 – 1 TU ( ≈ 67 sec)

## Slide 6: WUR Beacon Period
Signaling Method 2
  WUR Beacon Period subfield indicates WUR beacon period directly
    If we use TU for unit, one octet may not be enough (max 261 msec)
  So, we may use 2 (or 3) octets
    Max value is about 67 seconds (or 4.77 hours)
  WUR beacon won’t be transmitted when WUR Beacon Period subfield set to 0

## Slide 7: Summary
In this submission, we address TBD in WUR Beacon Period subfield
Two signaling methods are proposed
  AP can indicate WUR beacon period using PCR beacon period or not

## Slide 8: Straw poll 1
Which option do you prefer for WUR Beacon Period subfield?
  Option 1: WUR Beacon Period subfield has the value of WUR beacon period divided by PCR beacon period
  Option 2: WUR Beacon Period subfield indicates WUR beacon period directly

## Slide 9: Straw poll 2
Do you agree to followings?
  The WUR Beacon Period subfield is set to 0 when an AP doesn’t transmit WUR beacon frame