## Slide 1: Concluding Remarks P-OOK
Date: 2018-03-DD
Authors:

## Slide 2: Abstract
The idea of shortening the “on” period was initially proposed in [1], and we refer to it as P-OOK [2, 3]
It was verified by others in [4, 5]
Using P-OOK for the 62.5 kbit/s mode with a non-zero duration of 2 us provides a gain of 0.8-1.2 dB depending on receiver design. This comes without any additional complexity, i.e., “for free”
We will here see the performance in the PA limited case

## Slide 3: Performance results for PA limited case
 | AWGN @ 10% PER | TGnB @ 10% PER | TGnD @ 10% PER
Practical sync | -1.4 dB | -1.3 dB | +0.7 dB
Ideal sync | +1.2 dB | -1.8 dB | +1.5 dB

## Slide 4: Performance for non-PA limited case
 | AWGN @ 10% PER | TGnB @ 10% PER | TGnD @ 10% PER
Practical sync | +0.6 dB | +0.8 dB | +0.7 dB
Ideal sync | +1.2 dB | +1.7 dB | +1.5 dB

## Slide 5: Straw poll
Do you:
want to add P-OOK with non-zero time of 2 us for the 62.5 kbit/s mode as a mandatory feature?
want to add P-OOK with non-zero time of 2 us for the 62.5 kbit/s mode as an optional feature?
not want to add standardized support for P-OOK?

## Slide 6: References
[1] 0696r0 – Blank GI for the Waveform Coding
[2] 1673r1 – Partial OOK - Generalizing the Blank GI Idea
[3] 0142r3 – Additional Results for 62.5 kb/s: Symbol Structure and P-OOK
[4] 0071r0 – Performance Investigation on Partial OOK
[5] 0124r0 – Shorter ‘On’ Time Duration Study