## Slide 1: Concluding Remarks P-OOK
Date: 2018-03-06
Authors:

## Slide 2: Abstract
The idea of shortening the “on” period was initially proposed in [1], and we refer to it as P-OOK [2, 3]
It was verified by others in [4, 5]
Using P-OOK for the 62.5 kbit/s mode with a non-zero duration of 2 us provides a gain of 0.8-1.2 dB depending on receiver design. This comes without any additional complexity, i.e., “for free”

## Slide 3: Simulation Setup
We use ,
4 MHz receiver
0
0
ON
OFF
OFF
ON
1
1
ON
OFF
OFF
ON
P-OOK
P-OOK

## Slide 4: Performance for non-PA limited case
 | AWGN @ 10% PER | TGnB @ 10% PER | TGnD @ 10% PER
Correlation peak sync | +0.6 dB | +0.8 dB | +0.7 dB
Ideal sync | +1.2 dB | +1.7 dB | +1.5 dB

## Slide 5: Performance for non-PA limited case with practical synchronization
 | AWGN @ 10% PER | TGnB @ 10% PER | TGnD @ 10% PER
Practical sync | +1.0 dB | +1.0 dB | +1.0 dB

## Slide 6: Receiver window
What happens if we have a receiver window that is too wide?
0
1
0
1

## Slide 7: Performance for non-PA limited case including wider receiver window
A wider receiver window very slightly degrades the performance of the system

## Slide 8: Performance for non-PA limited case including wider receiver window using a power detector
By using a power detector instead of envelope detector, a wider receiver window can be used without loss of performance

## Slide 9: Observations using P-OOK with 2us symbols for the 62.5 kbit/s case
By tuning the receiver, it is expected that performance gains of 1 dB can be attained
This tuning of the receiver does not require any additional complexity (e.g. choosing good receiver parameters)
Even without any tuning in the receiver, P-OOK does not degrade performance noticeably

## Slide 10: References
[1] 0696r0 – Blank GI for the Waveform Coding
[2] 1673r1 – Partial OOK - Generalizing the Blank GI Idea
[3] 0142r3 – Additional Results for 62.5 kb/s: Symbol Structure and P-OOK
[4] 0071r0 – Performance Investigation on Partial OOK
[5] 0124r0 – Shorter ‘On’ Time Duration Study