## Slide 1: Protocol and frames for TDD link maintenance
Date: 2018-03-05
Name | Affiliation | Address | Phone | Email
Cheng Chen | Intel |  |  | Cheng.Chen@intel.com
Oren Kedem |  |  |  | Oren.Kedem@intel.com
Carlos Cordeiro |  |  |  | Carlos.Cordeiro@intel.com
George Cherian | Qualcomm |  |  | gcherian@qualcomm.com
Lochan Verma |  |  |  | lverma@qualcomm.com
Solomon Trainin |  |  |  | strainin@qualcomm.com
Michael Grigat | Deutsche Telekom | Deutsche-Telekom-Allee 7, 64372 Darmstadt, Germany |  | m.grigat@telekom.de

## Slide 2: Abstract
This contribution proposes the protocol and frames for TDD link maintenance.

## Slide 3: Motivation
The mmWave distribution network usage model was recently approved to be one of the use cases for 11ay (11-17/1019r2)
In order to support the operation of mmWave distribution network, several new management functions are needed (11-18/0130r1)
This contribution proposes a way to define and communicate several management functions for the new use case of mmWave distribution network.
  Goal is to build as much as possible on existing 11ad/ay spec, but introduce changes to accommodate new requirements.

## Slide 4: mmWave Distribution Network Management
As defined in 11-18/0130r1, the management functions in mmWave Distribution Network that will be addressed in this proposal include:
  Heartbeat
  Keep Alive
  Uplink Bandwidth Request

## Slide 5: mmWave Distribution Network Management (0130r1)
AP
STA
STA
Heartbeat
UL BW Request
Keep Alive
Management frames | Direction | Functions
Heartbeat | AP->STA only | Update parameters and schedule Tx/Rx time slots for associated CNs.
Keep Alive | AP->STA only | Indicate AP is alive and able to communicate, as well as negotiate Rx time slots with the peer STA
UL BW Request | STA->AP only | Indicate the aggregate state of traffic and request for change of BW grant.
(e.g., STA is collocated with another AP)

## Slide 6: Overall Proposal
Reuse existing Announce frame and include specific information elements in Announce frame to act as the Keep Alive/Heartbeat/UL BW Request messages.
  Keep Alive and Heartbeat coalesced into a single IE
Benefits of reusing Announce frame:
  Announce frame can be either Action or Action No Ack frame.
  The transmission of Announce frame can be either unicast or broadcast.
  Announce frame already includes the Timestamp field.
  TDD Slot Schedule element is already defined in [3] and included in Announce frame, which can be used for slot assignment/reservation for Keep Alive and Heartbeat messages.
  Other information elements can be included in Announce frame depending on the situation.
  Allows for minimal spec changes, minimizes overhead, and is efficient.

## Slide 7: Discussion
Some of the functions in Keep Alive/Heartbeat/UL BW Request messages can be achieved using existing elements defined in 11ay, with possibly some minor modifications.
  Slot assignment in Heartbeat and slot reservation in Keep Alive can be achieved by reusing TDD Slot Schedule element, with an added slot type to be “unavailable (see Slide 8)”.
  Rate adaptation can be done by reusing DMG Link Margin element, with some new fields added (see Slide 9-11).
    DMG Link Margin IE will be included in Announce frame
    For slow feedback, it can be transmitted separately as Keep Alive/Heartbeat.
    For fast feedback, it can be aggregated with BlockAck frame.
Define a new element for bandwidth request used in Keep Alive and UL BW Request messages (see Slide 12 and 13).

## Slide 8: Modification of TDD Slot Schedule element
Slot assignment information carried in Keep Alive message is only used for bandwidth reservation, rather than bandwidth allocation
  Applicable for DN-DN scenarios – see 0130r1
Therefore, we can add a new slot type in the TDD Slot Schedule element to indicate that this slot is unavailable.
Propose to use the reserved value “11 (binary)” in Bitmap and Access Type Schedule field within TDD Slot Schedule element to indicate the corresponding TDD slot is “unavailable.”

## Slide 9: Modification of DMG Link Margin element
Extend DMG Link Margin element and enable it to optionally contain the information fields used for TDD rate adaptation.
Fields | Octets | 
Element ID | 1 | 
Length | 1 | 
Activity | 1 | 
MCS | 1 | 
Link Margin | 1 | 
SNR | 1 | 
Reference Timestamp | 4 | 
Rate Adaptation Control | 2 | Contains the number of entries reported (NER) and indications of whether the element includes optional fields used for rate adaptation.
Parameters Across PPDUs | 0 or 3xNER | Optionally present. If present, contains the subfields of parameters across PPDUs.
Parameters Across LDPC Codewords | 0 or 8*NER | Optionally present. If present, contains the subfields of parameters across LDPC codewords.
Parameters Across Blocks/Symbols | 0 or 4*NER | Optionally present. If present, contains the subfields of parameters across SC blocks or OFDM symbols.
DMG Link Margin element format

## Slide 10: Modification of DMG Link Margin element
Subfields | Bits | Note
Number of Entries Reported (NER) | 3 | The value of this subfield plus one indicates the number of entries being reported. The entries are indexed (1 to 8) and represent space time streams. If the value of this field is greater than 1, the MCS, Link Margin and SNR fields are reserved.
Indication for Parameters Across PPDUs | 1 | Set to 1 if the DMG Link Margin element contains the “Parameters Across PPDUs” field. Set to 0 otherwise.
Indication for Parameters Across LDPC Codewords | 1 | Set to 1 if the DMG Link Margin element contains the “Parameters Across LDPC Codewords” field. Set to 0 otherwise.
Indication for Parameters Across SC Blocks or OFDM Symbols | 1 | Set to 1 if the DMG Link Margin element contains the “Parameters Across Blocks/Symbols” field. Set to 0 otherwise.
IsEDMG | 1 | EDMG (1) or non-EDMG (0). Used to differentiate MCS field.
IsSC | 1 | SC (1) or OFDM (0). Used to differentiate MCS field.
Reserved | 8 | 
Subfields | Bits
RSSI | 8
SNR Per STS | 8
Number of PPDUs | 8
Subfields | Bits
Average Iterations | 8
Max Iterations | 8
Nonzero Syndromes | 24
Number of LDPC Codewords | 24
Subfields | Bits
EVM | 8
Number of SC Blocks or OFDM Symbols | 24
Rate Adaptation Control field format
Parameters Across PPDUs field format
Parameters Across LDPC Codewords field format
Parameters Across Blocks/Symbols field format

## Slide 11: Modification of DMG Link Margin element
Field | Subfields | Note
Parameters Across PPDUs field | RSSI | RSSI for the RF chain, as defined in 30.2.2
 | SNR per STS | SNR for the space time stream, as defined in Table 54 (D1.0)
 | Number of PPDUs | Number of PPDUs used to over which the RSSI and SNR measurement were taken
Parameters Across LDPC Codewords field | Average Iterations | Average number of iterations used by the LDPC decoder for DPHY. One iteration includes processing of all rows. Value quantized to 0.1, range 0.0 to +25.5. Reset when Reset condition met.
 | Max Iterations | Maximum number of iterations used by the LDPC decoder for DPHY. One iteration includes processing of all rows. Value of integer, range 0 to +255. Reset when Reset condition met.
 | Nonzero Syndromes | Number of DPHY LDPC codewords with nonzero Syndrome. Reset when Reset condition met.
 | Number of LDPC Codewords | Number of DPHY LDPC codewords processed and included in the Average Iterations, Max Iterations and Nonzero Syndromes statistics. Reset when Reset condition met. Value 0 means not applicable.
Parameters Across Blocks/Symbols field | EVM | Indicates the average EVM in dB of the SC data symbols or OFDM data subcarriers, averaged across all PPDUs and SC blocks or OFDM symbols, having same modulation and MCS. Value quantized to 0.2dB, range -5.0 to +46.0dB. Reset when Reset condition met.
 | Number of SC Blocks or OFDM Symbols | Count of the SC Blocks or OFDM Symbols included in the average EVM value. Value is saturated to 224-1 if overflows. Reset when Reset condition met. Value 0 means not applicable.
Reset condition is defined as follows:
Any change of: modulation (SC/OFDM), MCS, Constellation, LDPC mode, GI/CP mode, MIMO rank, MIMO type.
End of reporting period

## Slide 12: TDD Bandwidth Request element
A newly defined TDD Bandwidth Request element carries the information fields needed for bandwidth reservation request included in Keep Alive and UL BW Request messages depending on the situation.
Order | Information | Notes
23 | TDD Bandwidth Request | The TDD Bandwidth Request element is optionally present. If present, the TDD Bandwidth Request element carries the information needed for bandwidth reservation for TDD networks.
Announce frame Action field format

## Slide 13: TDD Bandwidth Request element
TDD Bandwidth Request element format
Subfields | Bits | Note
Element ID | 8 | 
Length | 8 | 
Element ID Extension | 8 | 
Transmit MCS | 8 | Recommended MCS value for STA to AP transmission
Requested Tx Percentage | 16 | In unit of 0.01 percent
Number of Queue Params | 5 | Defines the number, N, of subsequent Queue Params subfields.
Reserved | 3 | 
Queue Params 1 | 72 | 
…… |  | 
Queue Params i | 72 | 1≤ i ≤N
Subfields | Bits | Note
TID | 5 | For values from 0 to 15, indicates the TID corresponding to the queue. Value 31 indicates that this field is not applicable. Other values are reserved.
Reserved | 3 | 
Queue Size | 32 | In units of bytes
Traffic Arrival Rate | 32 | Arrival rate since the last reporting event. In units of 1 Kbps.
Queue Params subfield format

## Slide 14: Summary
Set of changes proposed in this document include:
  Defining a new slot type in the existing TDD Slot Schedule element
  Modifying the existing DMG Link Margin element
  Defining a new element for link maintenance
  Defining capabilities to support each measurement type
We believe these are the minimum set of changes required to fulfill the requirements specified in 11-18/0130r1

## Slide 15: Straw Poll
Do you agree with the set of changes described in this presentation (Slides 6-13) to address TDD Link Maintenance?
  Yes
  No
  Abstain

## Slide 16: References
[1] IEEE 802.11-17/1019r2 “mmWave Mesh Network Usage Model”
[2] IEEE 802.11ay D1.0
[3] IEEE 802.11-17/1640r0 “Draft text for Scheduling for mmWave Distribution Networks”
[4] IEEE 802.11-18/0130r1 “Link Maintenance in Distribution Networks”