## Slide 1: Reconsidering Implicit Feedback for Beamforming
Date: 2018-03-08
Authors:
Name | Affiliations | Address | email
Roger Marks | Huawei | Denver, CO, USA | roger@ethair.net
Lyu Yunping (Lily) |  | Nanjing, PRC | lvyunping@huawei.com
Yang Bo (Boyce) |  | Nanjing, PRC | yangbo59@huawei.com
Yuan Fangchao (Dylan) |  | Nanjing, PRC | yuanfangchao@huawei.com

## Slide 2: Abstract
This contribution, intended for presentation to the IEEE 802.11 Wireless Next Generation (WNG) Standing Committee, discusses the value of reintroducing implicit channel feedback in future 802.11 standards.

## Slide 3: Motivation
Improving spectrum efficiency and network performance is important for WLAN.
Must continue to advance MIMO beamforming.
More spatial streams will further enhance network efficiency.
Accurate channel estimation is essential to MIMO beamforming.
Accurate channel estimation by explicit sounding becomes inefficient with many spatial streams.
Technology of channel estimation by implicit feedback has matured.
IEEE 802.11n HT supports both explicit and implicit feedback.
But 802.11ac VHT and P802.11ax HE support only explicit.
Implicit feedback for estimation requires TDD
Easy to exploit this advantage of 802.11.
Will 802.11 need to reintroduce implicit feedback for channel measurement for future standards?

## Slide 4: Background
The high-throughput (802.11n) PHY of Clause 19 specifies beamforming with both implicit (19.3.12.2) and explicit (19.3.12.3) feedback for channel estimation.
The very high-throughput (802.11ac) PHY of Clause 21 specifies SU-MIMO and DL MU-MIMO beamforming (21.3.11) using only explicit feedback for channel estimation.
During TGac activity, [6] addressed “Why Implicit TxBF is Better for 11ac”; straw poll agreed 31/0/20.
In TGac, [1] said “It is highly desirable to trim down to only one option for TGac SU-BF and MU-MIMO,” and raised issues with implicit feedback for channel estimation.

## Slide 5: Explicit vs. Implicit Feedback for Channel Estimation
Consider only the AP as beamformer and only the client as beamformee.
Explicit:
AP sends sounding frame to client
client calculates CSI
client sends calculated CSI to AP
Implicit (restricted to TDD):
client sends sounding frame to AP
AP calculates CSI based on channel reciprocity principle

## Slide 6: Comparison: Explicit vs. Implicit
 | Explicit | Implicit | Advantage
CSI Calculator | client | AP | Implicit: less burden on client
Sounding frame | One sent by AP, with HE-LTF per stream | One sent by each client | 
CSI feedback | separate report from each client; each one reports the measured CSI from each DL transmit stream | none | Implicit
Timeliness | after sounding frame, many CSI reports follow before data frame | data frame directly follows sounding frames | Implicit: less time passes between sounding and data since CSI report transmission intervenes in explicit case; works with shorter coherence time and higher speed clients

## Slide 7: Explicit feedback for channel measurement: Issues
Large overhead, even using compressed feedback
  Increasing number of spatial streams are expected in the future [4, 5].
  Overhead grows fast with spatial stream count.
  Lengthy channel feedback messaging delays interfere with timeliness of sounding frame.
Burden on client computation and power resources
  Channel estimation
  Calculation and feedback of compressed CSI
Frame designs need to be updated in order to support more spatial streams

## Slide 8: Implicit feedback for channel estimation: Issues
Issues with implicit feedback for channel estimation:
Sounding feedback cannot be collected from a beamformee with receive antennas that do not transmit.
Implicit feedback requires calibration.
The presumptions behind calibration correction need to be validated.

## Slide 9: Implicit feedback for channel estimation: Issue 1
Issue 1: “Sounding feedback cannot be collected from a beamformee with receive antennas that do not transmit.”
Possible approaches:
If client has fewer transmitters than antennas but switching is available:
  Client sends sounding frame from each antenna separately, after switching.
If some antennas are receive-only, then beamforming is supplemented with receive diversity gain [7].
Could use explicit measurement for such clients.
client
transmitter
switch

## Slide 10: Implicit feedback for channel estimation: Issue 2
Issue 2: “Implicit feedback requires calibration.”
IEEE Std 802.11 does not specify the full details of calibration.
Extensive research has gone into implicit channel estimation over the last few years due to its critical role in massive MIMO.
Earlier calibration methods made use of interactive sounding between the AP and client.
Recent research [2,3] has shown the possibility and effectiveness of transmit-side calibration (see next slide), calibrating DL TxBF based on sounding between the AP antennas only.
Calibration without sounding the clients is far more simple and reliable.

## Slide 11: Transmit-side calibration
ht1
hr1
ht2
hr2
ht3
hr3
ht4
hr4
AP
Electromagnetic reciprocity is valid.
RF chains are not reciprocal, but their effect on the channel can be modeled as relatively static, so they can be corrected by calibration.
Traditional precoding methods based on uplink sounding are only weakly dependent on calibration of RF chains at the beamformee [7]
  New methods demonstrate independence from RF chains at the beamformee.
RF chains at the beamformer can be successfully calibrated by sounding among beamformer antennas.
See [3] and many other sources.
client
Ht0
Hr0
Calibration sounding only here
CSI sounding only here (UL only)

## Slide 12: Implicit feedback for channel estimation: Issue 3
Issue 3: “The presumptions behind calibration correction need to be validated.”
Extensive research gone into implicit channel estimation over the last few years due to its critical role in massive MIMO.
The principles of the calibration have been validated in theory and practice.
The calibration model has been studied and validated in practical radios.
The time scale of calibration drift has been shown, experimentally, to be a minor source of inaccuracy in channel estimation.
New calibration methods have been proposed, including those based on frequency-dependent smoothing, predistortion compensation, comb calibration, etc.
See [2], [3], [8], [9], and references therein.

## Slide 13: Summary
With increasing MIMO complexity, overhead of explicit feedback for channel estimation becomes prohibitive.
Issues of implicit feedback for channel estimation can be solved today based on tremendous research efforts that have been made.

## Slide 14: Straw Poll 1
Do you think that future WLAN developments will lead to a demand for more MIMO spatial streams in a WLAN network?
  Yes: 39
  No: 1
  Need more information: 29
  Abstain: 1

## Slide 15: Straw Poll 2
Do you think that 802.11 should anticipate the reintroduction of implicit feedback for channel estimation in the future for standards below 7 GHz?
  Yes: 17
  No: 0
  Need more information: 46
  Abstain: 2

## Slide 16: References
[1] IEEE 802.11-10/1105r0, “11ac Explicit Sounding and Feedback,” 2010-11-09 [content not present in r1]
[2] “Real-time Distributed MIMO Systems,”SIGCOMM ’16, August 22 - 26, 2016
[3] “Reciprocity Calibration for Massive MIMO: Proposal, Modeling and Validation,” IEEE Transactions on Microwave Theory and Techniques, Vol. 65, No. 5, May 2017, pp. 1735-1750.
[4] IEEE 802.11-13/1046r2, “Discussion for Massive MIMO for HEW,” 2013-09-15
[5] IEEE 802.11-13/1440r0, “Argos | Practical Massive-MIMO,” 2013-11-12
[6] IEEE 802.11-10/818r1, “Why Implicit TxBF is Better for 11ac,” 2010-07-13
[7] Eldad Perahia and Robert Stacey, Next Generation Wireless LANs: 802.11n and 802.11ac (Second Edition) 2013.
[8] “Massive MIMO Performance—TDD Versus FDD: What Do Measurements Say?”
< https://arxiv.org/pdf/1704.00623.pdf >
[9] “Algorithms and Proofs of Concept for Massive MIMO Systems,” J. Vieira, 2017-01-01 (Ph.D. Thesis, Lund University)

## Slide 17: Appendix: Overhead comparison (1)
Simple, approximate calculation, just to show the effect of overhead
•Bandwidth: 20 MHz
•Rate: 7.3 Mb/s (MCS0)
•Explicit: MU-MIMO for UL feedback, using P802.11ax approach
•Implicit: Trigger UL NDP one by one (very slow method; could be improved)
•15 ms sounding interval
-Note: 5 GHz device moving at 1 m/s moves ¼ wavelength in 15 ms

## Slide 18: Appendix: Overhead comparison (2)