## Slide 1: ‘On’ Symbol Generation
Date: 2018-03-08
Authors:

## Slide 2: Background
A number of the PHY engineers met and discussed the construction of the 4 and 2 µs ‘On’ symbols
This presentation is a straw poll based on this discussion

## Slide 3: Straw Poll
Do you support adding the following text to the SFD?
  Yes/No/Abstain
4 µs ‘On’ Symbol
The 4 µs ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz. Thirteen subcarriers are used, (-6, -5, … -1, 0, 1, 2, … 6). The DC subcarrier is null. The other subcarriers are selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM. The last 16 values of the 64-point IFFT output are prepended to the 64 samples generating 80 samples, representing the 4 µs ‘On’ symbol. The PAPR is less than the PAPR of the 20-MHz legacy portion of the WUR PPDU. Up to three examples of coefficients will be provided in the standard.
2 µs ‘On’ Symbol
The 2 µs ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz. Thirteen subcarriers are used, (-6, -5, … -1, 0, 1, 2, … 6). The following subcarriers are null: (-5, -3, -1, 0, 1, 3, 5). The other subcarrier are selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM. The first 32 values of the 64-point IFFT output are selected. The last 8 samples of those 32 samples prepended to the 32 samples generating 40 samples, representing the 2 µs ‘On’ symbol. The PAPR is less than the PAPR of the 20-MHz legacy portion of the WUR PPDU. Up to three examples of coefficients will be provided in the standard.

## Slide 4: Motion
Add the following text to the SFD
  Move: Steve Shellhammer, Second: TBD
Copy Text From Previous Slide (after any edits)