## Slide 1: “Speak only when spoken to” mode
Date: 2018-04-10

## Slide 2: Abstract
It would be very useful for at least one purpose (managing 11b-only devices within g/n/ax BSSs), and useful for other purposes, to have a “speak only when spoken to” mode of operation. This presentation describes some of the motivating uses.
CIDs addressed: 1589

## Slide 3: A primary use case
2.4GHz devices from 11g on must use single-tone protection mechanisms when 11b-only (NonERP) devices are associated
  Cf. 10.27.2
There are relatively few currently deployed 11b-only devices
  But for IoT devices, this is a desirable design option
  It is commonly asserted that omitting OFDM modes entirely enables low power consumption, and the use of coin cell batteries
  And it only takes one such device in a BSS to trigger the protection mode requirement
  Some common estimates are that a single 11b-only device associating can cause an immediate 30% drop in BSS throughput—even if that device transmits only rarely

## Slide 4: A primary use case—II
The “speak-only-when-spoken-to” mode would provide a simple way of avoiding the throughput penalty, while still preserving the same level of coexistence:
  The (new, IoT-oriented) 11b-only non-AP STA could associate and enter speak-only-when-spoken-to mode: the STA would only be able to transmit when permitted (poll, TWT, RAW, or other)
  So no need for the AP to use single-tone protection mechanisms, on behalf of that STA, at any other time
More generally, this provides a way of managing multiple PHYs in future: no need to have longer and longer preambles incorporating every previous generation

## Slide 5: A second use case*
With deployed APs implementing ever-greater numbers of spatial streams, uplink transmissions can be received successfully at correspondingly lower received signal levels
However, there’s a catch: the AP has to set its CCA threshold at a correspondingly low level; and setting the level too low will cause deferral for OBSS traffic too often
The “speak-only-when-spoken-to” mode provides a simple way of optimizing operation: the AP can modify its CCA threshold dynamically—low levels when polling devices for which that is necessary
* If there were only one use, it would be reasonable to tie the mode to that one case

## Slide 6: Discussion
There are many possibilities for the enabling protocol:
  Setup & teardown to negotiate how often the STA needs to be polled, renegotiate, allow interrupts, etc.
  Mandatory or optional (or both as variants)

## Slide 7: Straw poll
Do you support (in principle) adding definitions and supporting protocol for speak-only-when-spoken-to mode?
  Yes
  No
  Need more detail but generally supportive
  Need more detail but generally not supportive
  No opinion