## Slide 1: WUR Beacon transmission
Date: 2018-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
WUR Beacon is defined in SFD and Draft spec.
Also we have discussed and passed a motion about FDMA transmission
So we will address how to transmit WUR Beacon frame when we use FDMA transmission

## Slide 3: FDMA
We had a passed motion for FDMA transmission [1]
  WUR PPDU can be transmitted in multiple channels
  WUR STAs are distributed in multiple channels
  Each WUR STA may only receive WUR PPDU through the allocated WUR channel

## Slide 4: WUR Beacon
WUR Beacon is key functionality of discovery and synchronization
  It is recommended that all WUR STA receive the WUR beacon frame
  However, unlike PCR, a WUR STA assigned to the secondary channel can not receive the WUR Beacon transmitted through the primary channel only
So we should define a rule for WUR STA operating in secondary channel

## Slide 5: Ground rule
AP follows legacy multi-channel contending rule for FDMA transmission
  WUR Beacon frame can be transmitted in 20 MHz, 40 MHz, 80 MHz, or 160 MHz channel
  WUR Beacon cannot be
  transmitted through
  the secondary channel only

## Slide 6: Option 1
WUR beacon is transmitted in all WUR channel
  All WUR STA can receive WUR beacon frame without channel switch
  However, WUR beacon frame cannot be transmitted on secondary channels when they are busy

## Slide 7: Option 2
WUR beacon is transmitted in one WUR channel only
  WUR STA has to switch its WUR operation channel for WUR beacon reception
  After receiving WUR beacon, the WUR STA will return to its WUR operating channel

## Slide 8: Other options ?
A presentation was submitted in January meeting
  It discussed two approaches to send WUR beacon on multiple WUR channels [2]

## Slide 9: Discussion
Option 1: WUR beacon is transmitted in all WUR channel
  Sometimes WUR beacon frame cannot be transmitted in secondary channel(s)
  If the WUR STA operating on secondary channel could not receive continuous WUR beacon frames, it may lose its synchronization
  There should be supplement beacon transmission for the WUR STA operated on the second channels

## Slide 10: Discussion
Option 2: WUR beacon is transmitted in one WUR channel only
  Channel switching may require a guard time and power consumption
  If a WUR STA couldn’t receive WUR beacon frame on the beacon channel at the TWBTT, it has to wait WUR beacon reception for a while on the channel
    To prevent channel mismatch problem, WUR beacon waiting time shall be indicated between AP and STA
    If an AP wants to send Wake up frame right after TWBTT, it may only send wake up frame after WUR beacon waiting time
We prefer option 2

## Slide 11: Summary
In this submission, we addressed how to transmit WUR beacon frame when we adopt FDMA
  If we adopt WUR beacon on all WUR channel, WUR STA doesn’t have to switch its WUR channel, but we may need additional WUR beacon transmission on secondary channel
  If we adopt WUR beacon on single channel, WUR STA has to switch its WUR channel, but no beacon retransmission are required

## Slide 12: Reference
[1] 11-17-1625-06-00ba-efficient-fdma-transmission-schemes-for-wur-wlan.pptx
[2] 11-18-0113-00-00ba-wur-beacon-transmission.pptx

## Slide 13: Straw poll 1
Do you support following sentences?
  WUR beacon frame is transmitted on single channel
  When the channel on which the WUR STA is operating and the channel on which the WUR beacon is transmitted is different, the WUR STA has to switch channel for WUR beacon reception
  After receiving WUR beacon, the WUR STA will return to its WUR operating channel