## Slide 1: Cabling Needs for Next Generation Wi-Fi
Date: 2018-04-27
Authors:

## Slide 2: Abstract
Examine 802.3 rates to support next generation Wi-Fi AP’s and systems.

## Slide 3: Overview
With the higher data rates of 802.11ax/ay systems and beyond, we need to examine the potential need for new 802.3 standards to support cabling requirements of 802.11 APs and distribution systems
The question is similar to the one asked a few years ago, which led to the development of 802.3bz for 2.5 and 5Gb/s operation over balanced twisted pair wiring. 802.3bz is now a completed amendment.

## Slide 4: Example Usage Models for Recent Amendments Requiring increased Backhaul Rates
Many of the 802.11ax usage models [1] indicate high number of STAs per AP with the potential for large aggregated traffic load, e.g. Usage 1a “200 users at 20 Mbps”
Several 802.11ay usage scenarios [2, 3] will also require high capacity backhaul to manage the increase in traffic
  In [2] Usage Model 5 “Video/Mass-Data Distribution/Video on Demand System” requires backhaul to “11ay interfaces deployed in ceilings of large room/space”
  In [3], the mmWave distribution network using fiber as backhaul could implemented with Ethernet over optical fiber

## Slide 5: Maximum PHY rates
2.4 GHz 11ax
  2.2941 Gbps (40 MHz, 8SS, MCS11, 0.8usec GI)
5 GHz 11ax
  9.6078 Gbps (160 MHz, 8SS, MCS11, 0.8usec GI)
60 GHz 11ay
  277.2 Gbps (8.64 GHz, 8SS, SC MCS20, Short GI)
  303.3 Gbps (8.64 GHz, 8SS, OFDM MCS 19, Short GI)

## Slide 6: Reality of Products and Deployments
Estimate of a future tri-band high-end AP:
2.4 GHz 11ax
  20 MHz, 4SS, MCS11, 0.8usec GI = 573.5 Mbps
5 GHz 11ax
  160 MHz, 6SS, MCS11, 0.8usec GI = 7.2059 Gbps
60 GHz 11ay
  2.16 GHz, 2SS, SC MCS20, Short GI = 17.325 Gbps
Summing across the bands (assuming simultaneous operation) and converting to throughput (with MAC overhead of 70%) gives a total throughput of 17.6 Gbps

## Slide 7: Throughput Requirement of 802.3
To support next generation Wi-Fi systems and products would require 802.3 to support 802.11 throughput of 17.6 Gbps
Since 802.3 is full duplex, the maximum rate would depend on the upstream vs. downstream 802.11 traffic mix
In the worst case, if we assume peak traffic in one direction, we would require 802.3 to support >17.6 Gbps

## Slide 8: References
[1] 13/0657r6, “Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA”
[2] 15/0625r7, “IEEE 802.11 TGay Use Cases”
[3] 17/1019r2, “mmWave Distribution Network Usage Model”