## Slide 1: Co-channel interference tolerance requirements for millimeter wave distribution networks
Name | Affiliation | Address | Phone | Email
Djordje Tujkovic | Facebook | 1 Hacker Way Menlo Park, CA 94025 |  | djordjet@fb.com
Krishna Gomadam |  |  |  | kgomadam@fb.com
Alireza Mehrabani |  |  |  | tarighat@fb.com
Nabeel Ahmed |  |  |  | nabeel@fb.com
Payam Torab |  |  |  | ptorab@fb.com
Nikolas Olaziregi | Nokia | Copernicuslaan 50, 2018 Antwerp, Belgium |  | Nikolas.Olaziregi@nokia.com
Michael Grigat | Deutsche Telekom | Deutsche-Telekom-Allee 7, 64372 Darmstadt, Germany |  | m.grigat@telekom.de

## Slide 2: Overview
Significance of co-channel interference (CCI) for fixed wireless access use case was discussed in [1]
Same presentation also proposed various CCI tolerance mechanisms
  PHY-level mechanisms
    Different preambles (signatures), signal rotation [non-standard DMG PPDUs]
    RSSI jump detection [using standard DMG PPDUs]
  MAC-level mechanisms
    Receive (Rx) abort (stopping the receive operation at PHY level) when it is determined the frame going through receive pipeline is not intended for the STA
This presentation attempts to:
  Specify a PHY-level CCI tolerance requirement for TDD capable DMG STAs (although it will benefit any other DMG device performance)
  Formalize the complementary (not alternative) MAC-level CCI tolerance mechanism
  Propose straw polls

## Slide 3: Need for co-channel interference tolerance (1) Severe impact in TDD case
With fixed wireless access and scheduled time slots the interference pattern can be severe
  Correlated transmit times on main and interfering links
Polarity concept mitigates self interference for collocated radios, but also aligns receive periods
Example
  Two Distribution Nodes (DNs) receiving from two Client Nodes (CNs) during the same TDD slot
  CN1 and CN2 can transmit almost at the same time, with arrival times deterministically different due to propagation delays
  Conflicts cannot always be resolved through network scheduling (i.e., assigning different TDD slots to CN1 and CN2)
In general early weak interference can occur any (early) time relative to the intended packet
  TDD transmission can start anywhere within a TDD slot
  Non-TDD DMG devices
  Other TDD instances
CN1 → DN1
PPDU
CN2 → DN2
PPDU
Example scenario: Transmissions beginning at TDD slot boundary
𝜹1 : Transmit slot boundary synchronized to within ±1 µs
𝜹2 : Time of flight difference (d1 – d2)/c typically within ±1 µs
(compare with DMG STF duration of 1.2364 µs)
𝜹1 + 𝜹2

## Slide 4: Need for co-channel interference tolerance (2) Field measurement - observations
CN2 Tx | Modem | Modem | Modem | DN1-CN1 | DN1
power | INR | SIR | SINR | throughput | PER
(dBm) | (dB) | (dB) | (dB) | (% of full rate) | (%)
31 | 9 | 10 | 9.5 | 4.60% | 92.00
29 | 8 | 11 | 10.4 | 3.70% | 93.00
27 | 7 | 12 | 11.2 | 4.60% | 92.00
25 | 5 | 14 | 12.8 | 4.60% | 92.00
23 | 3 | 16 | 14.2 | 4.60% | 92.00
21 | 2 | 17 | 14.9 | 3.70% | 92.00
19 | 0 | 19 | 16.0 | 3.70% | 92.00
17 | -2 | 21 | 16.9 | 3.70% | 92.00
15 | -4 | 23 | 17.5 | 4.60% | 90.00
13 | -6 | 25 | 18.0 | 18.70% | 69.00
11 | -8 | 27 | 18.4 | 65% | 27.00
9 | -10 | 29 | 18.6 | 93% | 5.00
7 | -12 | 31 | 18.7 | 99% | 0.70
Early weak interference impact is severe
  Example: 11ad baseband operating at ≥ 13.4 dB input SNR should have ~ 0% PER (measured 92% PER)
Interference to Noise Ratio (INR) has a high dynamic range
  -5 to 10 dB of interest for 11ad MCS set

## Slide 5: PHY requirement
TDD CCI rejection

## Slide 6: TDD Co-Channel Interference (CCI) Requirement (1) Background
Given INR high dynamic range, we suggest to formulate CCI requirement across different SNR regions, or alternatively, for different modulations
Formulations are equivalent; per-modulation (MCS) formulation is more structured (cleaner) and preferable
Interference waveform is made of other DMG PPDUs
Proposed requirement language
  Signal level absolute (dBm), relative to IEEE receive sensitivity (+X dB above sensitivity)
  Interference level absolute (dBm)
  Interference level does not include training fields to leave out power variations
  All levels at antenna input (over the air) for testability
  Packet error rate (PER) defined and maintained the same as IEEE receive sensitivity

## Slide 7: TDD Co-Channel Interference (CCI) Requirement (2) Proposed text (to highlight technical intention – final text can be refined)
20.3.3.9 Receiver co-channel interference rejection (TDD only)
For TDD devices receiving intended PPDUs (“signal”) and interfering PPDUs (“interference”), PER shall/ should be less than 5% for a PSDU length of 256 octets at MCS 0, and less than 1% for a PSDU length of 4096 octets at other MCSs, with MCS dependent signal and interference levels listed in Table xyz, defined at the antenna connector(s). Intended and interfering PPDUs are assumed to to be subject to the same antenna gain, and interfering PPDUs are assumed not to include any beamforming training fields.
  NOTE 1 — For RF power measurements performed over the air, the input level shall be corrected to compensate for the antenna gain in the implementation. The gain of the antenna is the maximum estimated gain by the manufacturer. In the case of the phased-array antenna, the gain of the phased-array antenna is the maximum sum of estimated element gain minus 3 dB implementation loss.
  NOTE 2 — Interfering PPDUs can be transmitted with any arbitrary offset relative to intended PPDU.
  Table xyz – TDD CCI Tolerance
MCS | Modulation | Signal level above IEEE receiver sensitivity (dB) | Interference level (dBm)
0 | DBPSK | 12 | -78
1 - 5 | BPSK | 2 | -78
6 – 9.1 | QPSK | 3 | -68
10 – 12.2 | 16-QAM | 7 | -64
12.3 – 12.6 | 64-QAM | 11 | -60

## Slide 8: TDD Co-Channel Interference (CCI) Requirement (3) Discussion
With the specified signal and interference levels
  RSSI in modem ((S+I+N)/(I+N)) jumps at least +6.5 dB with intended PPDU for all DMG MCS values
  Implementation assumptions comparable to those assumed for 802.11ad receive sensitivities 10 years ago
    Better noise figure and implementation loss is easily achievable today
  Different realistic combinations are possible to meet these requirements, e.g.,
    9 dB Noise Figure
    3 dB Implementation Loss (in the true sense of signal loss)
    24 dB Rx EVM (for operation up to 802.11ad MCS 12)

## Slide 9: TDD MAC requirement (TOOLS)
CCI rejection

## Slide 10: MAC-level CCI tolerance (1) Background, reminder
Interfering PPDUs can keep the radio busy at the beginning of a TDD slot, resulting in the STA missing the intended packet, even with sufficient SIR
Interfering PPDUs can be opportunistically rejected by aborting receive mode (Rx abort) at the end of (or shortly after) the previous TDD slot
This is a time-domain mechanism that works independent of interference power level
Interference sources
  DMG devices outside the network
  Neighboring links from different distribution networks (unsynchronized) on the same channel
TDD slot
STA A − Rx
STA B − Tx
TDD slot
STA A − Rx
STA C − Tx
B → A
PPDU
C → A
PPDU
Interfering PPDU
B → A
PPDU
C → A
PPDU
Interfering PPDU
With receive abort at the end of the slot:
C→A PPDUs can be correctly received assuming sufficient SIR
Abort receive at slot boundary or after a guard time based on largest time synchronization error
Without receive abort at the end of the slot:
the interfering PPDU will block the C→A PPDU even with sufficient SIR
Preamble
TDD slot guard time
Notes: 

## Slide 11: MAC-level CCI tolerance (2) Value addition to PHY-level mechanism
MAC-level rejection shows its value mostly at low (robust) MCSs
It is particularly useful to protect MCS 0 transmissions
  Examples: DMG Beacon, Announce and TDD SSW frames
Example
    Intended MCS 0 frame at sensitivity (-78 dBm)
      For example, C → A DMG Beacon or TDD SSW frame in the previous slide (valuable frames)
    Early interfering PPDU close to same power as intended PPDU (e.g., -78 dBm)
    SINR at modem input ~ -9.7 dB, about 2 dB more than what is required for MCS 0, but digital RSSI increase (jump) with arrival of desired PPDU < 1 dB *
     There is enough SINR to decode the intended PPDU, but no workable PHY-level mechanism to reject the interference; aborting the interference receive at the end of the first slot however leads to receiving the intended PPDU without error
    * Assuming 9 dB Noise Figure, 3 dB Implementation Loss, 24 dB Rx EVM
Notes: 

## Slide 12: MAC-level CCI tolerance (3) PHY-RXABORT primitive
PHY-RXABORT primitive
  Similar to PLME-RESET, without resetting Rx and Tx state machines
  Local, i.e., .request only
When to invoke
  At or shortly after end of a TDD slot where the TDD STA PHY has been in Rx mode
  At RA mismatch (opportunistically, for long enough PPDUs)
PHY-RXABORT | X |  | 

## Slide 13: Summary - Complementary requirements
PHY-level tolerance
  Can filter early weak interfering PPDUs, independent of position within a TDD slot
MAC-level tolerance
  Can filter interfering PPDUs that cross a TDD slot boundary, independent of power
  Can filter interfering PPDUs with RA mismatch in some cases, independent of power (1)
(1) Assuming sufficiently long PPDUS, sufficient SINR, implementation dependent

## Slide 14: Straw poll (1) – PHY-level CCI requirement for TDD
Do you agree with requirement in Slide 7 for TDD receivers? (summary below)
Summary: Same PER as IEEE receive sensitivity with following signal and interference levels
Signal
(DMG PPDU)
Interference
(DMG PPDU)
MCS | Modulation | Signal level above IEEE receiver sensitivity (dBm) | Interference level (dBm)
0 | DBPSK | 12 | -78
1 - 5 | BPSK | 2 | -78
6 – 9.1 | QPSK | 3 | -68
10 – 12.2 | 16-QAM | 7 | -64
12.3 – 12.6 | 64-QAM | 11 | -60
No training field for the purpose of specification
Arbitrary
(random) offset
 | Mandatory (“shall”) for TDD-capable devices | Recommended (“should”) for TDD-capable devices
Yes: |  | 
No: |  | 
Abstain: |  | 

## Slide 15: Straw poll (2) – MAC-level CCI requirement for TDD
Do you agree with adding a PHY-RXABORT primitive to the PHY SAP service primitives table (Table 8-2), with usage defined at least for mmWave Distribution Networks (TDD)? Usage will be optional, with examples including TDD slot boundaries and RA mismatch.
  Yes:
  No:
  Abstain:

## Slide 16: References
[1] 11-18-0164-01-00ay-interference-mitigation-in-distribution-networks