## Slide 1: Multiantenna TX Diversity
Date: 2018-05-07
Authors:

## Slide 2: Introduction
When multiple antennas are available at the Access Point, it is necessary to use some transmit diversity scheme to avoid destructive interference at the wake-up receiver
  Several earlier studies addressed this topic [1, 2]
As in [1,2] we recommend use of legacy CSD for the wideband portion of the PPDU
Here we focus on the narrowband portion of the PPDU
We consider two CSD designs for up to eight TX antennas
Cover both the high data rate (HDR) and the low data rate (LDR)
  Present Channel Model D simulations. AWGN sims in backup.

## Slide 3: 4 MHz Bandwidth
Since the narrowband portion is only 4 MHz in bandwidth we want to use larger CSD than in legacy systems
A larger CSD values provides a faster phase ramp in the frequency domain, leading to more phase rotations within this narrower 4 MHz bandwidth
For example, a 200 ns CSD had a phase rotation period of 5 MHz
  This indicates a larger CSD may be valuable

## Slide 4: MC-OOK ‘On’ Symbols
MC-OOK 2 µs ‘On’ Symbol
  32-pt FFT
  seq = [1, 1, 1, 0, -1, 1, -1];
  Used in Sync Field and HDR Data Field
MC-OOK 4 µs ‘On’ Symbol
  64-pt FFT
  seq = [1, 1, 1, -1, -1, -1, 1, 1, -1, 1, 1, -1, 1];
  Used in LDR Data Field

## Slide 5: High Data Rate CSD Designs
CSD Design | # Antennas | CSD Values (ns) | Comment
A | 1 | [0] | Uniform spacing
 | 2 | [0, -250] | 
 | 3 | [0, -250, -500] | 
 | 4 | [0, -250, -500, -750] | 
 | 5 | [0, -250, -500, -750, -1000] | 
 | 6 | [0, -250, -500, -750, -1000, -1250] | 
 | 7 | [0, -250, -500, -750, -1000, -1250, -1500] | 
 | 8 | [0, -250, -500, -750, -1000, -1250, -1500, -1750] | 
Since the HDR uses 2 µs ‘On’ symbols for both the Sync Field and the Data Field, we use the same CSD for both fields
Notation: We used negative CSD values, as in earlier amendments. It is straightforward to convert to positive CSD values by adding the duration of the MC-OOK ‘On’ symbol

## Slide 6: High Data Rate CSD Designs
CSD Design | # Antennas | CSD Values (ns) | Comment
B | 1 | [0] | Binary tree spacing
 | 2 | [0, -1000] | 
 | 3 | [0, -1000, -500] | 
 | 4 | [0, -1000, -500, -1500] | 
 | 5 | [0, -1000, -500, -1500, -750] | 
 | 6 | [0, -1000, -500, -1500, -750, -1250] | 
 | 7 | [0, -1000, -500, -1500, -750, -1250, -250] | 
 | 8 | [0, -1000, -500, -1500, -750, -1250, -250, -1750] | 

## Slide 7: HDR Model D Sim – CSD Design A

## Slide 8: HDR Model D Sim – CSD Design B

## Slide 9: HDR – Model D Simulation Summary
 | SNR (dB) @ 10% PER |  | SNR (dB) @ 1% PER | 
Number of TX Antennas | CSD Design A | CSD Design B | CSD Design A | CSD Design B
1 | 2.19 | 2.19 | 8.09 | 8.09
2 | 0.71 | 0.74 | 4.96 | 4.53
3 | 0.19 | 0.19 | 3.84 | 3.68
4 | -0.22 | -0.16 | 3.13 | 2.90
5 | -0.39 | -0.51 | 2.56 | 2.39
6 | -0.66 | -0.75 | 2.14 | 2.12
7 | -0.90 | -0.93 | 1.82 | 1.88
8 | -0.88 | -1.04 | 1.97 | 1.80
Design B (Binary Tree spacing) is generally better, particularly at 1% PER

## Slide 10: Low Data Rate CSD Designs
CSD Design | # Antennas | CSD Values (ns) | Comment
A | 1 | [0] | Uniform spacing
 | 2 | [0, -500] | 
 | 3 | [0, -500, -1000] | 
 | 4 | [0, -500, -1000, -1500] | 
 | 5 | [0, -500, -1000, -1500, -2000] | 
 | 6 | [0, -500, -1000, -1500, -2000, -2500] | 
 | 7 | [0, -500, -1000, -1500, -2000, -2500, -3000] | 
 | 8 | [0, -500, -1000, -1500, -2000, -2500, -3000, -3500] | 
Since the LDR uses 2 µs ‘On’ symbols for the Sync Field and 4 µs ‘On’ symbols the Data Field, we use the different CSD for the Sync and Data Fields
  Above is what we use in the Data Field
  CSD on Slide 5 is what we use for the Sync Field

## Slide 11: Low Data Rate CSD Designs
CSD Design | # Antennas | CSD Values (ns) | Comment
B | 1 | [0] | Binary tree spacing
 | 2 | [0, -2000] | 
 | 3 | [0, -2000, -1000] | 
 | 4 | [0, -2000, -1000, -3000] | 
 | 5 | [0, -2000, -1000, -3000, -1500] | 
 | 6 | [0, -2000, -1000, -3000, -1500, -2500] | 
 | 7 | [0, -2000, -1000, -3000, -1500, -2500, -500] | 
 | 8 | [0, -2000, -1000, -3000, -1500, -2500, -500, -3500] | 
Since the LDR uses 2 µs ‘On’ symbols for the Sync Field and 4 µs ‘On’ symbols the Data Field, we use the different CSD for the Sync and Data Fields
  Above is what we use in the Data Field
  CSD on Slide 6 is what we use for the Sync Field

## Slide 12: LDR Model D Sim – CSD Design A

## Slide 13: LDR Model D Sim – CSD Design B

## Slide 14: LDR – Model D Simulation Summary
 | SNR (dB) @ 10% PER |  | SNR (dB) @ 1% PER | 
Number of TX Antennas | CSD Design A | CSD Design B | CSD Design A | CSD Design B
1 | -1.34 | -1.34 | 4.54 | 4.54
2 | -3.07 | -3.28 | 1.14 | 0.60
3 | -3.75 | -4.00 | 0.06 | -0.65
4 | -4.37 | -4.47 | -1.02 | -1.45
5 | -4.71 | -4.68 | -1.48 | -1.71
6 | -5.04 | -5.02 | -2.18 | -2.06
7 | -5.33 | -5.22 | -2.62 | -2.40
8 | -5.29 | -5.31 | -2.21 | -2.72
Design B (Binary Tree spacing) is generally better, particularly at 1% PER

## Slide 15: Conclusions
Demonstrated Two CSD designs for our suggested 2 and 4 µs MC-OOK symbols, used in the Sync and Data fields, for multiantenna systems up to 8 antennas
With our suggested 2 and 4 µs MC-OOK symbols, both CSD designs work well
  The MC-OOK symbols used in this presentation work well for both CSD designs
The Binary Tree spacing design generally works better than the uniformly spaced design
We recommend that the binary tree spacing CSD design be included in the draft, for the example 2 and 4 µs MC-OOK ‘On’ symbols used in this presentation

## Slide 16: References
Rui Cao, Sudhir Srinivasa, Hongyuan Zhang, “Discussion on WUR Multi-Antenna Transmission,” IEEE 802.11-18/413r2, March 2018
Vinod Kristem, Shahrnaz Azizi, Thomas Kenney , “WUR performance study with multiple TX antennas,” IEEE 802.11-18/493r0, March 2018

## Slide 17: Backup

## Slide 18: HDR AWGN Sim – CSD Design A
A random phase rotation is applied to each transmit antenna to model RF carrier phase rotations due to different path lengths

## Slide 19: HDR AWGN Sim – CSD Design B

## Slide 20: HDR – AWGN Simulation Summary
 | SNR (dB) @ 10% PER | 
Number of TX Antennas | CSD Design A | CSD Design B
1 | -4.02 | -4.02
2 | -3.27 | -3.95
3 | -3.64 | -3.71
4 | -3.38 | -3.70
5 | -3.34 | -3.40
6 | -3.36 | -3.23
7 | -3.24 | -3.17
8 | -3.24 | -3.20

## Slide 21: LDR AWGN Sim – CSD Design A

## Slide 22: LDR AWGN Sim – CSD Design B

## Slide 23: LDR – AWGN Simulation Summary
 | SNR (dB) @ 10% PER | 
Number of TX Antennas | CSD Design A | CSD Design B
1 | -7.70 | -7.70
2 | -7.51 | -7.60
3 | -7.36 | -7.51
4 | -7.34 | -7.49
5 | -7.35 | -7.41
6 | -7.32 | -7.32
7 | -7.30 | -7.31
8 | -7.29 | -7.29