## Slide 1: Format for Group Addressed Wake Up Frames
Date: 2018-05-07
Authors:

## Slide 2
Abstract
In this contribution, we look at different options of addressing for group addressed wake up frames; in addition, we propose to include a multicast counter in group addressed wake up frames containing a GID.

## Slide 3: Introduction
802.11ba agreed to use group addressed wake up packets to wake up multiple STAs [1]
  “IEEE 802.11ba shall define a mechanism to wake up multiple WUR mode STAs (e.g., multiuser wake-up frame)”
  “GID is the GROUP ID provided by the AP and identifies one or more WUR STAs”
Some decisions have been made regarding addressing in group addressed wake up frames:
  Option 1: identified by a GID
  Option 2: identified by “0” and the frame body contains a list of WIDs
However, there may be additional schemes that are more beneficial
In this contribution, we evaluate these addressing schemes for their benefit and cost

## Slide 4: Addressing in Group Addressed Wake Up Frames (1)
Group addressed wake up frames may be used in several ways
  A group of STAs are woken up to receive a group addressed frame on PCR
  A group of STAs are woken up since AP has buffered frames for these STAs and the PCRs of these STAs are MU capable
  A group of STAs are woken up concurrently to reduce WUR signaling overhead
  GIDs may have implications: group addressed PCR packets [3], MU, etc.
Group addressed wake up frames can be addressed in several ways
  Option 1: Addressed by GID
  Option 2: Addressed by “0”and a list of individual WIDs
  Option 3: Addressed by GID in the initial multicast WUP; and addressed by GID and a list of individual WIDs in retransmissions

## Slide 5: Addressing in Group Addressed Wake Up Frames (2)
Option 1: Addressed by GID
  Provides the shortest WUR packet format with predicable length
  Needs WUR configuration for GID using PCR
    not expecting to be a big burden
  May wake up a STA multiple times
    E.g., when the AP detects that some STAs associated with a GID that have not been woken up yet and retransmits the multicast WUP with GID
    Other identifiers may need to be added
Option 2: Addressed by “0” and a list of individual WIDs
  May result into a long WUR packet given the low data rates
  Needs WUR configuration for WIDs using PCR
  Will not unnecessarily wake up any STAs
  Provides WUR STAs that do not support GIDs a way of multicast wake up, but require STAs to receive VL WUPs

## Slide 6: Addressing in Group Addressed Wake Up Frames (3)
Option 3: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retx
  Hybrid approach
  Needs indicators to differentiate initial or retransmission of multicast WUP
  Length of multicast packet can vary significantly depending on the number of WIDs included
  Needs WUR configuration for GIDs WIDs using PCR
  Will not unnecessarily wake up any STAs

## Slide 7: Addressing in Group Addressed Wake Up Frames (4)
Option 1 (group WUP addressed by GID) seems to minimize WUP medium time and provide predictable length of the WUP
  Needs to make sure that a multicast WUP doesn’t wake up a STA multiple times
  Particularly when STAs may have different duty cycles
Including a Multicast Counter field may solve the issue of waking up a STA multiple times
  Similar to broadcast WUP containing a sequence number [2] and BSS Parameter Update Counter [1]
  A WUR STA wakes up after receiving a WUP addressed to a GID that it is associated with and if the multicast counter contains a value that is different than the previous value
  A WUR STA ignores a multicast WUP if it is addressed to a GID that it is associated with and if the multicast counter contains the same value when it has already woken up by another group addressed WUP containing the same value

## Slide 8: Conclusion
We evaluated four different addressing options for multicast WUP
  Option 1: Addressed by GID
  Option 2: Addressed by “0” and a list of individual WIDs
  Option 3: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmissions
For Option 1, a Multicast Counter may be needed to prevent STAs from being woken up unnecessarily

## Slide 9
References
[1] 11-17/575r11, 802.11ba Specification Framework Document, Mar. 2018
[2] 11-17/1356r3, PS Operation for Duty Cycle STAs follow-up, Nov. 2017
[3] 11-18/464r3, Address Field in WUR Frame, Mar. 2017

## Slide 10: SP 1
Do you think that the following addressing option for group addressed wake up frames can be beneficial and should be considered to be included in 802.11ba :
  Option 3: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmissions

## Slide 11: SP 2
Do you agree that:
  A Multicast Counter field should be added to the group addressed WUP for Option 1 (group addressed wake up frame containing a GID)?