## Slide 1
Uplink Broadcast Service
Date: 2018-05-07
Authors:
Name | Affiliations | Address | Phone | email
Bahar Sadeghi Laurent Cariou Daniel Bravo Robert Stacy Farid Adrangi | INTEL | 2111 NE 25th Ave Hillsboro, OR 97124 USA | +1-503-803-2471 | Bahareh.Sadeghi@intel.com

## Slide 2: Abstract
[1 & 2] outlined sensor data collection as a use case for broadcast service on WLAN.
This contribution further develops the Uplink Broadcast Service and provides more information on
  Definition of UL BCS
  Its potential benefits
  Security considerations

## Slide 3: Uplink Broadcast
A mechanism to collect data from a STA targeted for a server in the cloud
  Does not matter which AP receives or forwards it
  Applicability: applications with best effort, low throughput, and infrequent traffic
Packet is sent pre-association as either a broadcast or destined to a particular AP
  STA may learn the AP address by listening
Benefits:
  For STA when overhead of association is significant; power save
  For AP in dense environments
    Low provisioning overhead
    Low AP resources required
  For users: zero set-up; fast AP bring-up in case of dense deployment
  For Wi-Fi: enablement of constrained low power Wi-Fi IoT devices with no IP support required

## Slide 4: More on Power Save Benefit
Scenario of interest
  STA is in power save most of the time
  STA has small amount of infrequent traffic
  STA may be mobile
Today: STA associates with an AP
  Option 1: STA wakes up every DTIM
  Option 2: STA wakes up when there is traffic to be sent and associates if association lost
  Option 3: AP Supports power saving features including BSS Max Idle/Proxy ARP/DMS, STA maintains association and wakes up to transmit data when available
Power save with UL BCS in Options 1 & 2
  Power save negligible in option 3
  AP deployment of the full suite of power save features needed to enable option 3 has been slow and is a significant effort
  UL BCS can be enabled via SW upgrade of (a thin layer in) AP

## Slide 5: Example Mechanism
STA turns on / wakes up, transmits data following CSMA/CA
  On one or multiple channels
  May scan for a beacon before transmission
  Packet includes IP address of the cloud server
AP forwards the packet to the IP address included
  It may announce its support for UL BCS in beacon
  It may optionally implement a flow control policy and drop or delay UL BCS packets
  It may optionally verify authentication of the sender with the server
  It may ACK the packet
Mechanisms to manage the UL channel access and limiting CSMA contention by UL BCS STAs can also be considered

## Slide 6: Security Considerations (1)
Credential and configuration provisioning
  Credentials: device identity, keys, server address, counter, etc.
  Can be provisioned at or post manufacturing
    Expected: at manufacturing
Key types
  Symmetric (i.e., pre-shared keys) or Asymmetric keys (public/private)
    Expected: pre-shared keys (between device and server)
Payload security (between IoT device and Server)
  Confidentiality and integrity with replay attack prevention
    Integrity expected to be implemented and used
    Confidentiality/privacy expected to be implemented but optionally used
Replay attack prevention
  Use of increasing monotonic counters
Internet
Server
AP
UL BCS STA
e2e encryption of payload
No encryption/authentication/trust
Common Network Security

## Slide 7: Security Considerations (2)
Possible Denial of Service attacks
  Malicious AP dropping packets
    It is best effort traffic
  Malicious STAs saturating the channel
    It can happen today w/ any 802.11 or other device
    May be reduced through installed policies
  Malicious STAs saturating backhaul
    AP can drop packets per chosen policy
Possible example mechanisms to control traffic from non-malicious devices:
  STA required to hear an AP indicating support before transmitting
  AP can impose limit on duty cycle of UL contention attempts
  AP can advertise specific target times for preferred UL BCS contention
  AP can advertise preferred channels for UL BCS traffic in order to steer UL BCS traffic in the frequency domain
Internet
Server
AP
UL BCS STA

## Slide 8: Summary
UL BCS enables use of Wi-Fi for constraint low power IoT devices with low throughput applications
UL BCS enables efficient scalable device management in AP for high density deployments of IoT Devices
A simple way to address possible security concerns is end-to-end encryption with pre-configuration of the device at manufacturing
More effective and efficient schemes are possible if limited DL traffic is used, e.g., ACK

## Slide 9: References
[1] 11-17/1736r4 -- Broadcast Service on WLAN
[2] 11-18/532r0 – Low Power Sensor Broadcast Use Cases