## Slide 1
Discussion on the response of a multicast wake-up frame
Date: 2018-05-07
Authors:

## Slide 2: Introduction
In unicast wake-up radio procedure, the retransmission procedure is based on the response frame as in [1]
  In unicast WUR operation, a STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up frame.
  AP may retransmit the WUR packet when it does not receive the response frame of wake-up packet from STA.
However, for multicast wake-up frame or wake-up frame containing multiple WUR ID, the response procedure is not defined
  When the rule is not defined, STAs may transmit the response frame or data frame, which makes collision with other uplink frames and downlink frame.
In this contribution, the discussion on several methods for response transmission is proceeded

## Slide 3: WUR operation for multicast wake-up frame
In current SFD, AP may schedule the downlink frame after transmitting the multicast Wake-up frame
  R.4.7.G: If a STA receives a non-individually addressed wake-up frame indicating a group addressed frame through the PCR, the STA may attempt to receive a group addressed frame through PCR
To check the STAs’ state, AP may transmit the short 802.11 frame (e.g. the trigger frame, null frame, BAR etc.)
Notes: 11aa procedure

## Slide 4: The ambiguity of the response frame for wake-up frame
There is no rule for multicast wake-up frame if they transmit the response frame
The ambiguity of response for multicast Wake-up frame may cause collision
  The uplink frame may collide with other uplink frames or the downlink frame from AP
To resolve the ambiguity, two options are possible:
  Define the rule not to transmit the response frame
  Use the indication in wake-up frame(GID type, indicator)

## Slide 5: Option 1: Define the rule not to transmit the response frame
The response frames for multicast Wake-up frame may cause collision
To avoid collision, the STA should not send the uplink frame after the wake-up frame, unless it indicated

## Slide 6: Option 2: Use the indication in wake-up frame
As in [2], AP may require the response frame in multicast Wake-up case
The STAs receiving the indicator may transmit the response frame of the wake-up frame
  If the response frame is not received, AP may retransmit the wake-up frame

## Slide 7: Conclusion
In this presentation, we discussed the ambiguity of response procedure of the wake-up frame in case of the multicast wake-up frame
The rule for response frame for the multicast wake-up frame is needed, to avoid collision
Two way for response frame is possible:
  Set the rule for multicast wake-up frame: The STA should not transmit the uplink frame in case of the multicast wake-up
  Use the indicator in Wake-up frame

## Slide 8: Reference
[1] IEEE 802.11-17/0575r11 “Spec framework”
[2] IEEE 802.11-18/103r3 “Further considerations on WUR frame format”