## Slide 1: Issues on the Frame Body with multiple WIDs
Date: 2018-05-08
Authors:

## Slide 2: Introduction
We have discussed that the units and the maximum size of Frame Body are 2 octets and 16 octets respectively [1]
  The size is indicated by 3-bit Length field
If the Frame Body field is present in Wake-up frame, multiple WIDs can be included
This contribution:
  Addresses issues on the Frame Body with multiple WIDs regarding padding
  Proposes truncation of the Frame Body in order to solve the issues

## Slide 3: Issues on the Frame Body with multiple WIDs
When multiple WIDs are present in the Frame body, padding of different lengths may occur depending on the number of WIDs
  While the Frame Body is in octet unit, the length of WUR ID is 12-bit
  The medium time of padding can be up to 192 us in LDR case
When the length of the FB is 48 (or 96) bits, different numbers of WIDs can be included in the FB
  In some cases, WUR STA might confuse 12-bit padding with WID
    Any 12-bit value can be used for WUR ID including 0x000 and 0xFFF
Frame Body Size:
If the value of Length field is L
FB size = 2(L+1) (Byte)
L | FB size (bits) | # of WIDs | Padding (bits) | Medium time of padding (us)
0 | 16 | 1 | 4 | HDR:16, LDR: 64
1 | 32 | 2 | 8 | 32, 128
2 | 48 | 3 or 4 | 12 or 0 | 48, 192
3 | 64 | 5 | 4 | 16, 64
4 | 80 | 6 | 8 | 32, 128
5 | 96 | 7 or 8 | 12 or 0 | 48, 192
6 | 112 | 9 | 4 | 16, 64
7 | 128 | 10 | 8 | 32, 128
 | Type (Wake-Up) | Length Present (1) | Length (2) | Address (0) | TD Control | Frame Body | FCS
 | WID1 | WID2 | WID3 | WID4 or padding
bits | 12 | 12 | 12 | 12

## Slide 4: Proposal
In order to reduce the padding and to avoid ambiguity in the number of WIDs in the Frame Body, unnecessary part of the Frame Body can be truncated by 1 octet
  In case the size of padding is greater than or equal to 8 bits
1-bit control information can be used to indicate the truncation of the FB
  The control bit is present in the TD Control, when the Frame Body is present in Wake-up frame
 | Type (Wake-Up) | Length Present (1) | Length (2) | Address (0) | TD Control (Truncation: 1) | Frame Body | FCS
 | WID1 | WID2 | WID3 | padding | truncated | 
bits | 12 | 12 | 12 | 4 |  | 8

## Slide 5: Benefits of the Frame Body truncation
The medium of Wake-up frame can be decreased
  By 32 us (HDR), 128 us (LDR)
No ambiguity on the number of WIDs in the Frame Body
The size of padding in the Frame Body, if present, is fixed to 4 bits
  As the padding is distinguished clearly from WUR IDs, any 4-bit value can be used for the padding
No change on the Frame Control field
  Since the Frame Control field is common for every type of WUR frame, having another bit for Length field is not recommended
L | T | FB size (bits) | # of WIDs | Padding (bits) | Medium time of padding (us)
0 | 0 | 16 | 1 | 4 | HDR:16, LDR: 64
1 | 1 | 3224 | 2 | 80 | 320, 1280
2 | 1 | 4840 | 3 | 124 | 4816, 19232
2 | 0 | 48 | 4 | 0 | 0
3 | 0 | 64 | 5 | 4 | 16, 64
4 | 1 | 8072 | 6 | 80 | 320, 1280
5 | 1 | 9688 | 7 | 124 | 4816, 19232
5 | 0 | 96 | 8 | 0 | 0
6 | 0 | 112 | 9 | 4 | 16, 64
7 | 1 | 128120 | 10 | 80 | 320, 1280

## Slide 6: Summary
In this contribution we have proposed to enable truncation of the Frame Body field containing multiple WIDs
  To increase the efficiency of the Frame Body
  To remove the ambiguity on the number of WIDs in the Frame Body
Whether the Frame Body is truncated is indicated by an 1-bit control information in the TD Control

## Slide 7: Strawpoll
Do you agree the following?
  When the Frame Body field is present in the Wake-up frame, the Truncation subfield is present in the TD Control field
    When the Truncation subfield is set to 1, the length of the Frame Body is reduced by 1 octet from the size indicated by the Length field

## Slide 8: Reference
11-18-0836-01-00ba-draft-text-for-wur-frame-format