## Slide 1: BCS Use Case Considerations
Date: 2018-05-21
Authors:

## Slide 2: Abstract
This presentation describes the following use cases.
Stadium Video Distribution

## Slide 3: Stadium Video Distribution

## Slide 4: Use Case Description
People in a stadium
Details of the game distributed to people in the stadium, e.g.: several different video streams for
  different video angles of the game (soccer etc.)
  Different sport activities that happen in parallel (athletics etc.)
People receive the video on their mobile devices

## Slide 5: Classification of Stadium Use Case
Power constrains:
  User device: medium (*)
  AP: low
User density: high (3,000 users per AP)
  Assuming
    Each user occupies 1m2
    Radius of the cell is 30m
Application:
  Packet size: large (video)
  Frequency of transmission: high
  Source of data:
    Data may be provided via an application that is co-located at the AP  data not passing the distribution system
    Data at a server (at the stadium or remotely)  data passes through the DS
(*) low = fixed power supply; medium = battery powered; medium time before charge (smart phone); high = sensor device with very long lifetime

## Slide 6: Classification of Stadium Use Case (cont.)
Security requirements
  AP does not need to trust / authenticate the recipient
  Recipient has to identify / authenticate the
    Source of data (= application level) or AP
Server
AP
STA
P2
A
P1
A
Data
Authenticator
OK
P2
A
P1
A
Frame
Server
AP
STA
P2
A
P1
A
P2b
A
P2a
P1b
A
P1a
Malicious Frame
Malicious frame can
be detected
MF
AP fragments
a packet
Malicious frame causes
data loss.
This is a potential DoS attack.

## Slide 7: Classification of Stadium Use Case (cont)
Security requirements (cont.)
  Privacy of users: do not allow to trace position (history) of users
  Integrity / authenticity of data broadcasted ... Why
  Encryption of data
    Only selected users might have to have access to the data (copyright issues?) … Why is this not solved on the application level?

## Slide 8: Potential attack scenarios for Stadium Use Case
Fake AP
  Current GTKSA uses AES, a kind of “Symmetric-key algorithm”.
  An AP and non-AP STAs in a GTKSA shares the same GTK and Key RSC/TSC.
  The AP encrypts broadcast frames by using the GTK and the Key TSC.
  The non-AP STA decrypts broadcast frames by using the GTK and the Key RSC.
  This means “Any STAs which can decrypt broadcast frames can produce encrypted broadcast frames”.
  So a malicious user can produce fake broadcast frames.
  The receivers can NOT check the integrity of broadcast frames.
DoS attack
  If the application level authentication mechanism supports per packet authentication and AP forwards each packet in a frame, the application level authentication works well.
  If the application level authentication mechanism does not support per packet authentication or AP fragments a packet into multiple frames, AP level authentication is required.

## Slide 9: References