## Slide 1: BCS Use Case Considerations
Date: 2018-05-28
Authors:

## Slide 2: Abstract
This presentation describes the following use cases.
Stadium Video Distribution
Sensor Uplink Broadcast

## Slide 3: Stadium Video Distribution

## Slide 4: Use Case Description
People in a stadium
Details of the game distributed to people in the stadium, e.g.: several different video streams for
  different video angles of the game (soccer etc.)
  Different sport activities that happen in parallel (athletics etc.)
People receive the video on their mobile devices

## Slide 5: Classification of Stadium Use Case
Power constrains:
  User device: medium (*)
  AP: low
  (*) low = fixed power supply; medium = battery powered; medium time before charge (smart phone); high = sensor device with very long lifetime
User density: high
  Current: 150-250 users per AP
    CISCO Connected Stadium Wi-Fi (https://www.cisco.com/c/dam/global/th_th/assets/docs/seminar/AISwifi_Cisco_Connected_Stadium_WiFi.pdf)
    Bi-directional communication
  If the STAs never send frames (no association/GCR), hidden node problem can be ignored.
  This means uni-directional broadcast can reduce interference and use larger cell.
  Assuming each user occupies 1m2 and the radius of the cell is 30m, 3,000 users are served by one AP.

## Slide 6: Classification of Stadium Use Case (cont.)
Application:
  Packet size: large (video)
  Frequency of transmission: high
  Source of data:
    Data may be provided via an application that is co-located at the AP  data not passing the distribution system
    Data at a server (at the stadium or remotely)  data passes through the DS

## Slide 7: Classification of Stadium Use Case (cont.)
Security requirements
  AP does not need to trust / authenticate the recipient
  Recipient has to identify / authenticate the
    Source of data (= application level) or AP
    If the application level authentication mechanism supports per packet authentication and packets are never fragmented, the application level authentication works well.
    If the application level authentication mechanism does not support per packet authentication or a packet is fragmented into multiple frames on the route from the server to the STA, AP level authentication is required.
Server
AP
STA
P2
A
P1
A
Data
Authenticator
OK
P2
A
P1
A
Frame
Server
AP
STA
P2
A
P1
A
P2b
A
P2a
P1b
A
P1a
Malicious Frame
Malicious frame can
be detected and discarded
MF
AP fragments
a packet
Or a packet fragmented by a router
Authentication of P2 is failed
by Malicious frame. It causes
data loss.
This is a potential DoS attack.

## Slide 8: Classification of Stadium Use Case (cont)
Security requirements (cont.)
  Privacy of users: do not allow to trace position (history) of users
  Integrity / authenticity of data broadcasted
  Encryption of data (optional or out of scope)
    Most broadcasting contents are considered as public and preferred to be widely distributed.

## Slide 9: Potential attack scenarios for Stadium Use Case
Fake AP
  Current GTKSA uses AES, a kind of “Symmetric-key algorithm”.
  An AP and non-AP STAs in a GTKSA shares the same GTK and Key RSC/TSC.
  The AP encrypts broadcast frames by using the GTK and the Key TSC.
  The non-AP STA decrypts broadcast frames by using the GTK and the Key RSC.
  This means “Any STAs which can decrypt broadcast frames can produce encrypted broadcast frames”.
  So a malicious user can produce fake broadcast frames.
  The receivers can NOT check the integrity of broadcast frames.
DoS attack
  If the application level authentication mechanism supports per packet authentication and AP forwards each packet in a frame, the application level authentication works well.
  If the application level authentication mechanism does not support per packet authentication or AP fragments a packet into multiple frames, AP level authentication is required.

## Slide 10: Sensor Uplink Broadcast

## Slide 11: Use Case Description
Sensors in the range of one or more AP(s)
Sensors broadcasts data to a remote server via AP(s)
  Does not matter which AP receives or forwards it
  Applicability: applications with best effort, low throughput, and infrequent traffic
AP(s) may forward the data to the server

## Slide 12: Classification of Sensor Use Case
Power constrains:
  Sensor: high
  AP: low
Sensor density: various (low to high)
Application:
  Packet size: small (sensor data)
  Frequency of transmission: low
  Source of data:
    Data are generated by sensors
    Data may be forwarded by AP(s) on application layer

## Slide 13: Classification of Sensor Use Case (cont.)
Security requirements
  e2e encryption between sensors and servers
  Frames from sensors to APs are required to authenticate
Internet
Server
AP
UL BCS STA
e2e encryption of payload
authentication to filter uplink packets
Common Network Security

## Slide 14: Potential attack scenarios for Sensor Use Case
Replay attack
  Prevent by increasing monotonic counters
DoS attack
  Malicious AP dropping packets
    It is best effort traffic
  Malicious STAs saturating the channel
    It can happen today w/ any 802.11 or other device
    May be reduced through installed policies
  Malicious STAs saturating backhaul
    AP can drop unauthenticated packets

## Slide 15: References
Use Cases of BCS, Hitoshi Morioka (SRC Software), https://mentor.ieee.org/802.11/dcn/18/11-18-0383-00-0bcs-use-cases-of-bcs.pptx
Security Considerations for BCS, Hitoshi Morioka (SRC Software), https://mentor.ieee.org/802.11/dcn/18/11-18-0384-00-0bcs-security-considerations-for-bcs.pptx
CISCO Connected Stadium Wi-Fi, https://www.cisco.com/c/dam/global/th_th/assets/docs/seminar/AISwifi_Cisco_Connected_Stadium_WiFi.pdf
Uplink Broadcast Service, Bahar Sadeghi (Intel), https://mentor.ieee.org/802.11/dcn/18/11-18-0875-00-0bcs-uplink-broadcast-service.pptx