## Slide 1: Discussion on WUR (802.11ba) States
Date: 2018-07-06
Authors:

## Slide 2: Abstract
This contribution provide a first draft state diagram for the 802.11ba non-AP STA and some supporting discussion.
r1: provides alterative drafts of the state diagram and supporting discussion based on discussion and listed references.
r2: adds a State Table, a Mode Diagram, and multiple variations on the state diagram. Also several typos and editorial corrections have been made. The terms have been refined so that the term non-AP STA refers to only the non-AP STA (PCR), WURx is the wake-up receiver, and device is used to describe the device consisting of a non-AP STA and a WURx. Also, several slides were moved to an appendix.
r3: same as r2, but uploaded to correct miss-upload of wrong file as r2.
r4: editorial updates and corrections, as suggested at the 12 July 2018 AM2 ARC SC session

## Slide 3: Assumptions
The PS mode configuration (this includes both legacy PS mode configuration and WUR mode configuration) is established during association or with a frame exchange between the non-AP STA and its associated AP when the non-AP STA is in the Active state or Awake state.
After PS mode/WUR mode configurations are agreed the device may move into a PS mode/WUR mode by the non-AP STA sending an acknowledged frame to the AP with the Power Management subfield of the Frame Control field set to 1 and then receiving an ACK of that frame from the AP.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the device: e.g. the AP will buffer frames and notify the device as specified for the configured mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the device’s “ability” to move into a state of: Awake, Doze, WUR Awake or WUR Doze (as configured).
The non-AP STA may change its state to Active at any time by sending an acknowledged frame to the AP with the Power Management subfield set to 0.

## Slide 4: Assumptions to be Confirmed
A device in WUR PS mode may change its PS mode to the non-AP STA’s pre-configured “legacy” PS mode by sending an Enter WUR Mode Suspend frame to the AP with the Power Management subfield set to 1, which is ACKed.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the non-AP STA: e.g. the AP will buffer frames and notify the non-AP STA as specified for the configured “legacy” PS mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the non-AP STA’s “ability” to move into a state of: Awake or Doze.
A device with a negotiated WUR PS mode which has suspended the WUR mode may return to the negotiated WUR mode by sending an Enter WUR Mode frame to the AP with the Power Management subfield set to 1, which is ACKed.
  After sending the ACK to the non-AP STA the AP will follow the procedures to support the device: e.g. the AP will buffer frames and notify the device as specified for the WUR PS mode.
  The non-AP STA after receiving the ACK from the AP may be in any state, but can “assume” the AP will support the device’s “ability” to move into a state of: WUR Awake or WUR Doze.
NOTE: By convention, “WUR Mode Setup frame with Action Type field of the WUR Mode element set to xxx” is called “xxx frame”

## Slide 5: AP Assumed Possible States (16) for the non-AP device
State Name | Associated | PPDUs Received | WUR PPDUs Received | PM bit
UnAssociated/Active | No | Yes | No | 0
Associated/Active | Yes | Yes | No | 0
Legacy PS Awake | Yes | Yes | No | 1
Legacy PS Doze | Yes | No | No | 1
WURx Awake | Yes | No | Yes | 1
WURx Doze | Yes | No | No | 1
“WUR Discovery” | No | No | Yes | 0
“UnAssociated/WUR Discovery “ | No | Yes | Yes | 0
“Associated/WUR Discovery” | Yes | Yes | Yes | 0
“Inactive” | No | No | No | 0
Not Allowed | No | No | No | 1
Not Allowed | No | No | Yes | 1
Not Allowed | No | Yes | No | 1
Not Allowed | No | Yes | Yes | 1
Not Allowed | Yes | No | No | 0
Not Allowed | Yes | No | Yes | 0
Power Save:
Discovery:

## Slide 6: Therefore there are Six “Power Save” Device States:
“Active Mode”
UnAssociated
  STA: PPDUs can be received and transmitted, infrastructure BSS services are not available.
Associated
  STA: PPDUs can be received and transmitted, infrastructure BSS services available
“legacy PS Mode”
  Awake
    STA: PPDUs can be received and transmitted, infrastructure BSS services available
  Doze
    STA: PPDUs are not received, infrastructure BSS services available
“WUR Mode”
  WURx Awake
    STA (PCR): PPDUs are not received, infrastructure BSS services available, WUR: WUR PPDUs can be received
  WURx Doze
    STA (PCR): PPDUs are not received, infrastructure BSS services available, WUR: WUR PPDUs cannot be received

## Slide 7: WUR Device Mode Diagram
Active Mode
“Legacy” PS Mode
WUR PS Mode

## Slide 8: WUR State Diagram Proposal (Alternate 4)
Note: WUR Discovery can be performed in any “WURx Awake” state
“Power Save States”

## Slide 9: WUR Power Save State Diagram Proposal (Alternate 3)

## Slide 10: WUR Power Save State Diagram Proposal (Alternate 2)

## Slide 11: References
IEEE 802.11-18/1016r2: “WUR State Diagram Proposal – Hamilton”
E-mail from the reflector from Mika Kasslin “Re: [STDS-802-11-TGBA] Updated WUR architecture and state machines uploaded” 2018-07-05
IEEE 802. 11-18/1098r0: “ARC SC Teleconference Minutes June 21 2018”
Private E-mail from Ganesh Venkatesan 27 June 2018 “802,11 Power Save and WUR state diagram (adaptation of 18-1016r1)”

## Slide 12: Appendix

## Slide 13: Changing State of A Non-AP STA
Unassociated can go to: Associated via association.
Associated can go to: Unassociated via disassociation, a different Associated State via reassociation. If configured an associated STA can also go to Power Save Mode or WUR mode and move to Awake State, Doze State, WURx Awake State, or WURx Doze State.
Awake can go to: Dose as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
Doze can go to: Awake as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
WURx Awake can go to: WURx Doze via the configured WUR mode. If a WUR wakeup frame is received move to Associated, and an WUR STA can suspend WUR mode and move to Awake, or Doze.
WURx Doze can go to: WUR Awake as allowed by the configured WUR mode
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 14: AP Expected Behavior for each non-AP STA State
Unassociated: An AP can receive frames from any non-AP STA.
Associated: An AP can receive and send frames from/to the non-AP STA and provides infrastructure services.
Awake: An AP assumes the STA can receive and send frames with the AP.
Doze: An AP assumes the STA cannot receive frames from the AP, and the AP buffers the traffic to the STA.
WURx Awake: An AP assumes the STA WURx can receive a WUR wake up frame and that the STA will signal the AP once it is in associated or awake state. The AP also assume the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
WURx Doze: An AP assumes the STA WURx can not receive a WUR wake up frame. The AP also assume the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 15: WUR State Diagram Proposal-Hamilton
from: [1]

## Slide 16: WUR State Diagram Proposal-Venkatesan/Huang [4]
from: [1]

## Slide 17: WUR State Diagram Proposal-Alternate based on [1],[2],[3]