## Slide 1: Discussion on WUR (802.11ba) States
Date: 2018-07-06
Authors:

## Slide 2: Abstract
This contribution provide a first draft state diagram for the 802.11ba non-AP STA and some supporting discussion.
r1: provides alterative drafts of the state diagram and supporting discussion based on discussion and listed references.
r2: adds a State Table, a Mode Diagram, and multiple variations on the state diagram. Also several typos and editorial corrections have been made. The terms have been refined so that the term non-AP STA refers to only the non-AP STA (PCR), WURx is the wake-up receiver, and device is used to describe the device consisting of a non-AP STA and a WURx. Also, several slides were moved to an appendix.
r3: same as r2, but uploaded to correct miss-upload of wrong file as r2.
r4: editorial updates and corrections, as suggested at the 12 July 2018 AM2 ARC SC session
r5: updates based on ARC/TGba Joint meeting Thursday 12 July 2018 PM2 (see [4]). Slides 3, 4, 6, and 8 has been changed.

## Slide 3: Assumptions
The PS mode configuration is established during association or with a frame exchange between the non-AP STA and its associated AP when the non-AP STA is in the Active state or Awake state.
The WRU mode configuration is established during association or with a frame exchange between the non-AP STA and its associated AP when the non-AP STA is in the Active state or Awake state.
If the WUR mode is configured and not suspended:
  When the AP receives and acks a frame from a non-AP STA with the Power Management (PM) subfield of the Frame Control field set to 1 the AP will assume the device containing the non-AP STA is in WRU mode and will follow procedures to support the device (e.g. buffering frames, sending WUR frames, etc.).
  The device containing the non-AP STA after receiving the ack may be in any state, but can “assume” the AP will support the device’s “ability” to be in: Awake, Doze, WUR Awake or WUR Doze state. (as configured)
If the WUR mode is suspended or not configured:
  When the AP receives and acks a frame with the PM subfield of the Frame Control field set to 1 from a non-AP STA the AP will assume the non-AP STA is in PS mode and will follow procedures to support it (e.g. buffering frames).
  The non-AP STA after receiving the ack may be in any state, but can “assume” the AP will support the its “ability” to be in: Awake or Doze state (as configured)

## Slide 4: Additional Assumptions
A non-AP STA may set its state to Active by sending an ACKed frame to the AP with the PM subfield set to 0.
A device with WUR mode configured may change the effect of sending a frame with the PM subfield set to 1, by sending an Enter WUR Mode Suspend frame to the AP. After the frame is ACKed:
  When the AP receives and acks a frame with the PM subfield of the Frame Control field set to 1 from a non-AP STA the AP will assume the non-AP STA is in PS mode and will follow procedures to support it (e.g. buffering frames).
  The non-AP STA after receiving the ack may be in any state, but can “assume” the AP will support the its “ability” to be in: Awake or Doze state (as configured)
A device with WUR mode configured and WUR mode suspended may change the effect of sending a frame with the PM subfield set to 1, by sending an Enter WUR Mode frame to the AP with the PM subfield set to 1. After the frame is ACKed:
  The AP will assume the device containing the non-AP STA is in WRU mode and will follow procedures to support the device (e.g. buffering frames, sending WUR frames, etc.).
  The device containing the non-AP STA after receiving the ack may be in any state, but can “assume” the AP will support the device’s “ability” to be in: Awake, Doze, WUR Awake or WUR Doze state. (as configured)

## Slide 5: AP Assumed Possible States (16) for the non-AP device
State Name | Associated | PPDUs Received | WUR PPDUs Received | PM bit
UnAssociated/Active | No | Yes | No | 0
Associated/Active | Yes | Yes | No | 0
Awake | Yes | Yes | No | 1
Doze | Yes | No | No | 1
WURx Awake | Yes | No | Yes | 1
WURx Doze | Yes | No | No | 1
“WUR Discovery” | No | No | Yes | 0
“UnAssociated/WUR Discovery “ | No | Yes | Yes | 0
“Associated/WUR Discovery” | Yes | Yes | Yes | 0
“Inactive” | No | No | No | 0
Not Allowed | No | No | No | 1
Not Allowed | No | No | Yes | 1
Not Allowed | No | Yes | No | 1
Not Allowed | No | Yes | Yes | 1
Not Allowed | Yes | No | No | 0
Not Allowed | Yes | No | Yes | 0
Power Save:
Discovery:

## Slide 6: Therefore there are Six “Power Save” Device States:
“Active Mode”
  UnAssociated
    STA: PPDUs can be received and transmitted, infrastructure BSS services are not available.
  Associated
    STA: PPDUs can be received and transmitted, infrastructure BSS services available
“legacy PS Mode”
  Awake
    STA: PPDUs can be received and transmitted, infrastructure BSS services available
  Doze
    STA: PPDUs are not received, infrastructure BSS services available
“WUR Mode”
  WURx Awake
    STA (PCR): PPDUs are not received, infrastructure BSS services available, WUR: WUR PPDUs can be received
  WURx Doze
    STA (PCR): PPDUs are not received, infrastructure BSS services available, WUR: WUR PPDUs cannot be received

## Slide 7: WUR Device Mode Diagram
Active Mode
“Legacy” PS Mode
WUR PS Mode

## Slide 8: WUR State Diagram Proposal (Alternate 4)
WUR Discovery can be performed in any “WURx Awake” state
“Power Save States”
The dashed WURx states are optional, the WURx is only “required” to be in WURx Awake or WURx Doze state in WUR PS Mode

## Slide 9: WUR Power Save State Diagram Proposal (Alternate 3)

## Slide 10: WUR Power Save State Diagram Proposal (Alternate 2)

## Slide 11: References
IEEE 802.11-18/1016r2: “WUR State Diagram Proposal – Hamilton”
E-mail from the reflector from Mika Kasslin “Re: [STDS-802-11-TGBA] Updated WUR architecture and state machines uploaded” 2018-07-05
IEEE 802. 11-18/1098r0: “ARC SC Teleconference Minutes June 21 2018”
Private E-mail from Ganesh Venkatesan 27 June 2018 “802,11 Power Save and WUR state diagram (adaptation of 18-1016r1)”
IEEE 802.11-18/1355r1: “Meeting Minutes July 2018” – TGba minutes.

## Slide 12: Appendix

## Slide 13: Changing State of A Non-AP STA
Unassociated can go to: Associated via association.
Associated can go to: Unassociated via disassociation, a different Associated State via reassociation. If configured an associated STA can also go to Power Save Mode or WUR mode and move to Awake State, Doze State, WURx Awake State, or WURx Doze State.
Awake can go to: Dose as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
Doze can go to: Awake as allowed by the configured power save mode, can renegotiate or end Power Save Mode, can go in to WUR Awake or WUR Doze if configured by sending a resume WUR frame.
WURx Awake can go to: WURx Doze via the configured WUR mode. If a WUR wakeup frame is received move to Associated, and an WUR STA can suspend WUR mode and move to Awake, or Doze.
WURx Doze can go to: WUR Awake as allowed by the configured WUR mode
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 14: AP Expected Behavior for each non-AP STA State
Unassociated: An AP can receive frames from any non-AP STA.
Associated: An AP can receive and send frames from/to the non-AP STA and provides infrastructure services.
Awake: An AP assumes the STA can receive and send frames with the AP.
Doze: An AP assumes the STA cannot receive frames from the AP, and the AP buffers the traffic to the STA.
WURx Awake: An AP assumes the STA WURx can receive a WUR wake up frame and that the STA will signal the AP once it is in associated or awake state. The AP also assumes the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
WURx Doze: An AP assumes the STA WURx can not receive a WUR wake up frame. The AP also assumes the STA cannot receive frames from the AP and the AP buffers the traffic to the STA.
Note a Non-AP STA can at any time send a frame to the AP and change its state.

## Slide 15: WUR State Diagram Proposal-Hamilton
from: [1]

## Slide 16: WUR State Diagram Proposal-Venkatesan/Huang [4]
from: [1]

## Slide 17: WUR State Diagram Proposal-Alternate based on [1],[2],[3]