## Slide 1: What is an ESS?
Date: 2018-06-01
Authors:

## Slide 2: Abstract
Ongoing discussion re:
“What is an ESS?”

## Slide 3: What is an ESS?
Current definition depends on the relationship to LLC
  “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
That would mean a 802.1 Bridged LAN (for example) creates an ESS. Probably not what we (802.11) meant.
We probably meant something about transparency of “location of attachment”/”mobility”, from whatever is using the 802.11 MAC
  and other entities, necessary to accomplish this? ESS == demarcation of this transparency??
Is it:
  Transparent to whatever upper layer is above 802.11?
  Includes entities beyond (above?) 802.11? (Like bridges in the 11ak scenario?)
  The APs have to have some common/similar configuration settings? (SSID, at least. Probably other facilities (security, etc.) and policies?)
Changes to Figure 4-1: ‘BSS’s are just STAs. These ovals are BSAs. Also, should we be saying “OBSA”?

## Slide 4: What is an ESS? (Continued)
Current definition depends on the relationship to LLC
  “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
We probably meant something about transparency of “location of attachment”/”mobility”, from whatever is using the 802.11 MAC 802 Services
  includes other entities, necessary to accomplish this? (EAP Auth Service? Bridges (11ak)? ANQP, etc?) ESS boundary == demarcation of this transparency?? Yes, + common domain of “mobility” that works, including security, policy, etc., necessary for mobility that actually works.
Is it:
  Transparent to whatever upper layer is above 802.11? No, boundary may be higher than that
  Includes entities beyond (above?) 802.11? (Like bridges in the 11ak scenario?) Yes, as needed
  The APs have to have some common/similar configuration settings? (SSID, at least. Probably other facilities (security, etc.) and policies?) Yes.
Changes to Figure 4-1: ‘BSS’s are just STAs. These ovals are BSAs. Also, should we be saying “OBSA”?

## Slide 5: What is an ESS? – Direction?
Straw proposal - ESS is: [Edit this list, per discussion]
Set of one of more basic services sets (BSSs)
Appears as a single logical network, to layers above the ESS boundary
The boundary might be above 802 (above Layer 2), or might be within Layer 2 (the MAC SAP, etc.)
The boundary must exist/be clear for participating end stations (see 802 O&A), and external devices that can interwork with the participating end stations
Provides transparency of “location of attachment” / “mobility”, as seen by layers above the ESS boundary, on both participating end stations and external end stations.
Includes all entities necessary to provide the services and transparency required.
Has a common domain of mobility and a common security and policies and configuration necessary to deliver the transparency from mobility.

## Slide 6: ESS and HESS?
What is an HESS (from the term “HESSID”)?
“Homogenous [sic] extended service set (ESS)”
Is an HESS a type of ESS, or a separate (perhaps similar) concept?
MSGCF has an “ESSIdentifier”, which is the concatenation of SSID and HESSID. Why/when do we need both?
Is this related to an SSPN? No not really – the SSPN is independent of any HESSID assignment. SSPN is a destination where I am being taken to. See Figure R-2.
(Also, in figure R-2 and Figure 4-8, the AAA server/client look to be in the data path – this doesn’t make sense. Ans, why are the BSSs not labeled BSSs?)

## Slide 7: HESS concepts (not necessarily what 802.11 says, now)
HESS purpose is to support 802.21 and/or WFA Passpoint/Hotspot 2.0
HESS is either/both consistent authentication, or equivalent access to “external things”
HESS is identifiable by HESSID, which is globally unique (MAC Address); identifies the SP (but perhaps not one-to-one)
HESS can/cannot span different ESSs or SSIDs
  Corollary: Which (if either) of these is related to 802.11 handoff?
Homogenous is misspelled ; HESS should be introduced as a term/concept
Discuss off-line with WFA experts, 802.21 experts…

## Slide 8: Needed concepts (not necessarily what 802.11 says, now)
Looked at WFA’s Deployment Guidelines:
  “If two APs have the same SSID they are considered to be part of the same wireless network. But, because SSIDs are not globally administered it is possible that two APs with the same SSID are in fact in different wireless networks. HESSID element [sic] allows devices to detect this condition.”
  What is “wireless network” in this context?
Concepts we need:
  Domain for Reassociation (and upper-layer mobility transparency)
  Domain for “same hotspot” (“local”)
  Domain for “hotspot from my [home] provider” (worldwide)
  Domain that uses the same security
  Equivalent access to “external things” (SSPN?) (CAG?)

## Slide 9: HESS concepts (not necessarily what 802.11 says, now)
Homogeneous ESS attributes (should be):
  => Must have a globally unique identifier
  Set of BSSs
  Mobility transparency to upper layers (one DS, Reassociate)
  => Same HESSID
  => SSID is the same
  => all available/reachable services are the same
  => reachable SSPN(s) are the same, if present
It’s not:

## Slide 10: Goal of <x>ESS discussion
802.11 needs to capture one or more types of STA mobility, and how each is communicated to the STA
An <x>ESS is a set of BSSs that have a common set of properties that a STA cares about.

## Slide 11: Example <x>ESS
What does version A do/have? :
  Same subnet
  IP address doesn’t change with mobility within a Version A
  “802.1Q Bridged Network”
  One DS
  Can Reassociate
  Can’t necessarily FT between all APs (more than one “mobility domain”) (not just because equipment is not capable/configured)
  Examples: 2 buildings far enough apart to not support FT (each building has its own “mobility domain”); groups of APs where there is too much latency between the groups to handle FT; <x>ESS subsetted to limit number of clients within each subset that can FT (each mobility domain has limited resource requirements)

## Slide 12: Example <x>ESS
What does version B do/have? :
  Access to the same authentication domain (RADIUS) – same database
  Not necessarily same subnet, etc.
  “Roaming Consortium”, etc. “Visited network”, “NAI Realm”

## Slide 13: Example <x>ESS
What does version C do/have? :
  Same accounting for use

## Slide 14: Example <x>ESS
What does version D do/have? :
  Same subnet
  IP address doesn’t change with mobility within a Version D
  “802.1Q Bridged Network”
  More than one DS
  Can’t reassociate across the DSs

## Slide 15: Example <x>ESS
What does version E do/have? :
  Same subnet
  IP address doesn’t change with mobility within a Version E
  “802.1Q Bridged Network”
  One DS
  Can reassociate
  Can FT

## Slide 16: Example <x>ESS
What does version F do/have? :
  Same/consistent security parameters