## Slide 1: What is an ESS?
Date: 2020-01-14
Authors:

## Slide 2: Abstract
Ongoing discussion re:
“What is an ESS?”

## Slide 3: Goal of <x>SS discussion
802.11 needs to capture one or more types of STA mobility, and how each is communicated to the STA
An <x>SS is a set of BSSs that have a common set of properties that a STA cares about.
  For example purposes, we consider/discuss <x>SS with at least two BSSs (== APs) so that we can discuss what is common and what is not.
Chair recommendations:
  For each type/topic, capture a “use case”/purpose/context
  How many such contexts are there, really?
  How many such contexts are in our (802.11) scope?
  How many such contexts are already identified (ignoring what they are named)? Is there any gap – or just confusion to sort?

## Slide 4: (Background) The 7 identified types
As of Sept 2018, had concluded the 7 types (“A” through “G”) on the following slides (5 – 11).
Status for further discussion, as of Sept 2018, on slide 12.

## Slide 5: Example <x>SS – “ESS”
What does type A do/have? :
  Single “802.1Q Bridged Network”
    That is:
    Same subnet
      There may be multiple subnets, but a given client sees a consistent subnet (or set of subnets it is using), as it moves around
    IP address(es) doesn’t change with ‘moving’ within <x>SS
    Transparency of location (“appears as a single BSS to UL”)
  One DS
  Can Reassociate
  Must have same SSID (careful!) (md D1.5 4.3.5.2)
  Can’t necessarily FT between all APs (more than one “mobility domain”) (and not just because equipment is not capable/configured, but due to ‘real’ barriers such as distance)
  Examples: Simple, well-known “ESS”; 2 buildings far enough apart to not support FT (each building has its own “mobility domain”); groups of APs where there is too much latency between the groups to handle FT; <x>SS subsetted to limit number of clients within each subset that can FT (each mobility domain has limited resource requirements)

## Slide 6: Example <x>SS – “HESS” (or close)
What does type B do/have? :
  Access to the same authentication domain (RADIUS) – same database (the same authentication server)
    Identified by (the WFA’s) HESSID
  Not necessarily same subnet, etc.
  Access to the same SSPN (802.11u)?? -- Need to settle this
  Example: National/Worldwide chain of stores
  No assumption that there is a single SSID -- Do we agree this?
  Discovery/Selection: SSPN information (“Roaming Consortium”, “Visited network”, “NAI Realm”, etc.)
  Connection credentials:

## Slide 7: Example <x>SS
What does type C do/have? :
  Same accounting for use
  Need to return to this, remind ourselves of the use case/scenario that’s different from type B

## Slide 8: Example <x>SS
What does type D do/have? :
  Single “802.1Q Bridged Network”
    That is:
    Same subnet
      There may be multiple subnets, but a given client sees a consistent subnet (or set of subnets it is using), as it moves around
    IP address(es) doesn’t change with ‘moving’ within <x>SS
  More than one DS
  Can’t reassociate across the DSs – check this in the spec
  May or may not have the same SSID
  Example: A house with two, unrelated APs (different vendor, for example), plugged into the same Ethernet switch, with the same SSID.
  Not a .11 concept, but a composite of separate .11 networks and a .1 concept

## Slide 9: Example <x>SS – “Mobility Domain”
What does type E do/have? :
  Single “802.1Q Bridged Network”
    That is:
    Same subnet
      There may be multiple subnets, but a given client sees a consistent subnet (or set of subnets it is using), as it moves around
    IP address(es) doesn’t change with ‘moving’ within <x>SS
  One DS
  Can reassociate
  Can FT
  Must have same MDID
  Must have same SSID

## Slide 10: Example <x>SS
What does type F do/have? :
  Same/consistent layer 2 security parameters
    “Coincidentally same security”
    Planned/assured same security
  Same SSID
  Not same 802.1Q Bridged network
  Not a useful concept in this discussion, just coincidental (sharing of same “phone profile”)
  BUT, distinguishing between F and D is important

## Slide 11: Example <x>SS
What does type G do/have? :
  Same Operating authorization domain
  (different, alternate concept:) Same operating master (e.g., DFS master, TVWS enabler, etc.)
  Not an <x>SS concept, but important as something else, related to regulatory domain knowledge/information PLUS enablement under that domain

## Slide 12: Summary/status (Sept 2018)
Type A is ESS, or we should modify ESS definition until it matches within the 802.11 spec
Type B is HESS, or we should modify (create) HESS definition until it matches within the 802.11 spec. (Note, we may extend into coordinating the concept with outside groups (WFA) that have similar concepts/use our facilities)
Type C is unclear – is this different from Type B?
Type D is covered by 802.1 Standards – no work to do
Type E is covered by “Mobility Domain”. We should double-check that it matches within the 802.11 spec
Type F is not useful, just coincidental - BUT, distinguishing between F and D is important
Type G is not in scope – it is some sort of enablement concept
Do we agree to all the above? Is anything missing?

## Slide 13: Proposed Way forward (Jan 2020)
Type A:
  Compare our key concepts to 802.11’s “ESS” and propose any changes we think will clarify/correct/complete the definition and description.
Type B:
  Compare our key concepts to 802.11’s “HESS” and propose any changes we think will clarify/correct/complete the definition and description.
  Note, we may extend into coordinating the concept with outside groups (WFA) that have similar concepts/use our facilities.
Type C:
  Drop it as beyond 802.11’s scope, other than the HESS concept.
Type D:
  Discuss in clause 4, as an 802.1 concept, beyond 802.11 facilities
Type E:
  Confirm is covered and correct in 802.11’s “Mobility domain”
Type F:
  Not really a useful concept, but make distinction from Type D in clause 4 discussion.
Type G:
  Not a type of “<x>ESS”, so not in scope at this point.

## Slide 14: Way forward (Jan 2020) – Type A
Type A key concepts:
  Single “802.1Q Bridged Network” (same subnet, IP address, location transparency)
  One DS (can reassociate)
  Must have same SSID (careful!) (REVmd 4.3.5.2)
REVmd definition:
  “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
REVmd 4.3.5.2:
  “An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS. The ESS does not include the DS.”
  “The key concept is that the ESS appears the same to an LLC layer as an IBSS.”

## Slide 15: Way forward (Jan 2020) – Type A (cont)
Recommendations:
  Modify the definition of ESS:
    From:
      “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
    To:
      “A set of one or more basic service sets (BSSs), with the same SSID, that are interconnected by a single distribution system (DS), which makes the set of BSSs appear to be a single IEEE 802 access domain to the LLC sublayer. that appears as a single 802.1Q Bridged Network to any station (STA) associated with one of those BSSs, or to any device connecting via the portal, if one is present.
      NOTE—For correct operation all APs in an ESS advertise the same SSID.”
      NOTE--<something about GLK not being one of these>
  Add to subclause 4.3 some discussion of the association, as the relationship between a non-AP STA and the DS (via its particular “associated AP” at any point in time). Also discuss the concept of reassociation where the DS association is maintained across AP to AP transition within the ESS. (See next slide.)

## Slide 16: Way forward (Jan 2020) – Type A (cont)
Recommendations:
  Modify the definition of ESS:
    From:
      “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
    To:
      “A set of one or more basic service sets (BSSs) that are interconnected by a single distribution system (DS); an ESS appears as a single IEEE Std 802™ access domain to the logical link control (LLC) sublayer.
  Add to subclause 4.3 some discussion of the association, as the relationship between a non-AP STA and the DS (via its particular “associated AP” at any point in time). Also discuss the concept of reassociation where the DS association is maintained across AP to AP transition within the ESS. (See next slide.)

## Slide 17: Way forward (Jan 2020) – Type A (cont)
Recommendations:
  Original text in 4.3.5.1 (the “Overview” subclause of the “DS concepts” subclause):
    “The DS enables mobile device support by providing the logical services necessary to handle address to destination mapping and seamless integration of multiple BSSs.
      An access point (AP) is any entity that has STA functionality and a distribution system access function (DSAF), which enables access to the DS, via the WM for associated STAs.”
  Change to:
    “The DS enables mobile device support by providing the logical services necessary to handle address to destination mapping and seamless integration of multiple BSSs.
      An access point (AP) is any entity that has STA functionality and a distribution system access function (DSAF), which enables access to the DS, via the WM for associated STAs. To invoke this access, a non-AP STA joins a BSS and associates to the AP operating that BSS. This causes the AP to notify the DS of the non-AP STA’s location within the network. The non-AP STA moves to another BSS operated by an AP connected to the same DS in another location by reassociating to this new AP. The new AP updates the DS with the non-AP STA’s new location at the completion of the reassociation.
      The STA’s location information is internal to the DS, thus STA mobility is transparent to upper layers. See 4.3.5.2 (Extended service set (ESS): the large coverage network). ”

## Slide 18: Way forward (Jan 2020) – Type A (cont)
Update Clause 4.3.5.2 (“Extended service set (ESS): the large coverage network”):
  Original text:
    “The DS and infrastructure BSSs allow IEEE Std 802.11 to create a wireless network of arbitrary size and complexity. IEEE Std 802.11 refers to this type of network as the ESS. An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS. The ESS does not include the DS.
    The key concept is that the ESS appears the same to an LLC layer as an IBSS. STAs within an ESS can communicate and mobile STAs might move from one BSS to another (within the same ESS) transparently to LLC.”
  Change to:
    “The DS and infrastructure BSSs allow IEEE Std 802.11 to create a wireless network of arbitrary size and complexity. IEEE Std 802.11 refers to this type of network as the ESS. An ESS is the union of the infrastructure BSSs with the same SSID connected by a single DS. All BSSs in an ESS have the same SSID. The ESS does not include the DS.
    The key concept is that the ESS appears to be a single IEEE STD 802™ access domain to the LLC sublayer the same to an LLC layer as an IBSS. STAs within an ESS can communicate and mobile STAs might move from one BSS to another (within the same ESS) transparently to the LLC sublayer.”
Do we need to say security is the same across the ESS, or is that not required?

## Slide 19: Way forward (Jan 2020) – Type B
Type B key concepts:
  Access to the same authentication domain (RADIUS) – same database (the same authentication server)
    Identified by (the WFA’s) HESSID – Is WFA’s HESSID different?
  Access to the same SSPN (802.11u)?? -- Need to settle this
  No assumption that there is a single SSID -- Do we agree this?
REVmd definition:
  “A collection of basic service sets (BSSs), which may or may not be within the same extended service set (ESS), in which every subscription service provider network (SSPN) or other external network reachable at one BSS is reachable at all of them.”
REVmd discussion (11.33.2):
  In an infrastructure BSS, the Interworking element contains signaling for Homogeneous ESSs. The HESSID is a 6-octet MAC address that identifies the homogeneous ESS. The HESSID value shall be identical to one of the BSSIDs in the homogeneous ESS. Thus, it is a globally unique identifier that, in conjunction with the SSID, may be used to provide network identification for an SSPN.

## Slide 20: Way forward (Jan 2020) – Type B (cont)
Recommendations (and questions):
Suggest changes to definition to discuss access to RADIUS?
Add discussion of HESS concepts in subclause 4.3
Should those changes talk about access to and thereby to SSPN, via the RADIUS access? (Or, changes in 11.23 to expand on this?)
Both 802.11 and WFA definitions talk about the fact that the same SSID is not sufficient to know this is the same “wireless network”
  Need to define what we mean by “wireless network”?
  Should we have a mention that different SSIDs might access the same “wireless network”? Do we agree with that statement?
Any changes we make here should be liaised to WFA, so they are aware, and can make parallel changes (or argue with us).
  Related: Are WFA definitions still different from 802.11’s? (They have made some wording changes/clarifications since that claim was made.)
Anything about CAG, through here?
Is the domain for Reassociation (and upper-layer mobility transparency) the domain that has the same SSID (and same HESSID)?
Is the domain for “same hotspot” (“local”) the domain that has the same HESSID, regardless of SSID?
Is there a domain for “hotspot from my [home] provider” (worldwide)? This is really a question about roaming access (and roaming consortium, too).

## Slide 21: Way forward (Jan 2020) – Types D & F
Type D key concepts:
  Single “802.1Q Bridged Network”
  More than one DS
Recommendation:
  Add discussion in subclause 4.3 that notes that if there is not a shared DS, then reassociation (and “seamless roaming”) concepts may not work.
  However, it could still be a single 802.1 Bridged Network, so other aspects, like same IP address, and location transparency will still apply This should be mentioned in subclause 4.3, also.
Type F key concepts:
  “Coincidentally” (or planned) same/consistent layer 2 security parameters
  Same SSID
  But, not same 802.1Q Bridged network
Recommendation:
  Note these distinctions in subclause 4.3, also: Same SSID and/or same security access are not sufficient to imply same 802.1Q Bridged network

## Slide 22: Way forward (Jan 2020) – Types D & F (cont)
Following the paragraphs changed (on previous slides) in 4.3.5.2, add a paragraph:
“The key concept is that the ESS appears to be a single access domain to the LLC sublayer. STAs within an ESS can communicate and mobile STAs might move from one BSS to another (within the same ESS) transparently to the LLC sublayer.
For completeness of understanding, it is important to note that if multiple BSSs are configured with the same SSID, but the APs are not interconnected by a common DS, there is no guarantee of seamless mobility for STAs between those BSSs. However, such a deployment may have a common LLC sublayer interconnection, in which case, communication with location transparency to the LLC sublayer (a single access domain) is generally still possible, but such communication could be disrupted at times when a mobile STA moves between BSSs. [A mobile STA implementation needs to take this possible configuration into account.]”

## Slide 23: Way forward (Jan 2020) – General
Related, but separate:
Recommendation?
  Remove 802.2 (LLC) discussion, and substitute in 802.1 concepts (802.1Q, etc.)?
Upon further review, the only references to 802.2 are unrelated to this discussion. One in a NOTE in 7.2.3.2.4, suggesting that DS updates could be implemented with 802.2 XID null frames. And there are two references in a NOTE in 9.4.2.153 that LLC headers are defined in 802.2, for understanding the concept of LLC Header removal.
Neither of these are related to architecture discussions, so there are no “bad/old” architecture references to 802.2 anymore.

## Slide 24: Background/old discussion slides (scrub these for other/minor proposed changes to spec)

## Slide 25: What is an ESS?
Current definition depends on the relationship to LLC
  “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
That would mean a 802.1 Bridged LAN (for example) creates an ESS. Probably not what we (802.11) meant.
We probably meant something about transparency of “location of attachment”/”mobility”, from whatever is using the 802.11 MAC
  and other entities, necessary to accomplish this? ESS == demarcation of this transparency??
Is it:
  Transparent to whatever upper layer is above 802.11?
  Includes entities beyond (above?) 802.11? (Like bridges in the 11ak scenario?)
  The APs have to have some common/similar configuration settings? (SSID, at least. Probably other facilities (security, etc.) and policies?)
Changes to Figure 4-1: ‘BSS’s are just STAs. These ovals are BSAs. Also, should we be saying “OBSA”?

## Slide 26: What is an ESS? (Continued)
Current definition depends on the relationship to LLC
  “A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.”
We probably meant something about transparency of “location of attachment”/”mobility”, from whatever is using the 802.11 MAC 802 Services
  includes other entities, necessary to accomplish this? (EAP Auth Service? Bridges (11ak)? ANQP, etc?) ESS boundary == demarcation of this transparency?? Yes, + common domain of “mobility” that works, including security, policy, etc., necessary for mobility that actually works.
Is it:
  Transparent to whatever upper layer is above 802.11? No, boundary may be higher than that
  Includes entities beyond (above?) 802.11? (Like bridges in the 11ak scenario?) Yes, as needed
  The APs have to have some common/similar configuration settings? (SSID, at least. Probably other facilities (security, etc.) and policies?) Yes.
Changes to Figure 4-1: ‘BSS’s are just STAs. These ovals are BSAs. Also, should we be saying “OBSA”?

## Slide 27: What is an ESS? – Direction?
Straw proposal - ESS is: [Edit this list, per discussion]
Set of one of more basic services sets (BSSs)
Appears as a single logical network, to layers above the ESS boundary
The boundary might be above 802 (above Layer 2), or might be within Layer 2 (the MAC SAP, etc.)
The boundary must exist/be clear for participating end stations (see 802 O&A), and external devices that can interwork with the participating end stations
Provides transparency of “location of attachment” / “mobility”, as seen by layers above the ESS boundary, on both participating end stations and external end stations.
Includes all entities necessary to provide the services and transparency required.
Has a common domain of mobility and a common security and policies and configuration necessary to deliver the transparency from mobility.

## Slide 28: ESS and HESS?
What is an HESS (from the term “HESSID”)?
“Homogenous [sic] extended service set (ESS)”
Is an HESS a type of ESS, or a separate (perhaps similar) concept?
MSGCF has an “ESSIdentifier”, which is the concatenation of SSID and HESSID. Why/when do we need both?
Is this related to an SSPN? No not really – the SSPN is independent of any HESSID assignment. SSPN is a destination where I am being taken to. See Figure R-2.
(Also, in figure R-2 and Figure 4-8, the AAA server/client look to be in the data path – this doesn’t make sense. Ans, why are the BSSs not labeled BSSs?)

## Slide 29: HESS concepts (not necessarily what 802.11 says, now)
HESS purpose is to support 802.21 and/or WFA Passpoint/Hotspot 2.0
HESS is either/both consistent authentication, or equivalent access to “external things”
HESS is identifiable by HESSID, which is globally unique (MAC Address); identifies the SP (but perhaps not one-to-one)
HESS can/cannot span different ESSs or SSIDs
  Corollary: Which (if either) of these is related to 802.11 handoff?
Homogenous is misspelled ; HESS should be introduced as a term/concept
Discuss off-line with WFA experts, 802.21 experts…

## Slide 30: Themes in types
Example | 802.1Q Bridged Network | One DS/ Reassociate | FT | Same RADIUS/SSPN
A | Yes | Yes | Maybe | ??
B | Maybe | Maybe | Maybe | Yes
C | ?? | ?? | ?? | “Same Accounting” – same thing, or different?
D | Yes | No | No | ??
E | Yes | Yes | Yes | ??
F | ?? | ?/ | ?? | “Same security” – same thing or different?
G | ?? | ?? | ?? | Some other scope, really
In the following slides, Bold text identifies the defining attributes

## Slide 31: Needed concepts (not necessarily what 802.11 says, now)
Looked at WFA’s Deployment Guidelines:
  “In typical Wi-Fi deployments, if two APs have different SSIDs, they are considered to be different wireless networks. If two APs have the same SSID, they are considered to be part of the same wireless network. But because SSIDs are not globally administered, it is possible that two APs with the same SSID are, in fact, in different wireless networks. The homogeneous extended service set identifier (HESSID) element allows mobile devices to detect this condition. When two APs have the same SSID but from different wireless networks, the two networks have different HESSIDs.”
  What is “wireless network” in this context?
Concepts we need:
  Domain for Reassociation (and upper-layer mobility transparency)
  Domain for “same hotspot” (“local”)
  Domain for “hotspot from my [home] provider” (worldwide)
  Domain that uses the same security
  Equivalent access to “external things” (SSPN?) (CAG?)

## Slide 32: HESS concepts (not necessarily what 802.11 says, now)
Homogeneous ESS attributes (should be):
  => Must have a globally unique identifier
  Set of BSSs
  Mobility transparency to upper layers (one DS, Reassociate)
  => Same HESSID
  => SSID is the same
  => all available/reachable services are the same
  => reachable SSPN(s) are the same, if present
It’s not:

## Slide 33: (Background) Analysis of the 7 types
July 2019, more detailed analysis types A and E, and other concepts that need to be discussed, on the following slides (26 – 30).

## Slide 34: Type A analysis (“ESS”) – page 1
Single “802.1Q Bridged Network”
  That is:
  Same subnet
    There may be multiple subnets, but a given client sees a consistent subnet (or set of subnets it is using), as it moves around
  IP address(es) doesn’t change with ‘moving’ within <x>SS
  Transparency of location (“appears as a single BSS to UL”)
Current ESS definition (REVmd) is:
  extended service set (ESS): A set of one or more interconnected basic service sets (BSSs) that appears as a single BSS to the logical link control (LLC) layer at any station (STA) associated with one of those BSSs.
Conclusion:
  “appears as a single BSS to the LLC layer” ✓
  “to … any STA associated” ☹ (Needs “Portal”)

## Slide 35: Type A analysis (“ESS”) – page 2
One DS
  Mechanism for accomplishing the above, not a property
  (But, implies and is implied by, a single Portal (or none), to accomplish the above)
Must have same SSID (careful!)
  REVmd 4.3.5.2: “An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS. The ESS does not include the DS”
  WFA Deployment Guidelines: “If two APs have the same SSID they are considered to be part of the same wireless network. But, because SSIDs are not globally administered it is possible that two APs with the same SSID are in fact in different wireless networks.”
  Recommendation: Add clarification, somewhat like WFA’s comments, to 4.3.5.2, to discuss the “coincidentally the same” SSID scenario. Perhaps a hint that clients need to handle this?
  Conclusion: Client can’t (for sure) detect an ESS, but standard can discuss how it behaves. What does this mean for the requirements (“An ESS shall …”)

## Slide 36: Type A analysis (“ESS”) – page 3
Can Reassociate
  Just mechanism? (Does this add anything new?)
Can’t necessarily FT between all APs (more than one “mobility domain”) (and not just because equipment is not capable/configured, but due to ‘real’ barriers such as distance)
  Conclusion: Mobility domain is useful, and is independent of ESS, but must be a subset of an ESS. Covered as Type E.

## Slide 37: Type E analysis (“Mobility Domain”)
Same properties as Type A, plus:
  Can FT
  Must have same MDID
REVmd, subclause 3.1:
  mobility domain: A set of basic service sets (BSSs), within the same extended service set (ESS), that support fast BSS transitions between themselves and that are identified by the set’s mobility domain identifier (MDID).
Conclusion:
  Definition seems to cover it (assuming “ESS” is understood

## Slide 38: Remaining concepts analysis
Type B (“HESS”?)
Type C?
Distinction between Type D and Type F, and either needed?
More HESS discussion
Concepts we need:
  Domain for Reassociation (and upper-layer mobility transparency)
  Domain for “same hotspot” (“local”)
  Domain for “hotspot from my [home] provider” (worldwide)
  Domain that uses the same security
  Equivalent access to “external things” (SSPN?) (CAG?)