## Slide 1: Reason Why L2 Per Frame Authentication Is Required
Date: 2018-06-18
Authors:

## Slide 2: Abstract
This presentation describes the reason why L2 per frame authentication is required for BCS.

## Slide 3: System Structure Assumption
STA
STA
STA
AP
Internet
Server
IP Multicast
IEEE802.11
Multicast
STA selects information by ID of information (e.g. SSID)
STA
AP
Server
Router
Simplify

## Slide 4: Case 1: No Authentication
If no authentications are provided, a malicious user can make a fake AP easily by spoofing AP’s MAC address and Information ID.
Rogue AP can do the following attacks.
  DoS attack by injecting invalid frames to the stream
  Distributing fake information
STA
AP
Server
Router
Rogue AP
Spoofing
MAC address and
Information ID

## Slide 5: Case 2: Existing GTKSA
The existing GTKSA provides per frame authentication and encryption to the multicast frames.
The GTKSA uses symmetric algorithm.
A malicious user who can join the GTKSA can make a fake AP.
The existing GTKSA is not suitable for public use.
STA
AP
Server
Router
Rogue AP
Spoofing
MAC address and
Information ID

## Slide 6: Case 3: Application Layer Per Packet Authentication (No Fragmentation)
The server generates private/public key pair.
The CA signs the server’s public key.
The server distributes the public key to STAs with CA signature.
The STAs verify the server’s public key by preinstalled CA’s public key.
The server signs each packet by the private key.
The STAs can verify each packet by the public key.
If the packets are never fragmented by the router on the path, it will work well.
STA
AP
Server
Router
Private Key
Public Key
Sign
Data
Sign
Data
Sign
Data
Sign
Data
Sign
Data
Sign
Data
Preinstalled
CA Public Key
Sign by CA
Verify
Verify
Sign

## Slide 7: Case 4: Application Layer Per Packet Authentication (With Fragmentation)
Same as Case 3 except the router fragments packets.
If an invalid frame is injected between fragmented packets, the STA will fail to verify and discard whole packet.
Malicious user can cause DoS attack by injecting an invalid frame between fragmented packets.
For unicast, the server can avoid fragmentation by performing path MTU discovery and use DF flag.
For multicast, the server cannot perform path MTU discovery and the routers never returns ICMP “fragmentation required” message even if the packet size exceeds MTU. (IPv4)
STA
AP
Server
Router
Sign
Data
Sign
Data
Data
Sign
Data
Data
Invalid
Malicious
Sign
Data
Data
Invalid
Private Key
Public Key

## Slide 8: Case 5: L2 Per Frame Authentication
The AP generates private/public key pair.
The AP distributes the public key to STAs.
The AP signs each frame by the private key.
The STA can verify each frame by the public key.
The STA can detect invalid frames and discard them.
Of course, it can be used with application layer authentication.
STA
AP
Server
Router
Data
Data
Data
Invalid
Malicious
Data
Data
Sign
Sign
Private Key
Public Key