## Slide 1: Discussion on WUR FDMA Padding Issues
Date: 2018-07-10
Authors:

## Slide 2: Introduction
In May meeting, the concept of padding for WUR FDMA mode passes the motion [1].
Padding is only required on primary 20MHz sub-channel to align with the sub-channel with the longest duration.
LSIG LENGTH field signals the packet length of primary 20MHz sub-channel.
In this contribution, we discuss the potential coexistence issue of this padding scheme with legacy WiFi devices.

## Slide 3: Recap: WUR FDMA Padding [1]
The transmission on WUR primary 20MHz channel is equal to or longer than transmissions on other channels in WUR FDMA transmission.
If needed, the Padding is used to ensure that transmissions on the WUR primary channel always have the length indicated by L-length field in L-SIG.

## Slide 4: Coexistence Issues: OBSS
LSIG LENGTH field signals the duration of PPDU.
OBSS device only listens to the its own primary 20MHz channel, which can be a different channel from the BSS.
In current WiFi market, there are some devices that do NOT fully honor the CCA rule for LSIG LENGTH:
  If STA detects significant energy drop by xdB during reception, the Rx state machine will abort and reset CCA.
If the WUR FDMA packet does not align the energy on all 20MHz sub-channels, the listening STA will observe big energy drop in WUR portion, ~6dB for 80MHz.
The listening OBSS device may start transmission, and will collide with ongoing WUR packet.

## Slide 5: Example
OBSS primary channel lies on the secondary 20MHz of the BSS
OBSS STA1 received power is <-72dBm on all 20MHz, but is able to decode WUR LSIG.
OBSS STA1 can start 80MHz packet transmission and collide with WUR packet
BSS
OBSS
OBSS STA1
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
Legacy
Preamble
BPSK Mark
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
WUR-Sync
WUR-Data
BSS Primary
20MHz
Secondary
20MHz
Secondary
40MHz-1
OBSS Primary 20MHz
WUR
AIFS+backoff
Collision to STA2 WUR reception !
BSS STA1
STA1: 80MHz .11 packet

## Slide 6: Coexistence Issues: BSS
For STAs within the BSS, similar coexistence issue can also happen.
The listening STAs may constantly monitor the incoming packet power within its device bandwidth.
  Even the STA correctly decodes the LENGTH on the primary 20MHz channel.
  If AGC detects power drop by xdB during reception, the Rx state machine may abort and reset CCA
For WUR FDMA packets that do not align the energy on all 20MHz sub-channels, the listening BSS STA may start transmission during the WUR packet, and cause collision.

## Slide 7: Potential Solutions
Option 1: Pad all 20Mhz sub-channels to the same length.
  The length equals the longest duration among all 20MHz sub-channels.
  No extra cost for implementation.
Option 2: equal rate/format FDMA mode
  Limit FDMA to basic-mode-only operating AP, and allow only equal rate across 20MHz subchannels.
  No padding is needed.
  “basic mode” means WUR with 6 bytes payload and no frame body.
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
Legacy
Preamble
BPSK Mark
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
Legacy
Preamble
BPSK Mark
WUR-Sync
WUR-Data
WUR-Sync
WUR-Data
Primary
20MHz
Secondary
20MHz
Secondary
40MHz
WUR-Padding
WUR-Padding
WUR-Padding

## Slide 8: Summary
In WUR FDMA mode, primary-20MHz-only padding is proposed in the previous meeting [1].
In current WiFi market, some devices do NOT fully comply with the CCA rule based on LSIG LENGTH.
OBSS/BSS devices that observes low reception energy of the BSS WUR packet may start wide-bandwidth transmission and cause coexistence issues.
Propose two solutions:
  Option 1: Pad all 20MHz sub-channel to equal length
  Option 2: Restrict FDMA to be used in basic mode and equal rate across 20MHz sub channels.
Avoid unintentional collision without cost.

## Slide 9: References
[1] Dongguk and etc., 11-18-0762-04-00ba-efficient-wur-fdma-transmission
[2] Jianhan Liu and etc, 11-17-1625-06-00ba-efficient-fdma-transmission-schemes-for-wur-wlan

## Slide 10: Straw Poll
Do you agree to change the FDMA padding as the following:
  Option 1: Pad all 20MHz subchannels to the same length
  Option 2: Limit FDMA to basic-mode-operating AP only, allow only equal rate across all 20MHz subchannels
  No
  Abstain

## Slide 11: Straw Poll (PHY Ad Hoc)
Do you agree to change the FDMA padding as the following:
  Option 1: Pad all 20MHz subchannels to the same length
  Option 2: Limit FDMA to basic-mode-operating AP only, allow only equal rate across all 20MHz subchannels
  No:
  Abstain
  Option 1: 2
  Option 2: 5
  No: 2
  Abstain: 2