## Slide 1: HEz Ranging Availability Window
Date: 2018-07-09
Authors:

## Slide 2: Motivation/Background
Submission 18-855r1 discussed the notion of Availability Window for HEz Ranging
In this presentation, we propose a structure to represent the Availability Window and describe the mechanism to assign a Ranging Availability Window to an ISTA in order to execute HEz Ranging Exchange.

## Slide 3: Ranging Availability Window Assignment
ISTA includes a Availability/Unavailability bit mask element in IFTMR
RSTA assigns an Availability Window that best fits its operating conditions and the Availability/Unavailability bit mask of the ISTA to the ISTA and includes the assigned Availability Window in IFTM
TBD – how does RSTA communicate Ranging Availability Window change(s)?

## Slide 4: HEz Specific Subelement
Fields included in IFTMR frames
  Unavailability element describing ISTA’s Unavailability (Availability)
Fields included in IFTM frame when Status is Successful:
  Ranging ID
    Ranging ID assigned to the initiator (463r1) – only to unassociated STA; Associated STAs use AID instead of Ranging ID.
  Response: Immediate or Delayed
  MaxToAAvailableExp
  BSS Color*
  Ranging Window (Availability Window element)
    Ranging Window assigned to the ISTA for executing the HEz Ranging exchange
Fields included in IFTM frame when Status is not Successful:
  RSTA’s Availability Window for Ranging IE – needs discussion
* Note that IFTMR/IFTM are public access frames and hence are not colored

## Slide 5: Ranging Availability Window Element
 | Partial TSF | Duration | Reserved | Periodicity
bits | 16 | 6 | 2 | 8
 | Element ID (255) | Length (4n+2) | Extended Element ID | Count | Availability Window-1 | … | Availability Window-n
Octets | 1 | 1 | 1 | 1 | 4 | .. | 4
Availability Window Information
Ranging Availability Window IE

## Slide 6: Availability Window Information
Defined as <Partial TSF, Duration, Periodicity>
  Partial TSF (Same as in IEEE802.11-2016, See next slide)
  Duration
    In 100 usec units
    6-bit field describing how long the Availability Window is
    Range 100 usec to 6.4 msec
  Periodicity
    # of beacon intervals
    Size is 1 octet
    E.g. 3 indicates the window occurs once in three beacons
    Range 1 to 255 Beacons (100ms – 25.5s)

## Slide 7: Partial TSF
Truncated TSF value
As defined in IEEE802.11-2016 (Cl. 9.4.2.166 Fine Timing Measurement Parameters element)
  2 octets wide (bits 25:10 of TSF)
  The Partial TSF Timer value is derived as follows, so as to have units of TUs: from the 64 TSF timer bits at the start of the first burst instance of an FTM session, where the 10 least significant bits equal 0, remove the most significant 38 bits and the least significant 10 bits.
Reference for the Partial TSF
  Partial TSF along with Periodicity is an offset to the TSF in the most recent Beacon (after accounting for Periodicity) transmitted by the RSTA
  If included in a Probe Response, the Partial TSF along with Periodicity is an offset to the TSF (after accounting for Periodicity) in the Probe Response
    Note that the Partial TSF value is adjusted appropriately to match the elapsed time in Tus between the last transmitted Beacon and the TSF in the Probe Response

## Slide 8: Ranging Unavailability Element
Example:
  Count: number of bits in the Unavailability field (bit pattern)
    12`
  Unavailability field (bit pattern)
    1110000000111
 | Element ID (255) | Length | Extended Element ID | Count | Reserved | Unavailability | … | Unavailability
Bits | 8 | 8 | 8 | 9 | 7 | 1 | .. | 1
0 – 10 ms : Unavailable
10 – 20 ms : Unavailable
20 – 30 ms : Unavailable
30 – 40 ms : Available
40 – 50 ms : Available
50 – 60ms : Available
60 – 70 ms : Available
70 – 80 ms : Available
80 – 90 ms : Available
90 – 100 ms : Available
100 – 110 ms : Available
110 – 120 ms : Unavailable
120 – 130 ms : Unavailable
130 – 140 ms : Unavailable

## Slide 9: Ranging Unavailability Element
Implies periodicity requested by ISTA
  e.g., 1110000000111 => periodicity of 140 TUs.
  Expects to be polled once per period
  ISTA has the option to respond/not respond
Length: ceil(Count/8) + 2
Granularity is fixed at 10 TUs
Count (number of bits in the Unavailability bits): Availability: 1 Unavailable, 0 Available
Reference to the Unavailability field
  TSF Synchronized to the start of the next Beacon of the corresponding RSTA

## Slide 10: Straw Poll
We support the proposed Ranging Availability Window assignment procedure described in this submission
  ISTA describes its Unavailability/Availability using a bit pattern (in IFTMR) that is synchronized to the RSTA’s TSF (based on the last received Beacon from the RSTA or other means)
  RSTA assigns a matching Ranging Availability Window and returns it in IFTM
  ISTA becomes ‘available’ and listens to the RSTA’s Trigger (Location Poll) at the start of the Ranging Availability Window in order to execute the HEz Ranging protocol with the RSTA
Y: 13, N: 0, Abstain:0

## Slide 11: Motion
Move to approve the following exchange for a RSTA to assign a Ranging Availability Window to an ISTA:
  ISTA describes its Unavailability/Availability using a bit pattern (in IFTMR) that is synchronized to the RSTA’s TSF (based on the last received Beacon from the RSTA or other means)
  RSTA assigns a matching Ranging Availability Window and returns it in the corresponding IFTM
  ISTA becomes ‘available’ and listens to the RSTA’s Trigger (Location Poll) at the start of the Ranging Availability Window in order to execute the HEz Ranging protocol with the RSTA
Mover:
Seconder:
Result:11/0/1

## Slide 12: Opens
Need to define a minimum pattern size for the Unavailability bit pattern
Need to also consider if the bit pattern implies a ISTA proposed periodicity
  Note that the assigned Ranging Availability Window may have a shorter periodicity. In such cases the periodicity implied by the ISTA’s bit pattern indicates how often the ISTA may be expected to respond to Trigger (location poll) when the Ranging Availability Window opens.