## Slide 1: WUR PSD studies
Date: 2018-07-09
Authors:

## Slide 2: Introduction
Strong spectral lines were observed in WUR power spectral density [1]
  Transmit power in 3 KHz subband exceeds the specified FCC limits
In this presentation, we study different approaches to address this issue

## Slide 3: PSD of the WUR Transmit signal
PSD computed on WUR packet comprising of Sync sequence and 1000 data bits
  Strong spectral lines with spacing proportional to Manchester symbol rate
  Issue: When AP transmits with Max TX power of 30 dBm, the max Tx power in 3 KHz subband is 14.4 dBm
    Larger than the 8 dBm FCC limit in 3 KHz subband

## Slide 4: Spectral lines in the PSD
Reason for spectral lines in the WUR PSD
  Manchester coding and OOK signaling
  Same OOK pulse transmitted on air for all ON Manchester data bits/preamble bits
Methods to mitigate spectral lines
  Transmit different OOK pulse on air for different ON Manchester data bits/preamble bits
    Random phase approach [1]
      Apply random phase +1/-1 to the OOK pulse
    Random cyclic delay (shift) approach
      Apply different (random) amount of cyclic shift to the OOK pulses for different ON manchester data bits/preamble bits
    Receiver performance not impacted by applying random cyclic shift or random phase
      Energy detector: sum (abs(.)^2) of RX samples
      Envelope detector: sum(abs(.)) of RX samples
      These two metrics remain same with or without phase/cyclic shift

## Slide 5: WUR PSD with random phase approach
No strong spectral lines
When AP transmits with Max TX power of 30 dBm, the max Tx power in 3 KHz subband is 2.52 dBm (High rate) and 3.79 dBm (Low rate)
  Below the 8 dBm FFC limit

## Slide 6: WUR PSD with random cyclic shift approach
No strong spectral lines
When AP transmits with Max TX power of 30 dBm, the max Tx power in 3 KHz subband is 1.42 dBm (High rate) and 3.09 dBm (Low rate)
  Below the 8 dBm FFC limit

## Slide 7: Random cyclic shift approach
A random cyclic shift is applied to the OOK pulse transmitted for ON Manchester bits/preamble bits
  One way to realize this is to use a fixed length, predetermined cyclic shift sequence
  This sequence is known at the transmitter, but appear random to the current generation wakeup receiver
    More advanced receivers can regenerate the sequence, and can perform coherent detection
  Length of sequence can be smaller than total ON bits
    Repeat the cyclic shift sequence
    Larger the length, smaller the spacing between spectral lines in PSD
    Larger the length, smaller the magnitude of spectral lines

## Slide 8: WUR PSD with fixed length cyclic shift seq (Length = 16)
When AP transmits with Max TX power of 30 dBm, the max Tx power in 3 KHz subband is 6.40 dBm (High rate) and 7.52 dBm (Low rate)
  Below the 8 dBm FFC limit

## Slide 9: With fixed length cyclic shift sequence
Sequence length | Max Tx power in 3 KHz subband (Low Data Rate) | Max Tx power in 3 KHz subband (High Data Rate)
8 | 9.26 dBm | 7.65 dBm
16 | 7.52 dBm | 6.40 dBm
32 | 6.68 dBm | 5.75 dBm
64 | 5.77 dBm | 3.40 dBm
128 | 4.98 dBm | 1.43 dBm
As sequence length increases, the magnitude of spectral lines decreases
  16 length sequence is sufficient enough to meet the FCC regulations
Results generated for packet size of 1000 bits
  Smaller length sequences might be sufficient for small packet sizes

## Slide 10: Summary
Noticed spectral lines in WUR transmit signal
  Tx power exceeds FCC limits in certain regulatory domains
Studied two different approaches to mitigate this
  Random phase approach proposed earlier by Qualcomm
  Random cyclic shift approach
  Both are effective in mitigating the spectral lines

## Slide 11: Straw Poll
Do you support the method of random cyclic shift to mitigate the issue with spectral lines?
  Yes/No/Abstain

## Slide 12: References
[1] Steve Shellhammer, Bin Tian, Richard van Nee, “WUR Power Spectral Density, IEEE 802.11-18/0824r1,” May 2018