## Slide 1: Enabling WUR Protection
Date: 2018-07-04
Authors:

## Slide 2: Introduction
As per [1] WUR AP may optionally transmit protected WUR frames:
  to a WUR STA that has set the Protection Supported field in the WUR Capabilities element it transmits to 1.
Reception of Protected WUR frames will likely drain more battery as compared to reception of unprotected WUR frames, so from WUR STAs’ perspective it is better if protection of WUR frames is enabled only when required.
In this contribution we discuss some options related to enabling Protected WUR frame transmission.

## Slide 3: Enabling Protection
When should WUR AP enable protection of WUR frames?
  Protection can be enabled as a BSS policy ( WUR service in a BSS is either always protected or always unprotected).
    May not be good for WUR STA’s power consumption
    Not all WUR STAs support Protection
    Not responsive to changes in environment
  Or, protection is enabled only when deemed necessary:
    May be better for WUR STA’s power consumption
    More responsive to changes in environment
    Option 1: Upon request by WUR STAs:
      When a WUR STA detects “Attack”
    Option 2: AP/System makes the decision:
      May require collection of reports of “Attack” from WUR STAs.
For operation flexibility and WUR STA power saving, protection should be enabled only when required.

## Slide 4: Attack Detection
How does a WUR STA detect that it is under “Attack”?
  1. WUR Wake-up frames
  A WUR STA may conclude that it has been falsely woken up after receiving a WUR wake-up frame if the expected PCR frame/s is not received from the WUR AP. The expected PCR frame/s may be:
    Buffered BUs (Wake-up frame for individually addressed delivery)
    Group addressed BUs (Wake-up frame for group address delivery)
    Beacon frame with changed parameters (Wake-up frame with different counter value)
    Trigger frame with RU assigned for UL (Wake-up frame for Triggered-enabled TWT)
  A WUR STA may also conclude that it has been falsely woken up if the WUR AP explicitly indicates that it does not have buffered BUs for the STA (e.g. upon reception of ACK or Qos-Null frame that has the “More Data subfield” in Frame Control set to 0, in response to the first PS-Poll frame or APSD Trigger frame transmitted after switching to PCR mode).
  2. WUR Beacons
  A WUR STA may conclude that a received WU Beacon frame has been forged if difference between the value of the P-TSF carried by the WUR Beacon and the corresponding bits of the local TSF exceeds the maximum expected drift.
How exactly a WUR STA detects “Attack” need not be specified.

## Slide 5: Proposal (1/2)
WUR STAs keep count of “Attacks”
  Separate counters for False wake up and forged WUR Beacon, or just a single counter
When the value of the “Attack” counter exceeds a specified threshold, WUR STA “informs” the WUR AP.
  Threshold may be a fixed value or a value informed by the AP
WUR AP may use the information to enable Protection for WUR frames.
  May also trigger integrity Keys generation and exchange as well as WUR Mode re-negotiation
  Example for False wake up attack:
Series of false wake-up attacks detected

## Slide 6: Proposal (2/2)
WUR STAs may “inform” WUR AP of “Attacks” in two ways:
  Option 1: Directly as a Request to enable Protection
    E.g. using a “Protection Request” bit in the WUR Mode element in Enter WUR Mode (Suspend) Request Action frames.
  Option 2: Indirectly as an event report
    E.g. reusing 802.11 Event Report element (9.4.2.68)
6 = WUR
WUR Event Type | Event Counter
0 (False Wake-up) | FalseWakeupCount
1 (False WUR Beacons) | FalseWURBeaconCount
Option 2 allows WUR APs to collect information from several WUR STAs before making the decision to enable Protection (especially for group address WUR frames)

## Slide 7: Summary
In this presentation we discussed options related to enabling Protected WUR frame transmission.
For operation flexibility and WUR STA power saving, we think that protection should be enabled only when required.
We proposed that:
  WUR STAs keep count of “Attacks”
  When the value of the “Attack” counter exceeds a specified threshold, WUR STA “informs” the WUR AP.

## Slide 8: Straw Poll 1
Do you agree that WUR STAs may “inform” WUR AP of false wake-ups?
6Y/2N/A

## Slide 9: Straw Poll 2
Which option do you prefer for WUR STAs to “inform” WUR AP of “Attacks”?
Option 1: Directly as a Request to enable Protection
  E.g. using a “Protection Request” bit in the WUR Mode element in Enter WUR Mode (Suspend) Request Action frames.
Option 2: Indirectly as an event report
  E.g. reusing 802.11 Event Report element (9.4.2.68)
Abstain

## Slide 10: References
[1] IEEE 802.11ba-D0.3