## Slide 1: Simulations with Recommended Symbols and CSD
Date: 2018-MM-DD
Authors:

## Slide 2: Introduction
At the May meeting the Task Group adopted Spec Text for the Single Channel MC-OOK On and Off Waveform Generators [1]
Earlier at the March meeting a number of PHY engineers agreed off-line [2] for “Up to three examples of coefficients will be provided in the standard,” however there was insufficient time at the meeting to hold a straw poll on that topic
Here we provide recommended subcarrier coefficients for the single channel 2 and 4 µs MC-OOK On Waveform Generators
Also a number of companies have made presentations on TX Diversity [3-6]
Here we also provide recommendation CSD Designs for TX Diversity
Spec Text documents for an Annex to include MC-OOK Symbol and CSD recommendations has also been prepared

## Slide 3: MC-OOK 2 µs On Waveform Generator Recommendations
Based on the text in [1] we recommend the following coefficients for the 13 subcarriers in the 64-pt IFFT for the 2 µs On Waveform Generator
Based on the text in [1] we recommend the following coefficients for the 13 subcarriers in the 64-pt IFFT for the 4 µs On Waveform Generator

## Slide 4: Recommended CSD Designs for Sync Field and HDR Data Field
Number of Transmit Antennas | CSD Values (ns)
1 | [0]
2 | [0, -1000]
3 | [0, -1000, -500]
4 | [0, -1000, -500, -1500]
5 | [0, -1000, -500, -1500, -750]
6 | [0, -1000, -500, -1500, -750, -1250]
7 | [0, -1000, -500, -1500, -750, -1250, -250]
8 | [0, -1000, -500, -1500, -750, -1250, -250, -1750]
We recommend the following CSD design for the Sync Field and High Data Rate (HDR) Data Field, both of which use 2 µs MC-OOK symbols

## Slide 5: Recommended CSD Designs for LDR Data Field
We recommend the following CSD design for the Low Data Rate (LDR) Data Field, which uses 4 µs MC-OOK symbols
Number of Transmit Antennas | CSD Values (ns)
1 | [0]
2 | [0, -2000]
3 | [0, -2000, -1000]
4 | [0, -2000, -1000, -3000]
5 | [0, -2000, -1000, -3000, -1500]
6 | [0, -2000, -1000, -3000, -1500, -2500]
7 | [0, -2000, -1000, -3000, -1500, -2500, -500]
8 | [0, -2000, -1000, -3000, -1500, -2500, -500, -3500]

## Slide 6: Simulations
We provide Simulation Results using our recommended 2 and 4 µs MC-OOK Symbols and our recommended CSD designs for up to 8 antennas

## Slide 7: HDR AWGN Sims

## Slide 8: LDR AWGN Sims

## Slide 9: HDR Model D Sims

## Slide 10: LDR Model D Sims

## Slide 11: Conclusions – MC-OOK On Symbols
Both the 2 and 4 µs MC-OOK On symbols have been selected for low PAPR
  2 µs On symbol – PAPR = 2.25
  4 µs On symbol – PAPR = 2.06
The results in AWGN and Model D for High Data Rate (HDR) and Low Data Rate (LDR) are both very good [7]
Both MC-OOK symbols have been show to work well with multiple CSD designs (linear CSD increase and binary tree CSD)
  This shows that the symbol designs are robust and not highly sensitive to the choice of CSD design

## Slide 12: Conclusions – Recommended CSD Design
The CSD design approach of Binary Tree selection of CSD values follows the legacy 802.11 CSD design approach
The CSD design recommended here provides the maximum frequency diversity by using high CSD values
Shown to have limited loss in AWGN [5]
  Less than 0.8 dB loss for HDR and 0.4 dB loss for LDR with up to eight antennas (@ 10% PER)
Shown to have excellent diversity gain in Channel Model D [5]
  Diversity gain of up to 2.5 to 3 dB for HDR and 3 to 4 dB for LDR for four to eight antennas (@ 10% PER)

## Slide 13: Final Conclusions
Motions for including these MC-OOK symbols and CSD designs have been including with the Spec Text document on those topics

## Slide 14: References
Steve Shellhammer and Rui Yang, “Spec Text for Single Channel MC-OOK On and Off Waveform Generators,” IEEE 802.11-18/967r0, May 2018
Steve Shellhammer, “On Symbol Generation,” IEEE 802.11-18/584r0, March 2018
Rui Cao, Sudhir Srinivasa, Hongyuan Zhang, “Discussion on WUR Multi-Antenna Transmission,” IEEE 802.11-18/413r2, March 2018
Vinod Kristem, Shahrnaz Azizi, Thomas Kenney, “Updated results on WUR performance with multiple TX antennas,” IEEE 802-11/772r0, May 2018
Steve Shellhammer and Bin Tian, “Multiantenna TX Diversity,” IEEE 802.11-18/773r0, May 2018
Miguel Lopez, Dennis Sundman, Leif Wilhelmsson, Omni-directional multi-antenna TX through OFDM symbol diversity, IEEE 802.11-18/881r2, May 2018
Steve Shellhammer and Bin Tian, “Simulation on the Effect of OFDM Symbol Design,” IEEE 802.11-18/418r0, March 2018