## Slide 1: Concerns about Sync Detector False Alarms
Date: 2018-07-DD
Authors:

## Slide 2: Introduction
The purpose of this presentation is to study the response of the HDR and LDR Sync Detectors to the HDR and LDR Data Fields
This is relevant to cases where the receiver begins reception after the Sync Field
  This can occur within a BSS when the STA wakes up early and catches the Data Field of an earlier packet but misses the Sync Field
  This can occur in an OBSS since there is no synchronization between BSS’s
It turns out that there can be significant false alarms in those cases
This leaves the MAC to process the packet, which will eventually fail. However, during that processing time the receiver cannot receive a real packet

## Slide 3: False Alarm within a BSS
False alarm on Data Field of First Packet
PHY/MAC processing for a period of time to determine this is not a true packet detection on the Sync field
If that packet processing takes too long you could miss the next packet, in the case of multiple WUR packet transmissions

## Slide 4: False Alarm within a BSS (Second Example)
False alarm on Data Field of First Packet
PHY/MAC processing for a period of time to determine this is not a true packet detection on the Sync field
False Alarm again on the same Data Field
Packet Processing into the beginning of the next packet, resulting in missing the Sync field in the next packet
This can continue along for multiple packets

## Slide 5: False Alarm due to OBSS
BSS and OBSS are unsynchronized, so it is quite possible to begin reception during an OBSS packet
False alarm on Data Field of OBSS Packet
PHY/MAC processing for a period of time to determine this is not a true packet detection on the Sync field
  Delayed too long to receive Sync File of packet intended for STA
Miss the true packet intended for STA

## Slide 6: False Alarm due to OBSS (Second Example)
BSS and OBSS are unsynchronized, so it is quite possible to begin reception during an OBSS packet
False alarm on Data Field of OBSS Packet
PHY/MAC processing for a period of time to determine this is not a true packet detection on the Sync field
Second False Alarm during OBSS Data Field, delay Sync Detection past true packet intended for STA
Miss the true packet intended for STA

## Slide 7: Sync Detector Study
Here we study the HDR and LDR Sync Detector outputs with the following input signals
  AWGN
  HDR Data Field (with 6 bytes of random data)
  LDR Data Field (with 6 bytes of random data)
  HDR Sync Field (for HDR Sync Detector)
  LDR Sync Field (for LDR Sync Detector)
For each case we look at the maximum output of the Sync Detector and plot the results in a CDF over multiple experiments
Look at the response to HDR and LDR Data field compared to the threshold set by AWGN
  Measure the probability of false alarm on the Data Field
Look at the impact of receiver sensitivity if we increase the threshold to eliminate false alarms

## Slide 8: HDR Sync Detector
Here the HDR Sync Detector combines a correlator and signal power estimator
We take the maximum value to see how it compares for the various signal types
There is a similar detector for the LDR Sync Field

## Slide 9: HDR Sync Detector – CDF of Detection Statistic
As expected, the output due to the HDR Sync Field is significantly higher than for AWGN
However, the output for HDR and LDR Data Field are high compared to AWGN. If the detector threshold is set by AWGN statistics then false detection would result for HDR and LDR Data Fields

## Slide 10: LDR Sync Detector – CDF of Detection Statistic
Similar situation for LDR Sync Detector

## Slide 11: False Alarm Rate – HDR Sync Detector
With a AWGN threshold of 0.29 the false alarm rate on HDR and LDR Data Fields is virtual 100%

## Slide 12: False Alarm Rate – LDR Sync Detector
With a AWGN threshold of 0.20 the false alarm rate on HDR and LDR Data Fields is virtual 100%

## Slide 13: False Alarm Rate – Simulations
Ran Simulations with the “Data Field Only” with no Sync Field in the transmission
Measured the False Alarm Rate versus SNR, for both the HDR and the LDR Data Fields
As the SNR goes up to around 0 dB the False Alarm Rate approaches 100%, as expected based on earlier CDF plots

## Slide 14: Study Impact of Raising Threshold
To avoid the false alarms on the Data Field, we can raise the Sync Detector threshold
The threshold is selected to be high enough to avoid the false alarms, based on CDF curves (see earlier slides)
Ran AWGN sims
 | Original Threshold | New Threshold
HDR Sync | 0.29 | 0.63
LDR Sync | 0.20 | 0.62

## Slide 15: PER Sims – Low Data Rate – New Threshold
Significant SNR impact

## Slide 16: PER Sims – High Data Rate – New Threshold
Smaller SNR impact, but still significant
  HDR more limited by Data Field

## Slide 17: Modified Threshold – SNR Impact
 | SNR (dB) (Original Threshold) | SNR (dB) (New Threshold) | SNR Impact of New Threshold (dB)
HDR | -4.0 | -1.7 | 2.3
LDR | -7.7 | -2.1 | 5.6

## Slide 18: Conclusions
The CDF of the Sync Detector outputs due to HDR and LDR Data Field inputs are significantly higher than for AWGN input
The CDF for the HDR Data Field input is particularly high
If the detector threshold is set based on the AWGN statistics then false detection on the data field will be common
  Simulation results show that with the same threshold that close to 100% False Alarm Rate
If the detector threshold is raised to minimize false alarms on data fields, then PER performance will significantly suffer
  If the threshold is increased to eliminate the False Alarms the SNR impact on the LDR is over 5 dB, in AWGN
In our opinion, this is a significant issue

## Slide 19: Straw Poll
Should the Task Group investigate solutions to this False Alarm problem?
  Yes
  No
  Abstain