## Slide 1
Issues on channel usage in WUR FDMA transmission
Date: 2018-07-10
Authors:

## Slide 2: Introduction
The FDMA transmission and the following channel access method has been proposed in [1]
The channel switch procedure among secondary channels is needed when the channel is busy in every duty cycle of WURx
  The determination method of sensing the secondary channel access issue (when WURx of STA cannot receive the WUR frame because of channel status) is needed
  The channel switch method to recover the secondary channel access issue is needed
In this contribution, the discussion on channel access method and channel switching invocation are proposed

## Slide 3: Recap: FDMA transmission of WUR frame
The FDMA WUR frame has been agreed:
  Each 20MHz only contains one 4MHz sub-channel for wake-up signal transmission.
  Similar to 11ax’s 20MHz only operation, one wake-up receiver can stay in one of the sub-channel in wide bandwidth.
AP access the channel based on the channel access method in legacy 802.11 standard’s method

## Slide 4: Recap: Punctured FDMA signal
The punctured structure of the FDMA enables the reduced unfairness issue of the channel usage [2]
However, if the channel is busy, AP cannot send the WUR wake-up frame to STA allocated in that 20MHz band
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #o
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
L-STF
Wake-Up Signal for WUR STA #p
L-LTF
L-SIG
BPSK-Mark
Wake-Up Signal for WUR STA #m
L-LTF
L-SIG
BPSK-Mark
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
L-STF
L-STF
CCA Busy
CCA Busy

## Slide 5: Channel access issue: for continuously busy status in secondary channel
If the secondary channel is busy in every duty cycle period, the allocated STAs cannot receive the wake-up frame
However, the channel switching cannot be performed because of the channel status in that secondary channel
  The method of invoking channel switch is needed
The channel switch invocation method can be made in 2 ways:
  STA initiated method: by wake-up signal to check connectivity with channel alive cycle
  AP initiated method: by broadcast wake-up frame in WUR primary channel

## Slide 6: Invoking channel switch by checking connectivity with channel alive cycle
STA may check the channel status by transmitted WUR frame to other station
  If any kind of WUR frame is received in the allocated channel, the channel is valid
If there is no WUR frame transmitted in that 20MHz channel, AP may transmit the null wake-up frame after the predetermined period

## Slide 7: Invoking channel switch by checking connectivity with channel alive cycle
If STA does not receive the wake-up frame for some duration, it may proceed the channel switch procedure
  The channel switch procedure can be performed in PCR, by using the WUR mode setup frame

## Slide 8: Invoking channel switch by wake-up frame in WUR primary channel
AP may detect the channel status and the status of WUR frame transmission
If AP detects that channel access issue, AP may transmit the wake-up frame in the primary 20MHz channel after WUR beacon to switch the FDMA channel

## Slide 9: Conclusion
In this presentation, we discussed channel switching issue in FDMA transmission
The detection and recovery of channel access issue for FDMA WUR wake-up frame can be proceeded in 2 ways:
  STA initiated method by channel alive cycle and null wake-up frame
  AP initiated method with WUR wake-up frame in primary 20MHz channel after the WUR beacon frame

## Slide 10: Straw poll
Do you agree with the following?
  The channel switch invocation method in case of continuous channel access failure in FDMA transmission is needed
  Y:
  N:
  Abs.:

## Slide 11: Reference
[1] IEEE P802.11ba D0.3
[2] IEEE 802.11-18/791r0 “Preamble Punctured WUR FDMA Transmission”