## Slide 1: Vehicular-to-Pedestrian Channel Models
Date: 2018-07-10
Authors:

## Slide 2: Abstract
Protect vulnerable road users to reduce accidents with reliable vehicle-to-pedestrian communications
Accurate vehicle-to-pedestrian channel models to design reliable vehicle-to-pedestrian communications
Comparison of V2X channels
Related work on vehicle-to-pedestrian channel models
V2P path loss models

## Slide 3: Motivation
Vulnerable road users account for 30% of road fatalities in Europe.
Sensor-based crash avoidance systems suffer from limitations.
360 degree awareness by direct exchange of information between vehicles and pedestrians
[1]

## Slide 4: Motivation
Accurate V2P channel models required for reliable communication system
Extensive work has been done for
vehicle-to-vehicle (V2V)
vehicle-to-infrastructure (V2I)
person-to-network (P2N)
V2P channel models only 3 recent papers
[2] @ 1.85 GHz, [3] @ 3.8 GHz, [4] @ 5.2 GHz
Much work to be done!
V2I
V2V
V2P
P2N

## Slide 5: Comparison of V2X Channels
V2V, V2I and V2P: Different antenna height, mobility pattern, and propagation scenarios  different propagation aspects
Nonstationary V2V and V2P channels: Time-variant channel statistics due to moving TX, RX, and dynamic environment
Signal attenuation: Strong spatio-temporal correlations
Stochastic channel models [2]: Large-scale VANET simulators e.g., ns3 and OMNet++
 Average packet delivery ratio, but difficult to account for geometry dependent correlations
Geometry-based stochastic channel model (GSCM) [3], [4]: Link level and system level simulations in particular for safety-relevant applications such as platooning, automated and remote driving
 Geometry dependent packet outages, but higher complexity

## Slide 6: Related Work: 3GPP 5G V2X Channel Models & Evaluation Methodology
3GPP 5G V2X use case groups [5]:
Vehicle platooning
Extended sensors
Automated driving
Remote driving
5G V2V performance evaluation for use case groups: Adapted parameter sets of GSCM [6] for below and above 6 GHz
V2P and V2I models assume same parameters as V2V
  Realistic?

## Slide 7: Related Work: V2P Channel Models
V2P stochastic channel models (SCM) @ 1.85 GHz [2]
In-vehicle to pedestrian
LOS/NLOS and in pocket/next to face
Path loss, shadow, small scale, and multi scale fading parameters based on measurements
SCM with combination of Weibull and Rayleigh distributions
V2P channel models @ 3.8 GHz [3]
Only LOS evaluated
RX antenna fixed on long wooden stick  untypical, best case pedestrian scenario
Two-ray path loss model < 32 meters

## Slide 8: V2P Path Loss Models
Based on [43] @ 5.2 GHz:
Line-of-Sight (LOS):
  Static pedestrian: Two-ray ground reflection path loss model
  Moving pedestrian, texting: Log-distance path loss model + increased shadow fading
NLOS due to other nearby pedestrians: 5-10 dB additional path loss due to shadowing
NLOS due to parked vehicles: Multiple knife edge diffraction model
NLOS due to buildings: Log-distance path loss model (propagation through building) + knife edge diffraction (+ reflections/scattering)

## Slide 9: V2P Path Loss Models: LOS – Static Tripod
Log-distance path loss model
Reference distance d0 = 1 m
Loss at d0 PL(d0) = 46.77 dB
Path loss exponent n = 2.03
Log-normal shadow fading
Standard deviation 𝜎 = 3.23 dB
1.1 m
7 m
TX
RX
2 m

## Slide 10: V2P Path Loss Models: LOS – Moving Pedestrian, Texting
Pedestrian antenna at low elevation and close to body  self-body shadowing
Log-distance path loss model
Reference distance d0 = 1 m
Loss at d0 PL(d0) = 40 dB
Path loss exponent n = 2.44
Log-normal shadow fading
Standard deviation 𝜎 = 5.47 dB
1.3 m

## Slide 11: V2P Path Loss Models: NLOS, Crowd Shadowing
Nearby other pedestrians  5-10 dB additional path loss due to shadowing
Log-distance path loss model
Reference distance d0 = 1 m
Loss at d0 PL(d0) = 67 dB
Path loss exponent n = 1.26
Log-normal shadow fading
Standard deviation 𝜎 = 3.35 dB

## Slide 12: V2P Path Loss Models: Parking Cars, NLOS, Diffraction – First Results

## Slide 13: V2P Path Loss Models: Parking Cars, NLOS, Diffraction – First Results

## Slide 14: V2P Path Loss Models: Parking Cars, NLOS, Diffraction – First Results
Multiple knife-edge diffraction model + two-ray path loss model

## Slide 15: Conclusions
V2P channel different from V2V/V2I channel  3GPP 5G approach realistic?
V2P channel models: Recent papers [2] @ 1.85 GHz, [3] @ 3.8 GHz, [4] @ 5.2 GHz
V2P path loss models based on [4]:
LOS moving pedestrian, texting: increased shadow fading
LOS static pedestrian: Two-ray pathloss model
NLOS due to parked vehicles: Multiple knife edge diffraction model
NLOS due to other nearby pedestrians: 5-10 dB additional path loss due to shadowing

## Slide 16: Conclusions
V2P channel different from V2V/V2I channel  3GPP 5G approach realistic?
V2P channel models: Recent papers [2] @ 1.85 GHz, [3] @ 3.8 GHz, [4] @ 5.2 GHz
V2P path loss models based on [4]:
Accurate V2P channel models
Design reliable V2P communications
Protect vulnerable road users
LOS moving pedestrian, texting: increased shadow fading
LOS static pedestrian: Two-ray pathloss model
NLOS due to parked vehicles: Multiple knife edge diffraction model
NLOS due to other nearby pedestrians: 5-10 dB additional path loss due to shadowing

## Slide 17: References
[1] Wikipedia https://commons.wikimedia.org/wiki/File:D%C3%A9tection_de_personne_-_exemple_3.jpg
[2] Ibdah, Yazan and Ding, Yanwu (2015) Mobile-to-Mobile Channel Measurements at 1.85 GHz in Suburban Environments. IEEE Transactions on Communications, vol. 63, no. 2, Feb. 2015, pp. 466-475
[3] Makhoul, Gloria and D’Errico, Raffaele and Oestges, Claude (2018) Wideband Vehicle to Pedestrian Propagation Channel Characterization and Modeling. EuCAP 2018, 9.-13. Apr. 0218, London, UK.
[4] Rashdan, Ibrahim and Ponte Müller, Fabian and Wang, Wei und Schmidhammer, Martin und Sand, Stephan (2018) Vehicle-to-Pedestrian Channel Characterization: Wideband Measurement Campaign and First Results. EuCAP 2018, 9.-13. Apr. 2018, London, UK.
[5] 3GPP (2018) Study on evaluation methodology of new Vehicle-to-Everything V2X use cases for LTE and NR;(Release 15). TR 37.885, V15.0.0 (2018-06).

## Slide 18: References
[6] 3GPP (2018) Study on channel model for frequencies from 0.5 to 100 GHz (Release 15). TR 38.901, V15.0.0 (2018-06).