## Slide 1: System Level Simulation Results of Full Duplex Transmission
Date: 2018-07-02
Authors:

## Slide 2: Introduction
Full Duplex (FD) technology is currently being investigated as a candidate key technology for the next generation Wi-Fi systems [1-3].
Some initial results have been shown in [2] to demonstrate the throughput enhancement with interference cancellation.
This presentation provides further system level simulation results to show throughput gains of FD compared to half-duplex technology in existing Wi-Fi systems. The simulation is based on the NS3 simulation platform.

## Slide 3: Simulation Assumptions
Number of AP: 1, 4
Number of STAs per BSS: 10
BSS Range: 10m
Bandwidth: 20MHz @ 2.4GHz
Self interference cancelation (SIC): 80dB~120dB
Traffic model: full buffer
Packet size: 1500 bytes
Data MCS: link adaptation
Antenna#: AP 1, STA 1
STA position: random (uniform distribution) within a certain BSS range
BSS Range

## Slide 4: Transmission procedure
Baseline:
  EDCA based transmission
Full Duplex:
  Trigger frame initiates every transmission
    Symmetric case (both AP and STA have FD capability)
    Asymmetric case (only AP has FD capability)
Trigger
Data 1
BA 1
Data 2
BA 2
AP
STA
Trigger
Data 1
BA 1
BA 2
AP
STA1
Data 2
STA2
Symmetric case
Asymmetric case

## Slide 5: Simulation architecture
When start transmission, the AP should decide whether to send a Trigger frame
  Considering self interference and mutual interference, if the predicted sum rate of the two FD links (UL+DL) is higher than the link without using FD, then send a Trigger frame
If needed, send the Trigger frame, followed by data transmission
STA side: send data after receiving the Trigger frame
AP side
STA side

## Slide 6: Simulation Results (symmetric FD)
Setting:
  Mode: symmetric FD
  AP number = 1
  STA number per BSS = 10
  SIC = 80, 90, 100, 110, 120dB
Result:
  110dB SIC is needed to achieve maximum throughput gain
  Up to 125% throughput gain can be obtained
Throughput gain definition:
  throughput gain = (FD throughput – EDCA throughput)/EDCA throughput

## Slide 7: Simulation Results (symmetric FD)
Setting:
  Mode: symmetric FD
  AP number = 4
  STA number per BSS = 10
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  Up to 194% throughput gain can be obtained
  More throughput gain can be achieved comparing with the single BSS case

## Slide 8: Simulation Results (asymmetric FD)
Setting:
  Mode: asymmetric FD
  AP number = 1
  STA number per BSS = 2 (simple setting)
    STA1 is 1 meter away from the AP (near)
    STA2 is 5 meters away on the other side (far)
    Using near-far paring, the DL transmission to STA1 can have relatively high SINR, in which case we can see more FD gain
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  29%~44% throughput gain can be obtained in simple scenario
STA1
STA2
1 m
5 m

## Slide 9: Simulation Results (asymmetric FD)
Setting:
  Mode: asymmetric FD
  AP number = 1
  STA number per BSS = 10 (random setting)
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum throughput gain
  27% throughput gain can be obtained

## Slide 10: Latency Improvement
Besides throughput, latency is also an important performance metric
Due to the bi-directional data transmissions, a given amount of data frames are expected to finish transmission within a shorter time by using FD compared with half-duplex .
Simulation assumption:
  A fixed amount of data packets are put into the queues of the AP and the STAs at the beginning of the simulation
  The latency for each packet is measured by the following equation:
    Delay = the time that the packet is successfully received by the receiver – the time that the packet is put into the queue of the transmitter

## Slide 11: Latency Results
Setting:
  Mode: symmetric FD
  AP number = 1, 2
  STA number per BSS = 5
  Traffic Volume
    DL: 2000 Packets
    UL: 2000 Packets
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum latency gain
  43% latency gain can be obtained
Latency gain definition:
  Latency gain = (EDCA latency – FD Latency)/EDCA latency

## Slide 12: Latency Results
Setting:
  Mode: asymmetric FD
  AP number = 1
  STA number per BSS = 2, 5
  Traffic Volume
    DL: 2000 Packets
    UL: 2000 Packets
  SIC = 80, 90, 100, 110, 120dB
Result :
  110dB SIC is needed to achieve maximum latency gain
  Achievable latency gain goes from 8% to 22%

## Slide 13: Conclusion
Through NS3 based system level simulation, we demonstrate that a large amount of throughput gain can be achieved by using FD transmission
For throughput enhancement, we illustrate more than 100% throughput gain in the symmetric FD case, and 27%~44% throughput gain in the asymmetric FD case
For latency reduction, we show that up to 43% latency gain can be obtained in the symmetric FD case, and 8%~22% latency gain is achievable in the asymmetric FD case.

## Slide 14: References
[1] IEEE 802.11-18/0191r0, 802.11 Full Duplex
[2] IEEE 802.11-18/0549r0, Full Duplex for 802.11
[3] IEEE 802.11-18/0448r1, Full Duplex Benefits and Challenges