## Slide 1: NGV MAC Discussions
Date: 2018-07-08
Authors:

## Slide 2: Introduction
NGV SG was formed to enhance the throughput and possibly range from .11p [1][2][3].
  .11p is sufficient for basic safety applications.
  The new use cases are based on higher throughput and other enhancement.
    The PAR contribution asks for 2x throughput improvement
This document discusses the potential NGV MAC:
  MAC Technology Candidates
  Coex with .11p
  If possible, avoid optional features for OCB operation

## Slide 3: Recap: 802.11p PHY/MAC
PHY (BW=10MHz): 2x down clock of 11a
  BCC, 1SS
  GI=1.6us
  3/4.5/6/9/12/18/24/27 Mbps
    3/6/12 Mbps are mandatory
MAC:
  Outside the Context of a BSS (OCB) Transmissions
    STA’s capabilities are not announced in MAC layer
  Timing Advertisement
  Limited Frame sizes

## Slide 4: NGV MAC 1
OCB vs BSS:
  NGV device should at least work in OCB mode as 11p device.
    The use cases of NGV are similar to the use cases of 11p device.
  If BSS is adopted because of some use cases, the new .11 features, e.g. fast BSS transmission (11ai features) can be adopted.
    This operation may be in separate channel from OCB operation.
Coexistence of .11p Device and NGV Device:
  NGV device is also .11p device.
    A NGV device uses 11p PPDU to transmit frames to a 11p device.
  L-SIG protection: L-SIG in .11p PHY header indicates the end of NGV PPDU.
    A .11p device respects the NGV PPDU length as defined in .11p PHY header and does EIFS recovery at the end of NGV PPDU.
11p PHY
Header
NGV PHY
Header
Data field

## Slide 5: NGV MAC2
Frame Transmission in NGV PPDU:
  Unicast frame transmission of NGV device: A NGV device can transmit unicast frames in .11p PPDUs or NGV PPDUs to another NGV device.
    .11 management frame, up layer message or PHY header can be used for a NGV device to announce its NGV capability and potential other optional capabilities.
  Broadcast frame transmission of NGV device with the following potential solutions:
    Disallowing the broadcast frame through NGV PPDU
      It is not a good idea especially when a feature being only support by NGV devices requires broadcast frame support.
    Deciding whether the broadcast frames are allowed in NGV PPDU per the type/subtype/Category, e.g.
      The broadcast frames for the new features that are not supported by .11p device.
    Deciding whether the broadcast frames are allowed in NGV PPDU per the channel being used.
    Adaptive broadcast frame through NGV PPDU.
      Transmitting broadcast frame through .11p PPDU once a neighbor .11p device is detected. Otherwise transmitting broadcast frame through NGV PPDU

## Slide 6: NGV MAC3
Frame Length Indication
  NGV PHY Header indicates MPDU length in octets.
11p PHY
Header
NGV PHY
Header
MPDU
  MPDU Delimiter indicates MPDU length in octets.
11p PHY
Header
NGV PHY
Header
Data field
MPDU Delimiter
MPDU

## Slide 7: Summary
MAC technologies are discussed
.11p-NGV coexistence is discussed

## Slide 8: Reference
[1] Hongyuan Zhang, et al, “802.11 For Next Generation V2X Communications”, IEEE 802.11-18/0513r2.
[2] Bo Sun, et al, “802.11 NGV Proposed PAR”, IEEE 802.11-18/0861r3
[3] Hongyuan Zhang, et al, “NGV PHY Feasibility Discussions”, IEEE 802.11-18/0860r2