## Slide 1: CID 1195
Date: 2018-09-01
Authors:

## Slide 2: Abstract
This submission discusses CID 1195 of LB 232, and suggests a different solution from 18/810r1.
  Instead of allowing any AC to borrow the TXOP time of any other AC, only allow a higher AC to borrow TXOP time from a lower AC

## Slide 3: Reminder on EDCA TXOPs
The Transmit Opportunity (TXOP) is one of the key modifications introduced by IEEE 802.11e-2005
A TXOP is a period of time during which the TXOP owner may use the wireless medium “at will”
  As long as the duration of all transmissions of the TXOP owner and any (expected) responses to its transmissions do not exceed the TXOP limit the TXOP owner may send one or more (aggregated) frames

## Slide 4: TXOP is bounded
The use of TXOPs is limited by various rules
  One such rules is the following
Frames queued at ACs other than the AC that gained access to the wireless medium must not be transmitted
  Clause 10.22.2.7, page 1385 of IEEE 802.11-2016: “Multiple frames may be transmitted in an EDCA TXOP […] if there is more than one frame pending in the primary AC for which the channel has been acquired. However, those frames that are pending in other ACs shall not be transmitted in this EDCA TXOP […].”

## Slide 5: 18/810r1 asked a great question
Why can’t traffic from another AC be transmitted once traffic from the AC currently transmitting has completed, and if the TXOP still has available airtime?
This submission attempts to answer this question
  The authors also think that it is a good idea, but with caveats

## Slide 6: Differentiated Service in only meaningful if service is differentiated
If a STA has voice traffic ready to be transmitted, EDCA gives it a higher probability of gaining medium access than a STA with AC_BE traffic ready to be transmitted
This is good, because “Voice is an inelastic ‘real time’ application that sends packets at the rate the codec produces them […], should be given a low-delay queue […] to ensure that variation in delay is not an issue.” (RFC 4594 1.5.3)

## Slide 7: Differentiated Service in only meaningful if service is differentiated
By contrast, AC_BE is typically “for traffic that has not been identified as requiring differentiated treatment” (RFC 4594 2.1)
If AC_BE is allowed to borrow time from AC_VO access probability, now AC_VO is effectively competing against AC_BE, and AC_BE borrows some of AC_VO’s differentiated service
This asymptotes to removing the concept of differentiated service

## Slide 8: A thought experiment helps use visualize the challenge
Suppose a congested cell where most stations have voice and best effort traffic in their buffer
If every station sends BE within VO rules, then there is effectively no differentiation anymore, only one AC
18-810r1 took a numbered example, the following slides attempt the same logic, with an opposite conclusion

## Slide 9: VoIP vs BE Transmissions are Different
VoIP and Data traffic do not have the same differentiated service requirements
  VoIP typically sends single frames (e.g. 160 B payload with G711) at regular interval (e.g. 20 ms with G711)
  BE data is “anything else”, not time sensitive, and with “any” volume requirement (e.g. large FTP transfer, BitTorrent service, or just a single telnet character)
Allowing a lower AC to transmit after a higher AC but within the higher AC TXOP may be more efficient to the local STA, but it may negatively impact the general efficiency of that higher AC in the cell

## Slide 10: Transmission of a single VoIP
Suppose a standard single G.711 packet
RTS (52 µs) + SIFS (16 µs) + CTS (44 µs) + SIFS (16 µs) + AC_VO (44 µs) + SIFS (16 µs) + ACK (44 µs)
  Assuming control frames sent a 6 Mbps with legacy preamble
  Assuming 160 B voice payload + 28 B MAC overhead, MCS 7 20 MHz 1 SS 800 ns GI (65 Mbps)
  Air is free after 232 µs
RTS
CTS
AC_VO
ACK

## Slide 11: Frames Times
Slightly different computation than 18-810, with similar assumptions
RTS = 20 + 4*ceil((20*8+22)/24) = 52us
where
20 = 8LSTF+8LLTf +4LSIG
4 = 4us
20 = 20B for RTS
8=8b/B
22 = 16Service+6Tail
24 = 6Mbps * 4us
CTS = 20 + 4*ceil((14*8+22)/24) = 44us
Voice = 20 + 4*ceil(((160+28)*8+22)/(65*4)) = 44us
Ack = same as CTS

## Slide 12: Backoff durations
Assuming initial transmission attempts succeed
  AIFS = AIFSN × 9 µs
  CW = [0 … CWmin], average CW = ½ × CWmin
  AC_VO: 47.5 µs (16+9x7/2)
  Next STA can send at t = 232 + 47.5 = 279.5 µs

## Slide 13: Transmission of a single BE burst
Suppose an FTP transfer, 2528 µs TXOP
RTS (52 µs) + SIFS (16 µs) + CTS (44 µs) + SIFS (16 µs) + 8x(AC_BE (208.4 µs) + SIFS (16 µs) + ACK (44 µs))
  Assuming control frames sent a 6 Mbps with legacy preamble
  Assuming 1500 B payload + 28 B MAC overhead, MCS 7 20 MHz 1 SS 800 ns GI (65 Mbps)
  Air is free after 2275.2 µs
RTS
CTS
AC_BE
ACK
AC_BE
ACK
AC_BE
ACK
…

## Slide 14: Transmission of a BE burst within an AC_VO TXOP
The VoIP part still consumes 232 µs
Then: SIFS (16 µs) + 6x(AC_BE (208.4 µs) + SIFS (16 µs) + ACK (44 µs))
  AC_VO duration is 2080 µs
  Air is free after 1842.4 µs
RTS
CTS
AC_VO
ACK
AC_BE
ACK
AC_BE
ACK
…

## Slide 15: Once a Transmission Completes, what are the chances that the next transmission in the cell will be AC_VO (or AC_BE)?
Next STA with AC_VO traffic has to wait:
AIFSN[AC]+RAND(0,3) = 18 to 45 µs
Next STA with AC_BE traffic has to wait:
AIFSN[AC]+RAND(0,15) = 27 to 162 µs
AC_VO STA is likely to send (p=86.7%)

## Slide 16: These computations are simplified approximations
Adding more stations with more traffic types in their queue makes the computation more complex, less deterministic
  a) backoff is exponential with retries (higher client density implies more retries)
  b) This submission (and 18-810) assume ½ CWMin, but wait time is in fact a distribution … usually one STA will start earlier, if there is more than one STA. Also, critically, backoff time is *shared* between STAs.
  c) 16 + 9us * CWmin/2 is some kind of upper bound for lightly loaded networks only.
However, this simple model allows for a simple impact evaluation

## Slide 17: How delayed is the next voice packet?
If 2 STAs have a voice packet to send, and one wins the medium access:
  STA2 may have to wait about 280 µs (then has 87% chance of getting the next airtime slot)
  If STA1 is permitted to fill its AC_VO TXOP with other AC traffic, now STA2 may to wait about 1840 µs (then has 87% chance of getting the next airtime slot)
Allowing upper AC hijacking can multiply wait time by close to 7!

## Slide 18: Does it matter?
Delaying a single packet may seem insignificant
  That BE packet will need to be sent sooner or later anyway
However, Voice is real time
  Packets are timestamped
  In most networks, a ‘next packet’ delayed by more than 30 ms (compared to the previous packet timestamp) is discarded
  Each STA with VoIP packet coming into its transmission buffer must be given a high opportunity to be sent fast
  A voice packet will come into the buffer every 20 ms
time budget between packets: 20 ms

## Slide 19: How Many voice calls can my cell support?
With AC_VO offered a differentiated service (current method)
  279.5 µs between voice packets with 87% access chance seems to indicate support for a large number (107 packets per 30 ms!)
  In fact, overhead (beacon and others) reduces the available airtime
  A single STA sends 1 VoIP packet every 20 ms
  AC_BE access chances and collision chances follow a standard Poisson distribution
  Common designs call for 20 to 25 active calls per cell

## Slide 20: How Many voice calls can my cell support?
If lower AC piggy back within an AC_VO
  A single AC_VO burst now occupies 1842.4 µs
  A contending AC_VO STA may need to wait 1890 µs (1842.4+47.5), then contends with 87% chances to transmit (against AC_BE)
  But even in perfect conditions (no AC_BE win, no overhead [beacons etc.]), 16 calls saturate the 30 ms airtime space
  But a single STA sends one packet every 20 ms, there is only space for 10 calls within that space
  We are back to the VoIP efficiency of 802.11b (10 calls max)

## Slide 21: Conclusion 1
Allowing a lower AC to transmit into an AC with higher priority degrades the differentiated service offered to the higher AC
The consequence is effectively to transmit most traffic in the highest active AC and tends to suppress the “Differentiated” in DiffServ
A complex application and station mix makes the picture of real networks more complex
  But the general conclusion that allowing a lower AC to borrow time from a higher AC results in less time for the higher AC

## Slide 22: However, 18-810 raises another great point
“A successful TXOP is a precious resource
  In terms of overhead, receiving access to the wireless medium may be costly
  Collisions easily increase overhead to significant levels
Once a TXOP has been acquired it should be used to the full extent
  Under high load, the competition for TXOPs must be reduced since otherwise efficiency decreases”

## Slide 23: The main issue is gaining the access
AIFSN + random backoff consume time
Higher priority AC prioritization cannot be deterministic in a CSMA/CA system
  We cannot say “wait AIFSN=0 if AC_VO has to send”
    Collision rates would dramatically increase
  We cannot say “CW=0 for AC_VO”
    Collisions would be guaranteed
We need a waiting system to distribute access, but need to ensure that AC_VO gets access with minimum delay

## Slide 24: Once access is gained, using it makes sense
However, once a lower AC has gained access, allowing the same STA higher AC to leverage that same TXOP makes sense
  Collisions are already avoided by the access method
  We can provide differentiated service to the higher AC without collision risk

## Slide 25: Proposed additional text
Modify restriction on use of a primary AC’s TXOP
  IEEE 802.11-2016, Clause 10.22.2.7 (Multiple frame transmission in an EDCA TXOP), page 1385
Additional rules are needed describing that sharing with higher AC is permissible if the traffic of the AC that gained medium access was transmitted over the medium

## Slide 26: References
G. R. Hiertz, “CID 1195,” IEEE 802.11 submission 11-18/810r1, Sep. 2017.
J. Henry and A. Myles, “QoS mapping comment for 802.11md Letter Ballot,” IEEE 802.11 submission, 11-18/354r1, Feb. 2018.
Cisco, “Voice Over IP - Per Call Bandwidth Consumption,” Apr. 2016. [Online]. Available: https://www.cisco.com/c/en/us/support/docs/voice/voice-quality/7934-bwidth-consume.html