## Slide 1: Proposed Spec Text Change on WUR Capabilities Element
Date: 2018-08-24
Authors:

## Slide 2: Introduction
According to 11ba D0.4[1], a WUR STA declares that it has WUR capability by transmitting the WUR Capabilities element. The WUR Capabilities element contains a number of fields that are used to advertise WUR capabilities of a WUR STA.
WUR Capabilities element is included in Beacon frame, Probe Response frame and (Re)association Response frame transmitted by a WUR AP.
WUR Capabilities element is included in Probe Request frame and (Re)association Request frame transmitted by a WUR non-AP STA.

## Slide 3: WUR Capabilities Element
Indicate the supported bands for WUR operating channels for WUR non-AP STA and reserved for WUR AP
Indicate the maximum
time that the WUR non-AP STA requires to transition its PCR from doze state to awake state and reserved for WUR AP.
Indicate support for the reception of nonzero length Frame Body field in a WUR frame and reserved for WUR AP.
Indicate Group ID support and reserved for WUR AP.
Indicate support for the reception of protected WUR frame and reserved for WUR AP.
Indicate support for the reception of 20 MHz WUR PPDU with HDR and reserved for WUR AP.
Indicate whether the
WUR channel switching capability for receiving WUR Beacon and WUR
Wake-up frames that are transmitted in different channels is enabled or disabled and reserved for WUR AP.

## Slide 4: Discussion
Notice that all of information fields of the WUR Capabilities element are applicable to a WUR non-AP STA only.
  It is understandable that a WUR non-AP STA need not to know WUR capabilities of a WUR AP since it does not transmit WUR PPDU to the WUR AP.
  WUR mode negotiation initiated by the WUR non-AP STA can be based on WUR parameters in the WUR Operation element transmitted by the WUR AP.
It seems that the only reason why a WUR AP need to transmit the WUR Capabilities element is to declare it is WUR capable.
However, the WUR Operation element included in the Beacon frame, Probe Response frame and (Re)association frame transmitted by WUR AP can also be used to declare it is WUR capable.
Conclusion: it is unnecessary for a WUR AP to transmit the WUR Capabilities element.

## Slide 5: Proposed Spec Text Changes(1/3)
9.3.3 Management frames
L46P23: Delete the row corresponding to WUR Capabilities from Table 9-33 (Beacon frame body).
L32P24: Delete the row corresponding to WUR Capabilities from Table 9-36 (Association Response frame body).
L17P25: Delete the row corresponding to WUR Capabilities from Table 9-38 (Reassociation Response frame body).
L12P26: Delete the row corresponding to WUR Capabilities from Table 9-40 (Probe Response frame body).

## Slide 6: Proposed Spec Text Changes (2/3)
9.4.2.274 WUR Capabilities element
L4P32: change the paragraph as follows:
  A WUR non-AP STA declares that it has WUR capability by transmitting the WUR Capabilities element. The WUR Capabilities element contains a number of fields that are used to advertise WUR capabilities of a WUR non-AP STA. The WUR Capabilities element is defined in Figure 9-751d (WUR Capabilities element format).
L25P32: change the paragraph as follows:
  For WUR AP, the Supported Bands field is reserved.
L16P33: change the encoding for the PCR Transition Delay subfield in Table 9-318f as follows:
  Reserved for a WUR AP.
L26P33: change the encoding for the Nonzero Length Frame Body Support subfield in Table 9-318f as follows:
  Reserved for a WUR AP.
L38P33: change the encoding for the Group IDs Support subfield in Table 9-318f as follows:
  Reserved for a WUR AP.
L46P33: change the encoding for the Protection Support subfield in Table 9-318f as follows:
  Reserved for a WUR AP.
L54P33: change the encoding for the 20 MHz WUR PPDU with HDR Support subfield in Table 9-318f as follows:
  Reserved for a WUR AP.

## Slide 7: Proposed Spec Text Changes (3/3)
9.4.2.275 WUR Operation element
L3P34: change the following paragraph as follow:
  A WUR AP declares that it has WUR capability by transmitting the WUR Operation element. The WUR Operation element contains the set of parameters necessary to support the WUR operation. The format of the WUR Operation element is defined in Figure 9-751g (WUR Operation element format).

## Slide 8: References
[1] IEEE P802.11ba/D0.4, August 2018

## Slide 9: Straw Poll
Do you agree the spec text changes proposed in slides 5, 6 and 7?
  Y/N/A