## Slide 1: Simulation Scenarios
Date: 2018-08-21
Authors:

## Slide 2: Summary
Simulation Scenarios definition
  Proposed definition
  Proposed template description format
Discussion on the set of scenarios
  Summary of discussion so far
  Proposal for identifying a minimum set of simulation scenarios

## Slide 3: Definition of “Simulation Scenario”
A simulation scenario is defined by
  Topology: AP/STAs positions, P2P STAs pair positions, obstructions , layout, propagation model
  Traffic model
    STA - AP traffic
    P2P traffic (tethering, Soft-APs, TDLS)
    ‘Idle’ devices (generating management traffic such as probes/beacons)
  List of PHY, MAC, Management parameters
    We may want to fix the value of some parameters to limit the degrees of freedom, and for calibration
The group should adopt a common way to describe a scenario
  See a tentative template in document 11-18/1423r0

## Slide 4: Definition of “Simulation Scenario”
The purpose of a simulation scenario is not to exactly simulate a usage model, but rather to capture the key characteristics of that usage model, relevant for testing the effectiveness of new LC solutions
  We should define a preferably reduced number of simulation scenarios that cover most of the usage models
It is useful to limit the number of simulation scenarios to a minimum set that represents the most important challenges for LC
  Helps to better identify the goals for LC
  Facilitates comparison

## Slide 5: Current Status and Goals
TGax simulation scenarios document statistic
  Have 31 revisions in total
  From August 2013 to November 2015
Multiple usage models have been proposed at previous meetings
  Key considerations have been summarized in usage model (11-18/1109r5)
  Other characteristics are needed to represent the most important challenges for LC
In the next slides we try to
  Summarize key characteristics for each scenario

## Slide 6: Proposed Set of Simulation Scenarios
 | Scenario Name | Topology | Management | Channel Model | Traffic profile [tentative]
1 | Industrial wireless | A - Industrial Robotic work cell e.g. ~8m x 10m x 7m or ~5m x 5m x 3m size ~10s of STAs/AP, P2P pairs | Managed | Indoor-Manufacturing Cell | Industrial
2 | Hospital ward | B - Dense small BSSs e.g. ~6m x 6m x 3m size, ~1-3m inter AP distance, ~10s of STAs/AP, P2P pairs | Managed | Indoor-Office | Enterprise
3 | Enterprise | C - Dense small BSSs e.g. . ~14m x 14m x 3m size ~1-3m inter AP distance ~10s of STAs/AP, P2P pairs |  |  | 
 |  |  |  |  | Enterprise
4 | Residential | D - Apartment bldg. e.g. ~6m x 6m x 3m size, ~0.5-2 m inter AP distance ~10s of STAs/AP, P2P pairs | Managed | Indoor-Home | Home

## Slide 7: Proposed Unified Set of Scenarios
The identified scenarios in slide 6 cover most of the challenging usage models that will put LC solutions to a test
Would the group agree to adopt these scenarios as a baseline set?
  i.e. these scenarios to be used for proving effectiveness of LC solutions
If yes, we need to define each of them in details
  Call for submissions following the template in 11-18/1423r0

## Slide 8: Conclusion
Defined what a Simulation Scenario is
Identified a baseline set of simulation scenarios from earlier IEEE presentations
  The scenarios seem representative of most of the key aspects to be investigated in LC and cover the usage models (11-18/1109r5)
Do we agree to use these scenarios as a reference set?
  i.e. these scenarios are used for proving effectiveness of LC solutions
Call for submissions for refining scenarios description
  Following the proposed template in 11-18/1423r0

## Slide 9: References
https://mentor.ieee.org/802.11/dcn/18/11-18-1236-01-00bb-ieee-802-11bb-reference-channel-models-for-indoor-environments.pdf
https://mentor.ieee.org/802.11/dcn/18/11-18-1109-05-00bb-lc-usage-model-document.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-1000-02-0hew-simulation-scenarios.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-1001-09-0hew-simulation-scenarios-document-template.docx