## Slide 1: Discussions on the PHY features for EHT
Date: 2018-09-09
Authors:
Name | Affiliation | Address | Email
Xiaogang Chen | Intel | NE 25th Ave. Hillsboro, OR, US | Xiaogang.c.chen@intel.com
Qinghua Li |  |  | 
Feng Jiang |  |  | 
Kenney Thomas |  |  | 
Laurent Cariou |  |  | 
Stacey Robert |  |  | 
Ziv Avital |  |  | 
Tzahi Weisman |  |  | 
Assaf Gurevitz |  |  | 

## Slide 2: Outline
Recapture of SG motions
PHY design assumptions for EHT
Potential PHY topics in EHT
Summary

## Slide 3: Recapture of SG motions
Move to approve formation of an EHT SG (Extreme High Throughput Study Group) to develop a Project Authorization Request (PAR) and a Criteria for Standards Development (CSD) for a new 802.11 amendment for operating in the bands between 1 to 7.125 GHz, with the primary objectives:
  To increase peak throughput and improve efficiency
  To support high throughput and low latency applications such as video-over-WLAN, gaming, AR and VR
  With target start of the task group in May 2019

## Slide 4: Consideration on the assumptions in EHT
Operating band
  EHT STAs are able to work in 6GHz, 5GHz and 2.4GHz band.
  Only have EHT/HE/non-HT PPDU in 6GHz.
    Non-HT is used to carry short packet;
    Mode reduction (no VHT/HT modes in 6GHz) to simplify test.
Channelization
  Include 20MHz/40MHz/80MHz/160MHz/320MHz in 6GHz band.

## Slide 5: Consideration on the assumptions in EHT (Cont’d)
Coexistence with incumbents
  Master devices (AP) indicates the available channels in 6GHz.
    Master devides get these information from, e.g. data base.
  Subchannel/RU puncturing is used to accommodate the disabled frequency segment(s).
  Minimum CCA granularity is 20MHz
    Finer granularity will create significant changes in preamble design;
    Power of incumbents may be ignored in ED.

## Slide 6: Potential EHT PHY Features – Collocated MIMO
16 SS
  MUMIMO could be the beneficiary of 16SS;
    16SS could be optional for EHT AP given reasonable feedback overhead;
      Implicit FB;
        One end (AP) calibration.
      More efficient explicit FB.
4096 QAM
    Keep the cadence of introducing a new modulation level per WiFi generation;
      64QAM-> 11n; 256QAM-> 11ac; 1024QAM-> 11ax; 4096QAM-> EHT
    Feature of eye catcher for marketing;
    Be applied only if beamforming is used;
      No new EVM requirement for 4096 QAM;
      BF gain compensates EVM gap (-35dB instead of -42dB);
        Expect more BF gain as long as more antennas are deployed.

## Slide 7: Potential EHT PHY Features – Collocated MIMO (cont’d)
UL CQI measurement / UL Power control
  UL CQI helps TB RU selection;
  Efficient UL Power control is key to UL MUMIMO;
  Implementation based solutions
    AP uses reciprocal CQI in DL
      DL CQI is not a good reference due to BF;
      Unbalanced number of Tx/Rx antennas.
    AP leverages the UL traffic for CQI measurement / Power control
      UL BF can be applied in the client side and is transparent to AP;
      Data is not as efficient as NDP;
        Less STAs can be measured within one shot. Limited by Rx antennas at AP;
        Longer duration.
    NDP Short Feedback
        Can accommodate large number of STAs;
        But very sparse tone allocation.

## Slide 8: Potential EHT PHY Features – Collocated MIMO (cont’d)
UL CQI measurement / Power control
  Potential solution in EHT
    UL NDP
      Has been defined in 11az;
      Can be used for implicit beamforming;
      Can be leveraged for UL CQI measurement / power control.

## Slide 9: Potential EHT PHY Features – Distributed MIMO
Distributed MIMO (detailed analysis in back up slides)
  Multi-AP
    Some fancy design could complicate the implementation and defer EHT timeline;
    Simpler solutions need to be prioritized.
      Light coordination in Time/Frequency
        Less PHY changes comparing with the other two schemes.
      Nulling
        Coordination could be very complicated;
        Be polite to neighbor STAs is not free;
        Simplified version may be feasible with the sacrifice of flexibility;
      Joint processing
        The most complicated one from higher layer to PHY layer;
        Need extensive evaluation to justify the benefits.

## Slide 10: Potential EHT PHY Features – Distributed MIMO (Cont’d)
Sounding feedback for distributed MIMO
  Use 11ax sounding procedure as baseline;
  Minimize the feedback modes on the client side;
  May need other feedback modes (besides the modes in 11ax) depends on the category of coordination.

## Slide 11: Potential EHT PHY Features - Preamble
Green field preamble is not a good practice due to backward compatibility.
Auto detection
  Need to differentiate EHT, HE, non-HT, HT and VHT PPDU;
    It’s better to have a future proof solution instead of debating in every generation;
    It’s better if early termination can be achieved for intra PPDU power saving.
      11n STA treat 11ac/11ax PPDU as 11a PPDU;
      11ac STA treat 11ax PPDU as 11a PPDU and decode the whole PPDU;
      11ac/11ax treat EHT PPDU as ??
EHT-SIGB
  HE-SIGB information is well organized but frequency mapping is messy;
  Duplicated structure (1/2/1/2) over optimize the performance for wider BW and waste resource
  A decent frequency mapping scheme can be considered.

## Slide 12: Potential EHT PHY Features – Tone Plan
Physical 20MHz boundary is not aligned with the 242 tone RU of 80MHz PPDU in 11ax.
  Troubles keep popping up in 11ax already;
  Better to apply an easy fix in EHT.
320MHz channel in 6GHz.
  Extend the 80MHz tone plan is a simpler approach;
  Collecting null tones (DC/Guard) with a new tone plan has marginal gain.

## Slide 13: Potential EHT PHY Features – Incumbent Coexistence
11ax disabled subchannel could be a starting point;
  Finer puncturing granularities can be added;
    ~25% incumbents in 6GHz have BW <= 10MHz
    E.g. finer granularity can be 5 or 10MHz including guard.
Requirements for RU puncturing;
  Defining a mask
    DL Mask only as 11ax;
    Or DL+UL Mask.
  Leave to implementation
    More chance to be identified and blocked if a STA interferes incumbents

## Slide 14: Potential EHT PHY Features – MultiBand Operation
Mostly MAC Topic;
  MAC layer aggregation should be prioritized;
  Assuming MAC aggregation can solve most issues;
  PHY layer aggregation is considered only if critical issue is passed to PHY.

## Slide 15: Summary
To meet the tight timeline of EHT, essential PHY topics should be prioritized
  Preamble design;
  Tone plan;
  Incumbent Coex;
  Collocated MIMO enhancement;
  Distributed MIMO with minimal PHY changes;
  MultiBand (if anything pass to PHY).

## Slide 16: Back up
Analysis of the PHY impacts from distributed MIMO

## Slide 17: Frequency coordination
After the Master AP split the whole band (e.g. 80MHz) into subbands (e.g. 40MHz x 2). The coordinated APs
  Option I: use 40MHz mask and transmit 40MHz PPDU (BW = 40MHz in SIGA);
  Option II: use 80MHz mask and transmit 80MHz PPDU (BW = 80MHz in SIGA) with multi-AP OFDMA. Populate energy on 40MHz.
Options | I | II
Pros | Almost no PHY changes | Smooth AP transition and transparent to clients
Cons | Temporarily Mask change back and force; lose the flexibility of non-contiguous 40MHz; receive preamble on S20; | Need preamble & data boundary alignments; receive preamble on S20.

## Slide 18: Nulling
Coordinating procedure could be complicated (next page)
  Victim STAs identify interferer and report to master AP;
  Master AP schedule nulling on different frequency;
  Persecution AP sound the victim STA in neighbor BSS;
  Persecution AP apply nulling in data Tx in nulling widow.
Challenges
  Create nulling for neighbor STA also reduce the freedom of persecution AP itself;
    Feasible for AP with larger number of antennas;
  Limited flexibility to null multiple directions;
  If pursuing to this direction, better to keep one nulling direction per RU for simplicity

## Slide 19: Nulling (cont’d)

## Slide 20: Joint processing
Clock drifting between two APs
  Could introduce FFT window offset, Frequency offset between two APs;
  Sounding feedback may not match the channel when data is sent;
  Clock drifting during data transmission is hard to trace and compensate.
Power imbalance between antennas
  Create illed-conditioned channel;
  The impact need further evaluation.