## Slide 1: Response frame in WUR Mode Setup
Date: 2018-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have defined WUR mode signal in draft spec
  It is based on two-way signal consisting of a request frame and a response frame
    STA requests with preferred operating parameters
    AP accepts or denies STA’s request based on the parameters
If the request is accept, there is no issue in current text
However, if the request is denied, the STA does not know why the request was rejected
  So we will discuss this case

## Slide 3: Other MAC signaling
Following signals are based on two-way signaling (request/response) and there is reason for denial in response frame
  Using Status Code field
    GAS, Association, Authentication, ADDBA, Transition event report, RSNA event report, Diagnostic Report, Basic/DMG ADDTS, HCCA TXOP negotiation, TDLS Setup, Location Configuration, BSS Transition Management, TBTT Adjustment, Power Save Configuration, etc…
  Define own reason
    WNM Sleep Mode, TIM Broadcast, Directed Multicast Service, Flexible Multicast Service, Traffic Filtering Service, etc…

## Slide 4: WUR Mode Setup
We have defined WUR Mode Setup signaling [1]
  It begins when a STA transmits a request frame containing the following duty cycle parameters
    On Duration, Duty Cycle Period
  If the request if accepted, AP will response to the STA with followings
    WUR Mode Response Status (set to Accept)
    WUR ID
    WUR channel offset
    Starting Time of The WUR Duty Cycle
    Group ID List

## Slide 5: WUR Mode Setup
AP may deny STA’s request because of following reasons
  Unspecified reason
  Inappropriate WUR Mode Parameters requested by the STA
  WUR Mode Setup is temporarily unavailable
  Lack of ID space
  Out of AP memory
  Etc…

## Slide 6: WUR Mode Setup
If the AP deny the request from the STA, the AP will response to the STA with only the result
  WUR Mode Response Status is set to 1 (Denied)
  AP cannot modify the duty cycle parameters requested by the STA
The STA does not know why the request was rejected
So, if there is a reason for denial in response frame, the requesting STA can decide its next operation
  It can revise its duty cycle parameter and then retry
  It waits long enough for the AP to be ready
  It disassociates with the AP and scans other APs
  But details of how to optimize is implementation issue

## Slide 7: Denial reason in response frame
So we propose to define additional values in the WUR Mode Response Status field for denial reason
  0: Accept
  1: Denied, due to unspecified reason
  2: Denied, due to inappropriate WUR Mode Parameters requested by the STA
  3: Denied, due to lack of WUR ID space
  4: Denied, due to out of AP memory
  5: Denied, WUR Mode Setup is temporarily unavailable
  6-255: reserved

## Slide 8: Summary
In this submission, we propose to define additional values in the WUR Mode Response Status field for denial reason
  It can improve the behavior about WUR mode signal of WUR STA

## Slide 9: References
[1] IEEE P802.11ba™/D0.4

## Slide 10: Straw poll 1
Do you support modification of WUR Mode Response Status field in slide 6?