## Slide 1: Enabling STA to STA communication
Date: 2018-09-11
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 |  | kazuyuki.sakoda(at)sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud(at)sony.com
Morteza Hashemi |  |  |  | Morteza.Hashemi(at)sony.com

## Slide 2: Overview
Robustness and latency are critical for consumer devices use cases
As discussed in 11-18/1571, we think multi-hop relay can help mitigating blockage issue of 60GHz communication
To allow such network operation, 802.11ay STA should be able to communicate with STA in its neighborhood in addition to AP/PCP that it associates to
We further think that distribution network concept introduced in 11-17/1321 is beneficial to form such a network. In distribution network, it is desirable that STA can find its neighbor STAs
This contribution presents a suggested method to enable neighbor STA discovery efficiently

## Slide 3: STA to STA use case example
Here, we assume 1 BSS operation for simplicity. If we try to leverage path diversity effect, the link between STA1 and STA2 needs to be available even when the traffic is not ongoing
STA1
STA2
AP
Blocker
STA1
STA2
AP
Blocker
STA1
AP
STA2
Blocker
STA1
AP
STA2
Blocker
Case B:
Case A:

## Slide 4: STA to STA communication in DMG BSS
There are sufficient tools to enable STA to STA link set up already
The Information Request/Response frames and Relay Search Request/Response frames are usable to collect other STA’s information
AP can allocate SP with IsInitiatorTXSS subfield equal to 1, so that a STA triggers TX SSW to another STA, which helps initial BF and STA discovery

## Slide 5: Enabling STA to STA communication
STA to STA link set up needs to be done in proactive fashion
Ideally, a STA should perform neighbor STA discovery at the time of joining BSS
It should be beneficial if AP/PCP can kick STA to STA TX SSW when a new STA joins a BSS, i.e., AP asks STA1 to perform SSW toward STA2
STA2: newly joining BSS
STA1: existing STA in the BSS
AP
Joining BSS
Ask to perform TXSS
STA2: newly joining BSS
STA1: existing STA in the BSS
AP
TXSS
Discover each other

## Slide 6: Neighbor STA discovery
The following sequence enables STA discovery at the time of joining BSS
STA 2
(New STA)
AP
Asking to perform
TXSS
AP
DMG discovery signal to STA2 (TXSS)
STA2
(New STA)
STA 1
(Existing STA)
STA1
(Existing STA)
Joining BSS
Joining BSS
Ask to perform TXSS
TXSS

## Slide 7: Recap: multi-band discovery assistance
This STA discovery is similar to multi-band discovery assistance
Multi-band discovery assistance enables on-demand SSW at the time of joining BSS
STA 2
(New STA)
AP
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
AP
Lower band signal
mmW band signal
DMG discovery signal to STA2 (TXSS)
STA2
(New STA)

## Slide 8: Combined use of discovery assistance
DMG Discovery Asst.
Request
AP
DMG discovery signal to STA2 (TXSS)
STA2
(New STA)
STA1
(Existing STA)
DMG Discovery Asst.
Request
DMG Discovery Asst.
Response
DMG discovery signal to STA2 (TXSS)
STA 2
(New STA)
AP
STA 1
(Existing STA)
It would be beneficial if we can perform both discovery process altogether

## Slide 9: Summary
It is beneficial that 802.11ay STA can kick neighbor STA discovery and STA-STA link set up process efficiently
There are many existing components to enable STA to STA communication
We should be able to enable STA discovery with minimal changes to the specification
  Define a container of the signal asking TXSS (Announce frame or Information Request/Response frame)
  AP and STA behavior relating to discovery TXSS allocation

## Slide 10: References
[1] Draft P802.11ay D2.0
[2] IEEE 802.11-18/1571, “Benefits of multi-hop communications in 802.11ay”, Morteza Hashemi, et.al.
[3] IEEE 802.11-17/1321r0 “Features for mmW Distribution Network Use Case”, Djordje Tujkovic, et.al.