## Slide 1: LC Frontend Models
Date: 2018-11-14
Authors:

## Slide 2: Background
To support the channel modeling work of TG 11bb, this document proposes wideband LC Tx and Rx frontend models based on real measurements.

## Slide 3: LC Tx frontend
LC Tx comprises sophisticated driver electronics and LED/laser diode.
Tx DSP has single-ended or differential 50 W interface to the driver
Driver does impedance matching (from 50 W to few W at LED)
Aims at wide bandwidth through sophisticated circuit design
Bandwidth of high-power LEDs is limited by large area of active zone, radiative/non-radiative recombination effects play a minor role
Driver is custom-designed for each LED (e.g. infrared, visible)
Modulation and bias currents can be changed in the driver
Modulation current has an impact on the reach of the LC link
driver
Tx DSP

## Slide 4: LC Tx frontend response
Measured with vector network analyzer from DC to 300 MHz using Rx with multiple GHz BW
LED: CREE XPE RED-L1-R2_N3
Amplitude and phase response
Observations:
  High-pass ~100 kHz
  Little more gain up to 10 MHz
  Almost flat response with little ripple until 240 MHz
  Steep low-pass thereafter

## Slide 5: LC Tx frontend model
Variable gain [V/A] amplifier to set RMS modulation current [A]
Nth order low-pass with variable cut-off e.g. fg = 20, 100, 200 MHz
May be matched to the highest Tx signal bandwidth
High-pass fg = 100 kHz  may cause baseline wander effects!
Added constant bias current [A]
e/o converter with infinite BW and conversion efficiency hTx [W/A]
Any non-linear effects are ignored for now, may be included later
Nth order low-pass
1st order high-pass
VG
VGA
+
bias
e/o

## Slide 6: Tx filter model generation
Steps (see MATLAB code on the right):
Generate Butterworth highpass IIR filter n = 1, fc = 100 kHz, fbw = 1 GHz
Generate Butterworth lowpass IIR filter n = 13, fc = 237 MHz, fbw = 1 GHz
Transform Butterworth filters to second-order sections form
Combine highpass and lowpass filters
Output:
sos: Second-order sections parameter matrix (see next slide)
g: Gain factor (see next slide)
H: Matlab filter object
f_bw = 1e9; % Reference bandwidth (Hz)
%% Highpass filter
n_hi = 1; % Filter order
% Highpass cut-off frequency (Hz)
f_c_hi = 1e5;
[z_hi, p_hi, k_hi] = ...
butter(n_hi, f_c_hi/f_bw, 'high');
[sos_hi, g_hi] = ...
zp2sos(z_hi, p_hi, k_hi);
%% Lowpass filter
n_lo = 13; % Filter order
% Lowpass cut-off frequency (Hz)
f_c_lo = 2.37e8;
[z_lo, p_lo, k_lo] = ...
butter(n_lo, f_c_lo/f_bw);
[sos_lo, g_lo] = ...
zp2sos(z_lo, p_lo, k_lo);
%% Combined bandpass filter
passband_gain = -23.17; % Passb. gain (dB)
sos = [sos_hi; sos_lo];
g = g_hi*g_lo*10^(passband_gain/20);
H = dfilt.df2sos(sos, g);

## Slide 7: Tx filter parameters
Parameter matrix sos:
Gain factor g: 1,40738795875631E-08
k | b0 | b1 | b2 | 1 | a1 | a2
1 | 1 | -1 | 0 | 1 | -0,999685890072330 | 0,000000000000000
2 | 1 | 1 | 0 | 1 | -0,438344960151427 | 0,000000000000000
3 | 1 | 2 | 1 | 1 | -0,887102175721872 | 0,206305166337290
4 | 1 | 2 | 1 | 1 | -0,919219818954179 | 0,249979593051648
5 | 1 | 2 | 1 | 1 | -0,975816547084403 | 0,326941331405787
6 | 1 | 2 | 1 | 1 | -1,061972527809740 | 0,444098528743552
7 | 1 | 2 | 1 | 1 | -1,185825678654060 | 0,612517342065797
8 | 1 | 2 | 1 | 1 | -1,359712686983980 | 0,848973527438837

## Slide 8: Tx filter graphical representation

## Slide 9: LC Rx frontend
LC Rx comprises of PD + sophisticated transimpedance amplifier (TIA).
TIA does the impedance matching (from MWs at PD to 50 W)
Bandwidth limitation of PDs comes from large area mostly
TIA aims at wider bandwidth through sophisticated “bootstrap” design
Compensates the capacitance of large-area PD at the cost of more noise
Bootstrap TIA is custom-designed for a given PD
TIA has single-ended or differential 50 W interface to the Tx DSP
Bootstrap TIA
Rx DSP

## Slide 10: LC Rx frontend response
Measured with vector network analyzer from DC to 300 MHz using laser with several GHz BW
Amplitude and phase responses
Observations:
  Higher pass ~ few 100 kHz
  blocks DC, modulated ambient light
  Almost flat response with little ripple until 250 MHz
  Higher order low-pass thereafter

## Slide 11: LC Rx frontend model
o/e converter for PD with infinite BW and conversion efficiency hRx [A/W]
For PD, ignore the shot noise, while it is to be added directly after APD
Add AWGN for shot noise RMS ithermal [A] after the APD
High-pass filter fg = 100 kHz
Add AWGN for thermal noise RMS ithermal [A] before the TIA
AGC [V/A] to compensate overall attenuation in Tx + channel + Rx
Low-pass with variable cut-off frequency e.g. fg = 20, 100, 200 MHz
Could be matched to the required Rx signal bandwidth
1th order low-pass
1st order high-pass
VG
AGC
+
thermal
noise
o/e
+
shot
noise

## Slide 12: Rx filter model generation
Steps (see MATLAB code on the right):
Generate Butterworth highpass IIR filter n = 1, fc = 100 kHz, fbw = 1 GHz
Generate Butterworth lowpass IIR filter n = 6, fc = 258 MHz, fbw = 1 GHz
Transform Butterworth filters to second-order sections form
Combine highpass and lowpass filters
Output:
sos: Second-order sections parameter matrix (see next slide)
g: Gain factor (see next slide)
H: Matlab filter object
f_bw = 1e9; % Reference bandwidth (Hz)
%% Highpass filter
n_hi = 1; % Filter order
% Highpass cut-off frequency (Hz)
f_c_hi = 1e5;
[z_hi, p_hi, k_hi] = ...
butter(n_hi, f_c_hi/f_bw, 'high');
[sos_hi, g_hi] = ...
zp2sos(z_hi, p_hi, k_hi);
%% Lowpass filter
n_lo = 6; % Filter order
% Lowpass cut-off frequency (Hz)
f_c_lo = 2.58e8;
[z_lo, p_lo, k_lo] = ...
butter(n_lo, f_c_lo/f_bw);
[sos_lo, g_lo] = ...
zp2sos(z_lo, p_lo, k_lo);
%% Combined bandpass filter
passband_gain = 6.8; % Passb. gain (dB)
sos = [sos_hi; sos_lo];
g = g_hi*g_lo*10^(passband_gain/20);
H = dfilt.df2sos(sos, g);

## Slide 13: Rx filter parameters
Parameter matrix sos:
Gain factor g: 0,00269082217204371
k | b0k | b1k | b2k | 1 | a1k | a2k
1 | 1 | -1 | 0 | 1 | -0,999685890072330 | 0,000000000000000
2 | 1 | 2 | 1 | 1 | -0,810740644092165 | 0,176497458365327
3 | 1 | 2 | 1 | 1 | -0,911280817294377 | 0,322395236030663
4 | 1 | 2 | 1 | 1 | -1,160559924501940 | 0,684133898314801

## Slide 14: Rx filter graphical representation

## Slide 15: Summary
Realistic models for LC frontends Tx and Rx have been proposed
Models include major optical frontend effects considered relevant for evaluating the performance of physical layer proposals in TGbb
It has been shown how to simulate LC frontends in Matlab using standard filters for Tx and Rx
Parametrization of filters matches to measurements on real LC frontends, manufactured in our lab.
Check the appendix and reference for more details

## Slide 16: Appendix: Filter model structure
Serial cascade of biquadratic IIR filters („Second-order sections“)
Transfer function (per section):
Implementation (e.g. Direct form 2):
Transfer function ( sections): , : gain factor
See: https://en.wikipedia.org/wiki/Digital_biquad_filter, https://de.mathworks.com/help/signal/ref/zp2sos.html

## Slide 17: Further reading
L. Grobe, V. Jungnickel, K. Langer, M. Haardt and M. Wolf, "On the impact of highpass filtering when using PAM-FDE for visible light communication,"
2016 IEEE Wireless Communications and Networking Conference Workshops (WCNCW), Doha, 2016, pp. 239-245.