## Slide 1: Mandatory Protection Mechanisms
Date: 2018-09-09
r0: Initial draft
r1: Revised to add alternative possible change, straw poll

## Slide 2: Abstract
In most cases, the decision on whether or not to use protection mechanisms (RTS/CTS, CTS-to-Self) is left to individual STAs or (in ax) to the AP.
There is one major exception, in which use of a protection mechanism is required: whenever any (even one) NonERP STA is associated in the BSS (whether or not it has any data to transmit, and whether or not it is in a sleep mode), all transmissions in the BSS must be preceded by a protection mechanism in NonERP format.
This makes no sense. This decision should be left to the AP, which can best manage its own BSS. The necessary change to accomplish this is straightforward to make.
CIDs addressed: 1589 (which has a much different Proposed Change)

## Slide 3: Background
“An ERP STA shall use protection mechanisms (such as RTS/CTS or CTS-to-self) for ERP-OFDM MPDUs with the Type subfield equal to Data or an MMPDU when the Use_Protection field of the ERP element is equal to 1” (1735.51)
“Protection mechanisms frames shall be sent using one of the mandatory Clause 15 (DSSS … ) or Clause 16 (HR/DSSS … ) rates … and … waveforms” (1735.55)
“If one or more NonERP STAs are associated in the BSS, the Use_Protection bit shall be set to 1 in transmitted ERP elements” (1737.7)
“Use_Protection = 1 (HT Protection field equal to non-member protection mode or non-HT mixed mode) All HT transmissions shall be protected using mechanisms as described in 10.27.2 (Protection mechanism for NonERP receivers” (1739.18)
Page and line numbers from md D1.0

## Slide 4: Overhead imposed
Overhead varies according to protection mechanism (RTS/CTS or CTS-to-self), preamble (long or short), and data rate (1, 2, 5.5, 11)
Lowest possible overhead: CTS-to-self, short preamble, 11 Mbps
  Overhead (including SIFS) = 117 ms
If RTS/CTS is planned anyway, what counts is the additional overhead from having to send it in HR/DSSS format
  Additional overhead is at least 238 – 128 = 110 ms
Worst case (for functional protection: RTS/CTS, long, 1 Mbps)
  Additional overhead = 676 ms (cf. CTS-to-self worst case 314 ms)
  Not easy to know when worst case required
BSS throughput drops and STA power consumption increases when a single NonERP STA associates (even if rarely transmits)

## Slide 5: Prevalence
There are relatively few currently deployed 11b-only devices
  Though it only takes one such device in a BSS to trigger the protection mode requirement
  For IoT devices, this has been repeatedly cited as a desirable design option—it is commonly asserted that omitting OFDM modes entirely enables low power consumption, and the use of coin cell batteries
  It’s not clear how many 11b-only devices are out there, as several seem to be non-certified (cf. 11-14/0099r0)
  The potential benefit still seems worth making a change

## Slide 6: Impact of removing the mandate
Suppose ERP-OFDM data frames, at least, do not necessarily have to have NonERP protection, what is the downside?
  Case I: NonERP device wins contention, starts transmitting:
    All ERP & HT STAs would still have all HR/DSSS rates, so no impact
  Case II: ERP device wins contention, doesn’t use protection mechanism, starts transmitting ERP-OFDM:
    Immediate gain of 110+ ms if no NonERP device active
    A NonERP device could start transmitting at any stage after the ERP-OFDM frame begins, causing an extra collision—mostly impacts ERP device
    For NonERP device, some effect: NonERP device wakes, experiences repeated unexplained collisions, burns some unnecessary power
      Note it could actually help the NonERP device also (if transmissions to and from NonERP device are received at high enough power to overcome intereference)

## Slide 7: Impact of removing the mandate—II
It’s a straight tradeoff
  The (significant) efficiency gain if no NonERP device transmits during the current ERP-OFDM frame, versus
  The additional losses if a NonERP device starts to transmit during the current ERP-OFDM frame (and neither frame succeeds)
  2003 versus 2018: As traffic from 11b-only devices dwindles, the tradeoff drifts ever further in favour of no protection mechanism; it made more sense when 11g was bringing a different scheme into the band
Intermediate cases
  STAs (including the AP) are free to use protection mechanisms even if Use_Protection = 0
  If present proposal is adopted, an AP can toggle Use_Protection on and off

## Slide 8: Proposal 1
Make the following changes, relative to P802.11md D1.0:
  At 1737.7, delete “If one or more NonERP STAs are associated in the BSS, the Use_Protection bit shall be set to 1 in transmitted ERP elements.”
  At 1735.5, change “Protection frames shall be sent” to “When the Use_Protection field of the ERP element is equal to 1, protection frames shall be sent”
  At 1736.22, delete “Additionally, if any of the rates in the BSSBasicRateSet parameter of the protection frame transmitting STA’s BSS are Clause 15 (DSSS PHY specification for the 2.4 GHz band designated for ISM applications) or Clause 16 (High rate direct sequence spread spectrum (HR/DSSS) PHY specification) rates, then the protection mechanism frames shall be sent at one of those Clause 15 (DSSS PHY specification for the 2.4 GHz band designated for ISM applications) or Clause 16 (High rate direct sequence spread spectrum (HR/DSSS) PHY specification) basic rates.”
  At 1736.4, add at end of paragraph “An AP may set the Use_Protection bit to 0, based on its internal policies, which are beyond the scope of the standard.”

## Slide 9: Notes
The proposal makes no changes to requirements for ERP and HT devices to be capable of transmitting and receiving 1, 2, 5.5, 11 Mbps rates
The proposal makes no changes to beacons and other multicast frames
  Any frame that must be transmitted at a BSSBasicRateSet rate will continue to be sent at 1, 2, 5.5, or 11 Mbps if any NonERP STAs are associated in the BSS
  (Whether this should be so even when all associated NonERP STAs are in some sleep mode or other is a question for another day)
We could consider additionally adding a NOTE to alert readers to the possibility of a downside if Use_Protection is not set
  Proposal 1 does not include such a note

## Slide 10: Proposal 2
(From Menzo)
Sketch:
  Retain requirement for AP to set Use_Protection = 1
  Change requirement for STAs when Use_Protection = 1 to mandate use of protection mechanisms only when transmission exceeds some limit, e.g., 400 ms
  Maybe limit to uplink only, so the AP still always uses 11b CTS
Allows newly deployed / SW updated g/n/ax devices to save power

## Slide 11: Straw poll
Which option do you prefer:
  1. Make the change in (or along the lines of) proposal 1
  2. Make a change along the lines of proposal 2
  3. Make a change along the lines of either proposal
  4. Make no change

## Slide 12: APPENDIX

## Slide 13: Motion
Move to adopt the changes described in slide 8 of this document.
  Y
  N
  A