## Slide 1: 6 GHz operation for 11ax
Name | Affiliation | Address | Phone | Email
Ravi Gidvani | Samsung |  |  | ravi.gidvani@samsung.com
Ashok Ranganath | Samsung |  |  | ashok.r@samsung.com
Wook Bong Lee | Samsung |  |  | wookbong.lee@samsung.com
Tianyu Wu | Samsung |  |  | tianyu.wu@samsung.com
Shailender Karmuchi | Samsung |  |  | karmuchi.s@samsung.com
Alfred Asterjadhi | Qualcomm |  |  | aasterja@qti.qualcomm.com
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Date: 2018-09-10

## Slide 2: Introduction
In [1], restricting active scanning in 6GHz and scheduled medium access (trigger-based and scheduled EDCA) are proposed
We agree that limiting EDCA access (for both active scanning and normal data transmission) may bring higher network throughput and it may ensure implementation of fairness in overall BSS performance by central entity
However, the proposed scheme in [1] needs considerations (next page)
In this presentation we propose two step behavior in 6GHz which will bridge the gap between current implementations and proposed complete scheduled access

## Slide 3: Considerations of Complete Schedule Access Vs EDCA Access
Limiting active scanning in 6GHz prevents having 6GHz only AP in market
Since STA has more awareness of its surrounding and its own constraints for co-existence with other technologies, antenna or other resource availability which may or may not be predictable, it has no way to influence or control its own scheduling decision. Effectively it may not be backward compatible with presently implemented mechanisms methods for media access (for e.g.:- Fragmentation support is optional in 11ax. STAs may be forced to do fragmentation)
WLAN environment provides rich set of implementation's from different AP vendors. Since schedule of BSS is decided by one central entity it can even act as a single point of failure
Fine Timing Measurement (FTM) and Peer to Peer technologies will needs to be modified to coexist with scheduled access
As such an AP should support both EDCA access and scheduled access.

## Slide 4: Step 1
Two sets of channels can be defined in 6GHz
  Discovery channel: legacy 11ax mode of EDCA + triggered access (Mandatory Mode)
  Scheduled access channel: restricted EDCA access + triggered access (Optional Mode)
APs that need scheduled access + restricted EDCA mode in 6GHz will need to operate on two channels simultaneously either in single band or in dual band. One channel would be discovery channel and the other would be on scheduled access channel
APs shall be beaconing and accepting association only on discovery channel
STA that needs to discover 6GHz AP can scan on discovery channels only
After association, if STA needs to take advantage of AP’s optional mode of operation in scheduled access channel, it switches to the scheduled access channel
Note that AP can choose to operate 11ax mode of EDCA + triggered access mode on scheduled access channel
Merits
This approach prevents the need for STA to send probe request in midst of scheduled access
Keeps channels reserved fully for scheduled access for future implementation of EHT mode
Maintains backward compatibility with existing implementations
Provides foundation for separation of control and data path

## Slide 5: Step 2: Example
Ravi Gidvani(Samsung), et. al.,
Trigger
STA1 BSR
Ack
Mandatory
Random access RU grant
TBTT
TBTT
TBTT
TBTT
MU EDCA Timer Period
Data using EDCA
Mandatory
Random RU grant
Trigger
After sending BSR, if AP does not allocate RU(s) to the STA, then the STA will access channel using EDCA
Detail mechanism to solicit BSR is TBD

## Slide 6: Step 2
In scheduled access channel,
  STA shall disable its EDCA access until MU EDCA timers count has reduced to 0
  OMI methods to disable UL MU shall not be supported and not honored by AP
  AP should provide enough access to all its associated STAs
  If AP’s UL grant cannot satisfy STA’s UL bandwidth requirement and STA has sent a BSR, STA shall start MU-EDCA timer. AP shall provide grant for STA to send BSR.
    E.g. AP shall provide random access grants slots so that a STA, who has data to transmit but it is not part of AP’s schedule, can use this slot to send BSR or UL Data.
  When MU EDCA timer expires and STA has not received any grants it will fall back to regular EDCA access. If STA keeps getting sufficient grant to successfully TX at least one PPDU then STA shall not start MU-EDCA timer after successfully transmitting BSR.
  STA that is in EDCA mode will switch back to scheduled access mode once receiving bandwidth grants from AP
Merits
Prevents deadlocks on STA side that prevent STA from transmitting in head of line conditions
Maintains backward compatibility for STAs

## Slide 7: Reference
[1] 11-18/1256r0, “802.11ax operation in 6GHz band”