## Slide 1: CCI support of TDD stations
Date: 2018-September-12
Authors:
Name | Company | Address | Phone | Email
Alecsander Eitan | Qualcomm |  |  | eitana@qti.qualcomm.com
Assaf Kasher | Qualcomm |  |  | akasher@qti.qualcomm.com
Solomon Trainin | Qualcomm |  |  | strainin@qti.qualcomm.com
Payam Torab | Facebook |  |  | ptorab@fb.com
Nikolas Olaziregi | Nokia |  |  | nikolas.olaziregi@nokia.com

## Slide 2: Introduction
TDD systems operate in schedule mode, over a common channel and are required to operate with low FER/PER and low latency.
TDD systems operate multiple links reusing the frequency and time slots, hence it can be expected that receivers will sense interference from other nodes in the TDD network.
The above's sum to a requirement to the receiver to be able to operate in the presence of CCI without loosing packets.
This presentation provides analysis of the problem.
This topic was presented in 18/0164r01 (Interference mitigation in distribution networks)

## Slide 3: TDD systems
TDD systems operate within allocated slots in a unidirectional communication within each slot.
The slots are synchronized by a common time reference (usually GPS) to 1usec tolerance.
TDD systems reuse the medium with network planning to reduce the CCI.
  CCI is avoided by spatial reuse and synchronization of spatially interfering link
TDD systems do not use LBT, ED nor NAV
TDD systems are required to operate with low FER/PER and low latency.
In each slot(s) transmission is unidirectional, where frames are separated by RIFS or RIFS-SIFS. (RIFS can be 1.0-1.5used, SIFS up to 3.5usec)
TDD-SSW spacing is SBIFS (1usec)

## Slide 4: CCI – issue description
CCI (Co-Channel Interference) is the situation where a receiver is subject to one or more signals additional to the wanted signal, which overlap in time and frequency (to the wanted signal).
The CCI is much more challenging when the interferer signal is a signal of a type which needs to be decoded by the receiver
The CCI level during detection should be low since same SINR ratio applies to the payload reception thus limiting the throughput. (If interferer is stronger than packet, signal will not be received)
For DNs placed at equi-spaced intervals the expected CCI is 9.5dB below the desired signal.
In 18/0164r01 CCI>5dB was stated.

## Slide 5: TDD Access Timing - timeline
TDD Access Rules define the SP Guard Time as GT1, GT2 and GT3 Defined in Draft 2.0 at 9.4.2.266 TDD Slot Structure element
Although not specified in Draft 2.0, the GTx are “same” as the Guard Time defined in IEEE802.11-2016 in section “10.36.6.5 Guard time”
The above means that the time uncertainty at the receiver (actually between transmitter and receiver) is bounded by the Guard Time.
Since all DN and CN devices are synchronized to the same global timing and having a timing error bounded by the Guard Time, it means that the maximum reception time difference between unwanted and wanted frames is bounded by the Guard Time. In the case of STA operating in TDD mode this max time is defined by the GTx in “Slot Structure Control field”

## Slide 6: CCI (cont)
CCI most challenging case is when the interference arrives earlier than the wanted frame (see 18/0164r01 slide 5).
At slot start the time difference is up to a “Guard Time”.
Some slots are used for BF (e.g. TDD-SSW) where each frame may have different received power.
The max ΔT to be supported is the “Guard Time”.

## Slide 7: TDD CCI levels
All TDD system are static.
  All DN and CN stations are fixed installations
  The DN-DN and DN-CN are static links
  Changes are rarely expected to occur (add/remove of DN/CN and rerouting)
Link (slots) allocations are expected to be quasi-static
Given the above, any CCI is predictable (within some limits) and repetitive
  This means that CCI is not sporadic
TDD systems and stations are based on 11ad/11ay technology which doesn’t have fast and dynamic rate adaptations.
  Meaning that fast changes in SINR cannot be compensated.
  Therefore SINR must be controlled and managed (by network planning and scheduling)

## Slide 8: TDD CCI levels (cont)
Given all the above means that TDD systems deployment and configuration will be managed and all links will operate with the estimated CCI level.
No “random” nor CCI “spikes” are expected.
TDD systems are designed, deployed and tuned for high system throughput
Hence it can be expected that TDD systems to operate at high SINR, however some links (some of DN-CN) may operate at lower SINR
Given the DMG performance, especially the robustness of QPSK modulation, it can be expected that minimum SINR in interference limited links to be 6dB (MCS8)
Operators will deploy and configure their system according to their specific features, and therefore expected CCI range will be accordingly different (larger).

## Slide 9: Receiver CCI Resilience Requirements
A good receiver operating as TDD station is required to have CCI resilience.
Receiver should be able to detect and correctly receive a wanted WLAN packet in the presence of CCI WLAN frames even if the unwanted frame arrives earlier than the wanted frame. The specific values are deployment specific.
Implementation can achieve a wide range of values however the more challenging the CCI requirements are the higher FA can be expected and higher HW complexity is required.
Relaxing the CCI requirements to acceptable levels, is beneficial for the TDD STA implementation since it improves the receiver’s overall performance and cost.

## Slide 10: Proposed text for CCI resilience text
Co-Channel Interference (CCI) Resilience:
In the presence of DMG CCI, a DMG STA operating in a TDD SP should decode a PPDU that contains at least one MPDU with RA field set to the MAC address of the STA at least under the following conditions:
The RCPI of the PPDU is at least 3dB above actual receiver sensitivity; and
The RCPI of the CCI is 6dB or less than the RCPI of the PPDU; and
The PPDU has sufficient SINR to be decodable.
(same text as presented in 11-18-0932-01-00)

## Slide 11: Conclusion
TDD systems operate in schedule mode, over a common channel and are required to operate with low FER/PER and low latency. TDD systems operate multiple links reusing the frequency and time slots, hence it can be expected that receivers will sense interference from other nodes in the TDD network. The above's sum to a requirement to the receiver to be able to operate in the presence of CCI. The receiver is expected to include methods to be resilient to CCI (unwanted frame received before the wanted frame)
Unwanted frame may precede the wanted frame at TDD slot start by up-to “Guard Time”, with a power up-to XdB below the wanted frame power. (XdB value depends on and impacted by the TDD system deployment and configuration; reasonable value can be as low as 6dB)
CCI during the slot, mainly cause SINR degradation