## Slide 1: Discussions on Trigger Frame MAC Padding
Date: 2018-11-03
Authors:

## Slide 2: CIDs on TF MAC Padding (1)
15662 | Hongyuan Zhang | 27.5.3.2.2 | 282.22 | "An AP transmitting a PPDU that contains a Trigger frame or frame containing a TRS Control subfield shall ensure that the duration of the PPDU that follows BSYM is greater than or equal MinTrigProcTime indicated by the soliciting non-AP STA (see Table 9-262z (Subfields of the HE MAC Capabilities Information field)). BSYM is the OFDM symbol of the PPDU that contains either the last bit of SCH when BCC is used to encode the PSDU or the last coded bit of the LDPC codeword that encodes the last bit of SCH when LDPC is used to encode the PSDU," This sentence may have issues mathematically from PHY perspecitve. The description implies that the amount of MAC padding for trigger frame should be equivalent to the duration as defined in MinTRigProcTime AFTER the BSYM symbol boundary--meaning that MAC needs to find BSYM first. However this is contradictory to the math description of the number of octets in the MAC padding field as indicated by equations (9-0b) and (9-0c). We need to either (1) Adjust the text here to match the equations (9-0b) and (9-0c); or (2) Change the equations to reflect the text here. However, option(2) seems extremely difficult mathematically and too late for implementation, especially for the case of LDPC. This is because: First, it is awkward for MAC to compute the OFDM symbol boundary before even fully figuring out all the MAC fields; secondly and more importantly, the LDPC codeword length, extra symbol insertion, and other parameters are a function of the total number of data bits (see 19.3.11.7.5), while MAC padding field is part of the data bits to be encoded, so this ends up to a chicken and egg situation, and might be too late to address. | Revise the text to reflect the equations in (9-0b) and (9-0c), i.e. Option(1) in the comment.

## Slide 3: CIDs on TF MAC Padding (2)
16983 | Xiaogang Chen | 9.3.1.23 | 104.15 | eq 9-0b and eq 9-0c don't consider LDPC coding in which one CW could include both user info field and padding field. such that the padding bits cannot gain processing time to process the trigger frame. | Since the number of padding bits depends on MCS, and it's case by case regarding if user info field and padding field belong to the same LDPC CW or not, it's better to remove the equations and leave the padding bits to implementation.
16984 | Xiaogang Chen | 27.5.3.2.2 | 282.25 | Shall ensure that the duration of the PPDU that follows BSYM is greater than or equal MinTrigProcTime indicated by the soliciting non-AP STA. The decoding could end before the end of the BSYM because pre-FEC padding have 4 possible segments. The post-FEC padding with in the symbol can be used to parse trigger frame. so if inTrigProcTime is counted after BSYM, AP are adding more padding than the non-AP STA needed. | replace "BSYM is the OFDM symbol of the PPDU that contains either" with "BSYM is the PPDU that contains either"

## Slide 4: TF Padding Issues
Text in 27.5.3.2.2 is ok with BCC, but it does not have the right assumption of LDPC encoding flow:
BCC is convolutional code (no concept of code words), so this padding flow is OK:
LDPC’s is block code, and its parameters {LLDPC, NCW, Nshrt, Npunc, Nrep, LDPC Extra Symbol} are all determined by the PSDU length and coded bit length (i.e. “Npld” “Navbits”)—refer to 19.3.11.7.5 in Revmd D1.0.
  However, MAC padding bits is also part of PSDU
  See illustration in next page

## Slide 5: Cont’d

## Slide 6: Cont’d
Without knowing number of MAC padding bits, even the LDPC CW Length cannot be determined.
The BSYM computation for each user info field is even more complex at the AP side.

## Slide 7: LDPC Example
Consider a trigger frame with payload size ~260 bytes
  An example is a 6-user MU-BAR trigger frame
  8bytes CommonInfo + 41bytes UserInfo/user
Let’s assume the trigger frame payload is LDPC encoded and transmitted on a 20MHz VHT MCS0 PPDU
We consider the case with MinTrigProcTime = 16us
The procedure in Slide 5 results in an additional LDPC codeword to be added when recomputing the LDPC parameters
In total, about 40 (!) additional OFDM symbols worth of padding bits are needed, if AP really wants to satisfy the “BSYM requirement”.

## Slide 8: Possible Approaches
Option-1: provide a “closed form” method for LDPC to satisfy the “BSYM searching” text
  One example in Appendix
  Extremely complex for both spec writing and AP implementation.
Option-2: Limit the PPDU formats/coding when carrying TF:
  Example: Not allow 11n/11ac PPDU.
    11ax PPDU with LDPC may be ok, because AP may always append more than required PE to cover TF padding duration.
Option-3: remove the “BSYM searching” text from the spec and leave the padding method to AP implementation.
  For LDPC, the issue described above may still exist depending on implementation, STA may need to optimize its TF processing timing for LDPC.

## Slide 9: Straw Poll
Which direction in slide 9 do you prefer?
  Op-1
  Op-2
  Op-3

## Slide 10: Appendix: An example closed form LDPC Solution
Assume the worst case of LDPC parameters before computing the MAC padding length, e.g. LCW=1944, so that sufficient extra Rx processing time is always guaranteed.
Still requires compute LDPC parameter two times (before and after MAC padding), very complex if we want to cover all corner cases.
In most cases, more than necessary MAC padding will be added, more “overhead” on the trigger frame.
Example math process next page.

## Slide 11: Maths