## Slide 1: Time-Aware shaping (802.1Qbv) support in the 802.11 MAC
Date: 2018-11-10
Authors:

## Slide 2: Abstract
This presentation describes potential solutions to enable Time-Aware (8021Qbv) Traffic Shaping over the 802.11 MAC in order to control latency for time-sensitive and real-time applications.

## Slide 3: Outline
TSN Background
Time-Aware (802.1Qbv) traffic shaping
Time-Awareness within the 802.11 MAC
Conclusions

## Slide 4: IEEE 802.1 Time-Sensitive Networking (TSN)
TSN Components Common Standards
Latency
Reliability
Standard Ethernet with Synchronization, small and/or fixed latency, and extremely low packet loss
Reliability
Ultra reliability: Frame Replication and Elimination (P802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (P802.1AS-Rev)
Synchronization
Time synchronization: Time Synchronization (802.1AS)
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (P802.1Qcc) YANG (P802.1Qcp) Link-local Registration Protocol (P802.1CS)
Bounded low latency: Time-Aware traffic shaping (802.1Qbv) Preemption (802.1Qbu/802.3br) Cyclic Scheduling (802.1Qch) Asynchronous Scheduling (802.1Qcr)
Zero congestion loss
Credit: János Farkas, Ericsson
TSNA Conference 2017, http://www.tsnaconference.com/
√ 802.1AS over 802.11
Timing Measurement (TM)
Fine Timing Measurements (FTM)
√ 802.11aa (SRP over 802.11 for AV)
√ 802.11ak (802.11 links in an 802.1Q network)
Time-Aware shaping (802.1qbv) over 802.11 (extension to address latency)

## Slide 5: Time-Aware Traffic Shaping
Scheduling time-critical frame transmissions while avoiding contention with lower priority frames can give low jitter and guarantee worst case latency
  802.1Qbv defines Time-Aware shaper for Ethernet switches
frame selection
T
T
T
T
T
T
T
T
Multiple queues are controlled based on a repeating schedule (time, gate open/closed), time reference is provided by 802.1AS
Queues/Traffic classes
Qbv can be very effective, especially for predictable, periodic traffic
gate open
gate closed
gate open
gate closed
gate open
Transmission time

## Slide 6: Time-Aware Shaping over Wireless
Time-Aware shaping sitting on top of 802.11 MAC can resolve contention within each device and across multiple STAs/AP that share the medium
  Assumptions: managed network and 802.11 admission control is used for TSN traffic
STA 1
T
T
T
T
T
T
T
T
T
T
T
T
Shared medium
AP
STA 2
Other Traffic
Time-Sensitive Traffic
AP
STA 1
STA 2
…
gates closed
gates closed
gate open
gate open
gate open
gate open
All gates open
(Normal Operation)
gates closed
Example Scenario
The Qbv schedule defines when the gates open/close (implementation specific)
The schedule can take into account the 802.11 MAC/PHY mode (e.g. EDCA, 11ax DL/UL OFDMA, TWT, …)

## Slide 7: Simplified TSN Reference Stack
IEEE 802.1 Network
TSN Capabilities: time sync, time-aware, reservations, and many others …
Application
Transport
IP
IEEE 802.3
(Ethernet)
IEEE 802.11
(Wi-Fi)
MAC/PHY
Direct L2 access
IP Encapsulation
Link Layer
Media Specific Support required for TSN Capabilities
  Exchange the 802.1Qbv schedule between managed STAs
  Rules to certify the release of frames from the 802.11 queues according to the 802.1Qbv defined times and avoid contention between queues
802.11 requirements for Time-Aware (Qbv) capability:

## Slide 8: Intra-STA contention problems for time-sensitive frames
Collisions between EDCA functions are resolved within STAs
  high priority AC frames are transmitted and lower priority AC(s) backoff
On avg, high priority AC should get faster access, but a time-sensitive frame may still have to wait in some situations, e.g.:
  other frames in the same AC Queue
  other ACs get access first
  ongoing (long) TXOP from another AC
The time-aware concept can prevent some of the situations that increase worst case latency for time-sensitive frames
Time-sensitive frame
TXOP (AC_VI)
Time-sensitive frame

## Slide 9: Time-Awareness in the 802.11 MAC (option 1 – TSN queue)
A Time-Aware schedule defined (e.g. 802.1Qbv layer, other higher layer, …)
A queue for TSN traffic
A Time-Aware Shaper Function pauses/resumes EDCAFs to avoid contention
A frame selection function (implementation dependent) selects TSN frame(s) for transmission within SP
TSN Access Function: follows selected access mode rules (e.g. EDCA with existing/new AC parameters, 11ax Trigger-based access, …)
Service Period
Service Internal
Service Period
1. TSN Queue→ Open
2. Other EDCAFs paused
EDCAFs resume normal operation
3. Time-Sensitive frames selected/transmitted

## Slide 10: Time-Awareness in the 802.11 MAC (option 2 – TSN reuses EDCA queue)
A Time-Aware schedule defined (e.g. 802.1Qbv layer, other higher layer, …)
A TSN stream uses one of the EDCA queues (e.g. VO)
A Time-Aware Shaper Function pauses/resumes competing EDCAFs to avoid contention
A frame selection function (implementation dependent) selects TSN frame(s) for transmission within SP
Frame is transmitted using EDCAF (e.g. AC_VO), other access methods could also be used (e.g. 11ax Trigger-based)
Service Period
Service Internal
Service Period
1. AC_VO (Time-sensitive Queue)→ Open
2. Other EDCAFs paused
EDCAFs resume normal operation
3. Time-Sensitive frames selected/transmitted

## Slide 11: Time-Aware Shaping within managed BSSs
The 802.11 MAC provides an interface (primitive at the SME-MLME SAP) to configure the Time-Aware Shaper Function in each managed STA
  A 802.1Qbv scheduler (higher layer implementation) is responsible for resolving contention across all managed STAs
  The schedule must be communicated to managed STAs (new management frame can be defined)
A Time-Aware Scheduler may control multiple BSSs
  The schedule can be distributed by higher layers
  All managed BSSs (and STAs) must synchronize to the same time source as the Time-Aware scheduler

## Slide 12: Access mechanism for time-sensitive traffic
The Time-Aware functionality is independent of the access mechanism used
  Various access modes can be used: EDCA, 802.11ax Trigger-based Access, …
  Access mode could be a configuration parameter for the TSN Access Function (option 1)
  Admission control can be used to ensure low latency performance
802.11ax capabilities help increase efficiency
  STAs can be configured to use Trigger-based access
  The AP can schedule UL/DL to comply with the SP boundaries
  The AP may opportunistically schedule other traffic without impacting the time-sensitive traffic

## Slide 13: Impact of unmanaged BSSs
Time-Aware shaping operates on managed STAs
  Interfering transmissions may impact the capability to guarantee bounded latency
  Unmanaged STAs/BSSs are seen as interference
The Time-Aware scheduler can take into account the level of interference when admitting TSN flows and defining SP durations
  Latency bound vs. capacity tradeoffs will depend on the level of interference and deployment scenario

## Slide 14: Conclusions
Time-Aware traffic shaping is a TSN capability to control congestion and worst case latency in managed networks
The 802.11 MAC can enable this capability through a Time-Aware Shaper Function
  Avoid contention from competing traffic between managed STAs, and reduce worst case latency (important for real-time/time-sensitive applications)
  Modifications are limited to controlling queues and do not require new channel access mechanism
This capability will also enable 802.11 to be integrated with Ethernet-based TSN

## Slide 15: References
IEEE Std 802.1Qbv-2015.