## Slide 1: Considerations on 6 GHz Discovery
Date: 2018-11-12
Authors:
Name | Affiliation | Address | Phone | Email
Thomas Derham | Broadcom | 16340 W Bernardo Dr, San Diego |  | thomas.derham@broadcom.com
Matthew Fischer | Broadcom |  |  | 

## Slide 2: Background
802.11ax supports operation in the 6 GHz band. In a typical environment, there will be multiple ESS, each comprising multiple BSS, operating on primary channels spread across the 2.4, 5 and 6 GHz bands
  The introduction of 6 GHz operation will substantially increase the total number of primary channels on which BSSs might be operating
In the general case, a non-AP STA needs to discover (all) these BSS, spread across the multiple bands/channels, and decide which (if any) to associate to, typically based on multiple criteria, e.g.
  Per-network match on configured profile (e.g. SSID, security AKM/credentials, policy, ...)
  Per-BSS link quality assessment (e.g. based on RSSI, channel utilization, ...)
Objective: Optimize discovery (of 6 GHz channels) per two classes of KPIs:
  (1) STA KPIs: fast and energy-efficient discovery (e.g. for roaming, network re-selection) despite the increase in total number of channels
  (2) Network KPIs: minimize impact of discovery on network capacity and latency (e.g. avoid “probe storms” that degrade capacity and increase collisions)
Most all of the necessary building blocks are already present in 802.11

## Slide 3: Regulatory Context
Regulatory proceedings towards unlicensed operation in 6 GHz spectrum are ongoing in multiple domains
The details of potential regulatory rulings are not yet clear, but it is expected (e.g. see [1]) that client devices (non-AP STAs) will operate under some kind of control by an AP
  i.e. a chain-of-trust under the assumption that the AP “master” is operating per regulatory rules
It is reasonable to draw a parallel with 5 GHz DFS rules, e.g. a non-AP STA is “enabled” to transmit on a 6 GHz channel (possibly with certain exceptions) by reception of a signal such as a Beacon frame from an AP on that channel
Therefore, it is prudent to ensure that 6 GHz discovery can be performed quickly and efficiently under such rules
  faster than typical discovery time on 5 GHz DFS channels today
  while ensuring negligible impact on spectral efficiency
[1] https://docs.fcc.gov/public/attachments/FCC-18-147A1.pdf

## Slide 4: Typical Scanning/Discovery procedure by non-AP STA
(Step 1) Determine a set of channels to be scanned
  Typically, the set of channels that the STA considers are likely to contain BSSs (of interest)
(Step 2) Receive information in Beacon / Probe Response from each BSS on the channel
  evaluate each BSS based on measurements and contents of Beacon / Probe, e.g.
    SSID (and/or Roaming Consortium, etc) – network selection policy
    RSNE – security policy
    PHY/MAC Capabilities, link quality metrics (RSSI, BSS Load, ESP, ...) – link quality
    VSIEs – vendor-specific policies and feature support
(Step 3) Choose target BSS (if any) and initiate authentication/association procedure
For each channel in the channel set..
From all the discovered BSS on all scanned channels...

## Slide 5: (Step 1) Determine a set of channels to be scanned
Although the introduction of 6 GHz increases the number of channels on which BSSs might be operating, in most use cases the STA can substantially “prune” the set of channels to be scanned based on a-priori information. Examples:
(a) For roam scan, STA might only / preferentially scan channels on which the serving AP has indicated that neighboring BSS in the same ESS are operating
  e.g. STA receives solicited/unsolicited Neighbor Report / BTM Response from serving AP
(b) For scan to establish P2P (Soft-AP) data link, a higher-layer protocol (e.g. service discovery) operating on 2.4 or 5 GHz band will typically negotiate/determine the channel to be used by the Soft-AP
(c) For full scan (background / unassociated), STA might dynamically prune channels from the channel set based on information received from other APs during the first part of the scan
  e.g. STA discovers basic information about APs operating on 6 GHz channels from Beacons / Probe Responses received during its scan of 2.4 / 5 GHz channels
  STA uses this basic information to prune or deprioritize scan of 6 GHz channels that are unlikely to be of interest
Out of scope of 802.11
Already well covered by 802.11 and WFA certifications, minor tweaks would be beneficial (see next slide)
Propose requirement on AP devices operating in 6 GHz to optimize this use case (see next slide)

## Slide 6: (Step 1) Determine a set of channels to be scanned [cont]
Requirements to optimize step (1):
Mandatory requirement for a 2.4 / 5 GHz AP that is co-located with one or more 6 GHz APs with the same SSID to provide “basic information” about those 6 GHz APs in 2.4 / 5 GHz band
  Note it is possible an “AP device” may be operating multiple BSS on 6 GHz with the same SSID (e.g. on different 6 GHz subbands).
  “Co-located AP” means, per baseline, that the AP that “shares the same antenna connector” as the reporting AP (e.g. REVmd D1.6 9.4.2.21.10) – i.e. we can interpret this as being APs operated by the same physical “AP device” (e.g. dual/tri/quad-band concurrent AP)
The “basic information” to be advertised on 2.4 / 5 GHz band (in decreasing order of importance)
  1. OpClass + Channel: STA needs to know the 6 GHz channel on which the BSS is operating, so it does not prune (or prioritizes) scan on that channel
  2. (Short) SSID: Allow STA to determine whether it is interested in the BSS’s network
    note: for mandatory signaling of same-SSID co-located AP(s), this equals the SSID of the AP reporting the information
    note: indication that an AP is co-located with the reporting AP allows RSSI guesstimation (e.g. prune weak RSSIs)
  3. TBTT (if known by 2.4 / 5 GHz AP – not always): Allow STA to schedule passive scan of Beacon on 6 GHz
  4. BSSID: Useful for STA to match a Beacon / Probe Response received on 6 GHz
Note: Reduced Neighbor Report is a good example of an existing element in baseline that can efficiently carry this information in 2.4/5 GHz beacons/probes (also a WFA certified feature)
Since most 6 GHz APs will be part of dual/tri/quad-band concurrent AP devices, this mandatory requirement is sufficient for STA to discover existence of most 6 GHz APs from 2.4+5 GHz scan
  6 GHz APs that are not of this nature will likely have alternative mechanisms to a-priori determine the operating channel (e.g. P2P discovery of Soft AP, industrial network with preconfigured STAs, hidden network, etc)

## Slide 7: (Step 2) Receive information in Beacon or Probe Responses from each BSS
Once the STA has determined a set of channels containing BSSs (of interest), it then needs to receive information contained in Beacon or Probe Response frames from each BSS
In the general case, this requires an on-channel 6 GHz scan for each channel in the set
Since no legacy (pre-11ax) devices will be operating on 6 GHz band, optimization of the on-channel scan/discovery procedure can be particularly effective
  STA KPI: Minimize dwell time (and transmissions) on each 6 GHz channel
  Network KPI: Minimize airtime overhead consumed by discovery-related frames

## Slide 8: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Support for a Fast passive scanning mechanism in 6 GHz is important:
  If STA has to perform legacy passive scan (blindly listen for Beacon), typical dwell time per channel is > 100 ms
    Consumes excessive power (esp for battery-powered STAs)
    Slow roams contribute to outage (even if the number of channels to be scanned is relatively small per Step 1 pruning)
  Even if rules allow STA to send (certain types of) probe requests, existence of a Fast passive scan mechanism minimizes cases where it is desirable to do so, and so helps minimize probe airtime overhead
Fast Passive Scan
Requirements to support Fast Passive Scan
Allows STA to determine if BSS is of interest or not, and therefore whether to schedule reception of Beacon at TBTT.
(STA might go to sleep, return to home channel, or schedule dwell on another channel, while waiting for TBTT)
An HE AP operating on a 6 GHz primary channel transmits (11ai) FILS Discovery Frames at a regular cadence (e.g. 15-20 TUs)
  Includes Short SSID and TBTT information (and BSSID = TA)
  For Multi BSSID case, just Transmitted BSSID sends FILS DF, containing RNR to indicate the Short SSIDs of non-transmitted BSSIDs (which STA might be interested in)
An HE AP operating on a 6 GHz primary channel always uses Multiple BSSID element if it is operating multiple BSSs (VAPs)
  Mandatory feature to support in 11ax, in 6 GHz it is guaranteed that all STAs can parse it – avoid Beacon/Probe overhead multiplication from VAPs
Mandatory so STA can discover all BSS on 6 GHz channel with ~15-20 ms dwell time (similar to active scan, same/better discovery probability as passive scan with 100+ ms dwell time)
FILS DF can also be used as enablement signals

## Slide 9: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Analysis of total Fast Passive scan airtime overhead – assumptions:
  1x Beacon + 4x FILS Discovery frame per 100 TU TBTT, per “AP device”
  Transmitted in HE SU PPDU at a low mandatory HE rate of 8.6 Mbps (0.8 us GI, LTF=2)
  Durations:
    Preamble: 54.4 us
    Beacon payload (~250 bytes): 232.8 us
    FILS Discovery Frame payload (48 bytes): 44.7 us
  Beacon frame: 287.2 us
    => airtime per “AP device” = 287.2 * (1000/102.4) us/sec => 0.28%
  FILS Discovery frames (in standalone PPDU): 99.1 us
    => airtime per “AP device” = 99.1*4 * (1000/102.4) us/sec => 0.39%
    Note: If AP is anyway transmitting Trigger frames at the same cadence, FILS Discovery Frame overhead could be further reduced by aggregation in the same PPDU => 0.17%
These are very small overheads to enable efficient passive discovery in 6 GHz
Fast Passive Scan [cont]

## Slide 10: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Fast Passive Scan [cont]
Example:
Beacon
FILS Discovery Frame
AP1
STA
Dwell start
AP2
20 TUs
Dwell end
Dwell finished in ~20 ms
20 MHz
Discover AP2
Short-SSID not of interest so ignore
Discover AP1
Short-SSID of interest so schedule listen at TBTT
Sleep, return to home channel, dwell on another channel, etc
TBTT listen start
TBTT listen end

## Slide 11: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Active scan (transmission of probe requests) is primarily important for roam scan:
  STA needs to scan several channels containing roam candidate BSS, receive a beacon/probe from each BSS (to check capabilities, assess link quality, etc), and initiate association to the target BSS quickly before connectivity with current serving AP is lost
Comparative example: STA does purely passive scan on reception of a Neighbor Report from serving AP, which indicates roam candidates on five different 6 GHz channels
  Fast passive scan with 20 ms dwell on each channel
    On average, STA receives a beacon on 1 channel, and FILS DF on the other 4 channels
    TBTTs of the other 4 channels are randomly spread, occasionally occur at almost same time on multiple channels
  Even with optimal scheduling of TBTT listens, total delay to obtain all 5 beacons is likely ~200 ms
  In contrast, active scan would allow reception of Probe Responses from all channels in <<100 ms
Define rules that allow active scan where necessary, without causing unacceptable impact on network capacity or latency
  In non-time-critical scenarios, STAs would primarily use the Fast passive scan mechanism
Active Scan

## Slide 12: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Active Scan [cont]
Requirements to support (limited) Active Scan
An HE AP operating on a 6 GHz primary channel, when responding with a Probe Response frame to a Probe Request frame sent to the broadcast address, sends the Probe Response frame to the broadcast address in a 20 MHz SU PPDU
  Simple reference to this rule introduced by 11ai
If an HE STA performs active scan on a 6 GHz channel:
  Restrict or disallow transmission of Probe Requests with wildcard SSID
  The STA shall not transmit more than one Probe Request frame to the broadcast address in an SU PPDU in a given 20 TU period
Avoids retransmit overhead, e.g. if STA moves out of coverage or finishes dwell before response sent.
Also allows other STAs that are concurrently listening to also hear the probe response
Wildcard-SSID probe requests result in multiplicative overhead (solicit probe responses from every AP) so must be minimized – prime cause of probe storms.
Directed-SSID probe requests (even with bcast MAC) should be allowed for roam scan
This rule avoids STAs performing an inefficient full (all SSIDs) scan by sending multiple directed probe requests to each SSID.

## Slide 13: (Step 2) Receive information in Beacon or Probe Responses from each BSS [cont]
Active Scan [cont]
Example: Fast active roam scan
Beacon
FILS Discovery Frame
AP1
STA
SU Probe request
(directed SSID)
Probe response to bcast address in 20 MHz SU (others STAs can also hear)
Scan start
AP2
20 TUs
Scan end
Probes from both APs received in <20 ms
20 MHz
Note: If STA wants to scan for other SSIDs, it does so passively (extends dwell) since it has already sent an SU probe in the 20 ms period

## Slide 14: Summary
Given that 6 GHz increases the number of possible primary channels, help optimize STA’s scan by ensuring basic information about most 6 GHz APs can be discovered from 2.4 / 5 GHz scan
  Reuse existing frame such as RNR element from baseline
    with small enhancements to indicate co-location, non-transmitted BSSIDs, minimize element size, etc
“Greenfield” 6 GHz allows to substantially reduce discovery airtime overhead by mandating the use of a small number of baseline/11ax features:
  Multiple BSSID (amortize VAPs into single beacon/probe)
  FILS Discovery frames (fast passive scan)
  Broadcast probe response (avoid retry overhead)
Ensure the “probe storm” issues are solved, but also make sure roam scans are efficient
  Simple restricted rules for certain types of probe request transmission
Client STAs in 6 GHz will be performing various latency-sensitive operations: do not restrict STA behavior except where a negative impact on network KPIs is clearly evident
  e.g. roam scan probing, auth/assoc exchanges, ANQP, <<10 ms latency gaming/AR/VR/voice data traffic
  wildcard-SSID probe requests are a special case because they can solicit a large number of responses
  for post-association data traffic, ensure flexibility to configure EDCA operation on a per-AC basis
    optimize service KPIs and network efficiency for each traffic type (e.g. latency-sensitive data vs bulk data)