## Slide 1: Terminology for AP Coordination
Date: 2018-11-14
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Bin Tian |  |  |  | 
Jianhan Liu | Mediatek |  |  | 
Notes: September 2012

## Slide 2: Abstract
AP coordination has been discussed as a possible technology to be adopted in the EHT standard
Different levels of AP coordination are possible [1]
  Each comes with a different level of implementation complexity
The purpose of these slides is to clarify the terminology of the AP coordination area further
  An attempt to develop a common language for the key modes discussed so far
  Slides not meant to serve as an exhaustive list of AP coordination modes

## Slide 3: Terminology Basics
High level bifurcation of various AP coordination schemes
  Techniques where data of one user is sent from a single AP
  Techniques where data of one user is sent from multiple APs
Techniques of type 1. use the term Coordinated in their names
  Multiple APs are doing one (or both) of the following:
    Transmitting on the same frequency resource: Coordinating and forming spatial nulls to allow for simultaneous transmissions from multiple APs
    Transmitting on orthogonal frequency resources: Coordinating and splitting the spectrum to utilize it more efficiently
Techniques of type 2. use the term Joint in their names [2]
  Multiple APs are transmitting jointly to a given user

## Slide 4: Technique 1a : Coordinated BF
Solid blue lines are data transmissions to in-BSS STAs, dotted red lines are steered nulls to OBSS STAs
Key attribute: Signal for a user is only transmitted from one AP while forming nulls to OBSS STAs
AP1
AP2
BSS1
BSS2

## Slide 5: Technique 1b : Coordinated OFDMA
Extend 11ax OFDMA from single BSS to multi-BSS scenarios
Leads to efficient utilization of frequency resources across the network
  Increases efficiency when in-BSS traffic is not utilizing the resources fully
STA 1, 2, 3
STA 4, 5
40 MHz
20MHz
20MHz
Blue color spectrum being used by transmissions in BSS1
Green color spectrum being used by transmissions in BSS2
Synchronized transmissions
to achieve orthogonality

## Slide 6: Technique 2 : Joint Processing Transmissions
Solid blue lines are data transmissions
Key attribute: Signal for a user is transmitted from multiple APs
  Data of all participating STAs needs to be available at all APs
  MU-MIMO using one giant precoder over the combined array consisting of the Tx antennas of all APs
AP1
AP2
BSS1
BSS2

## Slide 7: Special Case of Joint Processing Transmissions: Joint Beamforming to a Single STA
This technique needs to be looked at separately as it might have less stringent synchronization requirements
  Easier than the Joint Processing Transmissions to multiple STAs
  Exploit beamforming and power gain from multiple APs
AP1
AP2
Single STA being served by multiple APs

## Slide 8: Generalization of Terminology
Joint processing transmission or coordinated BF may happen on part of the PPDU bandwidth
Need a name for the general transmissions where multiple APs are transmitting at the same time
  Regardless of the level of coordination in different parts of the spectrum
Suggest the name Distributed MU for such PPDUs
  An extension of the 11ax MU PPDU terminology

## Slide 9: Summary of Terminology on AP Coordination
Note: Above is not an exhaustive list of all AP coordination schemes
Coordinated Techniques
Coordinated Beamforming
Coordinated OFDMA
Joint Processing Techniques
Joint Processing Transmissions
Special case: Joint Beamforming to a single STA

## Slide 10: References
[1] Jianhan Liu et al, “Discussions on Multi-AP Coordination”, IEEE document 11-18/1509r0.
[2] R. Irmer, et. al., “Coordinated Multipoint: Concepts, Performance and Field Trials,” IEEE Communications Magazine, February 2011.