## Slide 1: 6 GHz – Out-of-band discovery discussion
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel |  |  | Laurent.cariou@intel.com
Po-Kai Huang | Intel |  |  | 
Robert Stacey | Intel |  |  | 
Date: 2018-11-11

## Slide 2: Introduction
This document intends to have a discussion on discovery of 6GHz APs in order to move forward
It incorporates the different proposals on discovery

## Slide 3: Objectives
Current steps for STAs full scan:
  1) First step: present list of SSIDs to user interface (no need for all IEs)
  2) Second step: for one or more selected BSSIDs/SSIDs, collect all IEs and RSSI
The objective is to allow STAs to discover all BSSIDs/SSIDs (part of multi-band devices) by scanning only 2.4/5GHz
  Include discovery element in beacons, probe response, assoc response
  Designed to work for single BSSID or multiple BSSID (with multiple BSSID set)
  First step in STAs full scan entirely done in lower bands
Note: If AP/STAs support OCT, they can also complete second step at 2.4/5GHz

## Slide 4: How to fulfil the objectives
To fulfil the objectives, we need:
  1- Mandatory requirements for multiband APs to send discovery information in lower bands
  2- Define the information that is carried in the discovery element
  3 - The definition/selection of the discovery elements (containers) that will carry the needed discovery information
In this document, we describe these 3 items

## Slide 5: 1 - Mandatory requirements
To achieve the objective, we need the following:
If an AP operating on a 6 GHz channel has a Multiband Collocated AP operating on a 2.4 or 5 GHz channel with the same SSID, then the multiband Collocated AP operating on a 2.4 or 5 GHz channel shall advertise the information of the AP operating on a 6 GHz channel in Beacon frames and in Probe Response frames addressed to a STA supporting operation in the 6 GHz band.
  Need also to cover the different cases where Multiple BSSID is used
If an AP operating on a 6GHz channel has an SSID for which there are no BSSIDs at 2.4/5GHz, then at least one of the Multiband Collocated APs at 2.4/5GHz shall advertise the information of this AP at 6GHz.
  To allow the STA to get all SSIDs by just scanning 2.4 and 5GHz: useful for the scan intended to present the list of SSIDs to the user interface
  Without this, the STA will need to go and scan 6GHz to make sure there are no other SSIDs.

## Slide 6: 1 - Mandatory requirements (cont)
Probably a good idea to also mandate that in the 6GHz beacon, we provide discovery information for the 2.4/5GHz collocated APs.

## Slide 7: 2 – What information to carry
Required:
  BSSID, SSID (short of full), operating class, operating channel
  Indication that it is collocated in the same device
Optional features that require signaling in discovery elements:
  If OCT is used: need an indication that this feature is supported
  If out-of-band association is recommended: good to provide this information
  Possibly others…
Good to have
  If the BSSID at 6GHz is part of multiple BSSID set,
    At least have an indication that this is the case (no beacons sent by this BSSID)
    provide the MaxBSSIDIndicator to help locate the right beacon/FILS DF

## Slide 8: 3 – What element to use
Multiband element
Reduced Neighbor Report
Modification of HE Operation element

## Slide 9: Discussion on discovery elements
Multi-band element:
  Designed specifically for discovery of collocated APs
  Need modifications for SSID information, handling of multiple BSSID set
  Optional subelement can allow to provide other information
Reduced neighbor report:
  Already used on WFA OCE program
  Needs to be modified to signal that it is collocated
  Needs to be modified to signal optional features (OCT, out-of-band assoc, multiBSSID…)

## Slide 10: Discussion on discovery elements
Modification of HE Operation element has the following issues
  Limited to a single AP/operating channel at 6GHz:
    Already many APs with 2 BSSIDs at 5GHz in different channels (low band and high band), very likely to have devices with at least 2 BSSIDs on 2 operating channels at 6GHz
  Does not cover the discovery in case the SSID is different
    2.4/5GHz APs have to be HE APs
  Overload of an element that is not meant for that (HE Op, when sent by the 5GHz AP is meant to carry information describing the 5GHz AP, not for describing other BSSs)

## Slide 11: Compromise solution
We propose to use the Reduced Neighbor Report as the single solution for the discovery of collocated APs in 2.4/5GHz beacons and probe responses

## Slide 12: Discussion with regards to Neighbor report Orthogonal discussion than discov
Discovery element (RNR or MBE) already included in beacons and probe response
Neighbor reports are mainly used when included in BTM response frames by an AP
  first case: transmitted by the AP at 2.4/5GHz that is part of the same multi-band device as the 6GHz AP
    If a neighbor report describing the 6GHz AP is included in BTM response, it does not need to indicate that it is collocated in the same multiband device as this information is known by the STA from probe response/beacon
  second case: transmitted by a non-collocated AP at 2.4/5/6GHz
    Obviously can not indicate that it is collocated with the current AP
    2 neighbor reports can be sent in a row to describe the AP at 5 and the AP at 6GHz and it is useful to know if they are collocated

## Slide 13: Annex

## Slide 14: Ex: Multi-BSSID with same SSID list at 5 and 6GHz
Beacon
BSSID5_0
SSID0
Beacon
BSSID5_1
SSID1
Beacon
BSSID5_2
SSID2
5GHz
Co-located BSSID set
Beacon
BSSID6_0
SSID0
Transmit BSSID
BSSID6_1
SSID1 profile
6GHz
Multi-BSSID set
Multiple BSSID element
BSSID6_2
SSID2 profile
MBE or RNR
BSSID6_0
MBE or RNR
BSSID6_1, same SSID, Max BSSID Indicator
MBE or RNR
BSSID6_2, same SSID, Max BSSID Indicator

## Slide 15: Ex: Multi-BSSID with more SSIDs at 6GHz
Beacon
BSSID5_0
SSID0
Beacon
BSSID5_1
SSID1
5GHz
Co-located BSSID set
Beacon
BSSID6_0
SSID0
Transmit BSSID
BSSID6_1
SSID1 profile
6GHz
Multi-BSSID set
Multiple BSSID element
BSSID6_2
SSID2 profile
MBE with BSSID6_0, with multiple BSSID element descrbing BSSID6_2, SSID2
MBE or RNR
BSSID6_1, same SSID, Max BSSID Indicator
Or RNR for BSSID6_0, and for BSSID 6_2 with ful SSID or OCT support